*********************************************************************************
*********************************************************************************
**********************                                ***************************
**********************    Documentation for TRACER    ***************************
**********************                                ***************************
*********************************************************************************
*********************************************************************************



  PROGRAM AUTHOR - S. L. Lawton,
                   Research Dept.,
                   Mobil Technology Company,
                   P. O. Box 480,
                   Paulsboro,
                   New Jersey 08066-0480
                   U.S.A.





 TRACER - PROGRAM TO CHECK CELL
===============================


 TRACER:
-------

 Tracer by S.L. Lawton, A Lattice Transformation - Cell Reduction Program.

The reduced cell is defined to be the unit cell with the smallest volume
whose axes are the three shortest non-coplanar translations in the lattice.
TRACER converts the cell parameters which you put in as input to the reduced
cell. Such a reduction to a triclinic lattice with c < a < b and the angles
alpha and beta as non-acute allows for the identification of the Bravais
lattice of highest symmetry which it represents. This is accomplished by
calculation of the scalar products

  A.A, B.B, C.C, B.C, C.A, A.B and comparison to matrices within the
program.

This is facilitated by using the reduced cell and considering all possible
combinations of axial lengths in the 14 Bravais lattices. There exists
only 43 independent cells whose axes correspond to the 3 shortest non-coplanar
translations in the lattice.

The one input parameter which might require clarification is the value of
DEL to be used. Lawton reports that for lattice parameters with errors
as low as 1 part in 10,000 Angstrom that a DEL = 0.10 is sufficient, while
errors of the order of one part in 1000 Angstrom might require DEL values
in the range of 0.50 to 1.00 (for Proteins use at least 1.0). The DEL value
imposes the upper limit on the equivalence of special relationships between
the scalar products used in the program. It essentially defines the absolute
value of the largest allowable difference between any two of the six reduced
cell scalar products. In as much as a DEL value to any extreme is undesirable
it has been our practice to run TRACER using DEL values of 0.10, 0.50 and
1.00 in the same run and then examine the output as a function of these
different DEL values. Usually the higher the standard deviation in the cell
parameters the higher the DEL value that should be used.



 INPUT
------


----line 1 Run number (terminates if equal to -1)

---- line 2 TITLE card

---- line 3 CONTROL input DEL
            CONTROL = 1 for direct space
                    = 2 for reciprocal space cell dimensions

            DEL = Absolute value of the largest permissible difference
                  between any two of the six reduced cell scalar products.

---- line 4 cell dimensions (free format)
            a, b, c, alpha, beta, gamma (Angstrom /degrees)

---- line 5 INSTRUCTION (format I3  !!!!!!!!!)

       This card(s) function as the commands to the program in
       transforming one cell to another. Each card contains an instruction.
       As many cards as necessary may be used to complete the desired
       successive transformations for any one compound.
       Their order specifies to the program the order in which the
       transformations are to be executed. The last instruction for a
       particular sequence of transformations must have either 7 or 8!!!!

       Both may not be present and neither may precede any with
       1,,2,3,4,5,6.

       NQ = 7 triggers cell reduction.
       NQ = 8 merely identifies the last cell in a sequence to which a
              transformation is to be made with no cell reduction is performed.

INSTRUCTIONS
=============

  NQ = 1   :Transform this cell to a new cell using a matrix supplied by
            the user on the corresponding transformation card.

  NQ = 2   :The initial cell is A-centred, transform to a primitive cell
            using a matrix held in subroutine CENTER

  NQ = 3   :..... B-Centred........

  NQ = 4   :...... C-Centred .......

  NQ = 5   :...... I-Centred ......

  NQ = 6   :........ F-Centred .......

  NQ = 7   :Get reduced cell and then identify and generate from it the
            unit cell of highest symmetry and its corresponding lattice
            parameters

  NQ=8   : This is a non-executive instruction notifying the program
           that no transformation is to be applied to this cell.
           This may be used for;
           (i) to calculate the inverse cell data of the input parameters,
           or
           (ii) to identify the name of the cell to which the previous cell
           is transformed when the previous cell in a transformation
           sequence involves any of NQ = 1,2,3,4,5,6)


 TRANSFORMATION cards

 each contains a 3 x 3 matrix one per card  for each NQ = 1

 in the order
 1,1  1,2  1,3  2,1  2,2  2,3  3,1  3,2  3,3



  INPUT FILE FORMAT ...


    The input file name is entirely the choice of the user.

    As an example, consider the file "test.dat" in the
  current directory.

  Format :

      line 1 : run number
      line 2 : title
      line 3 : control card TYPE and DEL
            TYPE=1 direct space input cell
            TYPE=2 reciprocal space input cell
            DEL= allowed error for transformation match
            DEL = 0.10, 0.50, 1.00 ie
                  use three consective runs in one file

      line 4 : cell parameters
      line 5 : INSTRUCTION number (FORMAT I3 !!!!!!!)
            =1 you supply matrix
            =2 A to P
            =3 B to P
            =4 C to P
            =5 I to P
            =6 F to P
            =7 find reduced cell (normal value)
       if you use 1 then next line has a 3x3 matrix on it

      next line can be next run number and repeat input
      last line : -1 in columns 1 and 2 to terminate job
      all other lines FREE FORMAT.



      Contents of file "test.dat"
       ------------
       1                            !run number
       test tracer                  ! title
       1  0.1                       ! real cell/ del
       10.51 15.15 6.54 90 151.7 90 ! cell
         4                          ! supplied cell is C-faced
         7                          ! find reduced cell
       -1                           ! terminate run
       ----------




  OPERATIONAL DETAILS  :


       To invoke the program, simply type "tracer" from a UNIX
  system or "run tracer" from a VMS system.
  Then, please insert the name of the input file and the name
  you wish to give to the output file, when you are prompted.
  The filename qualifier (".dat", ".out", etc.) should be included
  when the filename is typed in following the corresponding prompt.
 


---------------------------------------------------------------