File formats for Diffrac-11 files.  (Ver 2.0)

**************************************************
Diffrac-11 *.DIF file format.

 1- 4	SAMP ID.		These are alphanumerics
 5- 7	DATE OF MEAS  (A9,3^@)
 8- 9	TIME OF MEAS
10-12	OPERATOR NAME FROM FILLOC.DAT

13	SANG
14	ENAG
15	AINC
16	CTIM
17	res.

18	ANODE (A4)
19	WAVELENGTH

20	A=ADR, I=IDR;  I=integral, N=net intens.
21	npeak, nresid.peaks	(2I*2)
22	C=COMSEA, J=JCPDS
23	Apeture (rec 18 of .RAW file) 
24	?

25	MCELL (1=unitcell stored by appel)  MINO (1=hkl stored)
26-27	crystal system (A6);   bravais lattice (A2)
28-30	A,B,C of unit cell
31	cell volume
32-34	angles alpha, beta, gamma

35-38	res.

    FIRST PEAK
39-40	h,k,l,0 (4I*2)
41	D-value
42	Intensity
43	FWHM
44	Residual intensity

45-50	Next peak


************************************************************
Diffrac-11 *.RAW file.

 1-12	Same text as .DIF(1-12)
13-29	Copied from D500nn.DAT(1-17) with change to rec 19 (7)
19	Detector (2*SC+Monochrom);  Meas mode (0=unknown, 1=stepscan, 2=scan)
30	Num ranges; Operation code (2*delay time+Theta fixed. 0=norm)
  The following repeat for each range
31-34	SANG,EANG,AINC,CTIME
35	Theta fixed or delay time.
36-...  Counts for first range.


************************************************************
Diffrac-11 D500nn.DAT file

1	ANODE MATERIAL (A4)
2	LAMBDA
3	DELTA LAMBDA
4	KV; MA
5	DET. SLIT
6	APETURE (<=0 fixed)
7	Detector (2*SC+Mono. 0=PSPC without mono, 3=SC with mono.)

 8-12	Calib coef A0-A4 for 2-theta
13-17	Calib coef A0-A4 for intensity

18	MCHANG (Max # of samples);  MCHVER (1=special version without 1-21)
19	ANGMAX 2-theta
20	THERES (Reset angle)
21	Goniometer type (1=D500, 2=D501, 3=D500F, 4=the/the)
22-128  empty


************************************************************
Diffrac-11 DI11.CAT file  (RECL=20 words)

Rec 1 has: NFILES, NRECS (max nfiles-1) 18*0

Records 2 to NRECS have:
 1- 2	DEV(A4) 
 3- 5	FILE(A6)
 6-13	SAMPLE ID (A16)
14-17	I*2 counts for files: .RAW, .DIF, .PLT, .???
18-20	Reserved.


************************************************************
Diffrac-11 MEASnn.PAR file (Recl=2 words)
This is from experience; the manual is not accurate.

 1	MEPNRC (0=empty)
 2	MAXSMP (1-80);  MAXRNG (1-20)
 3	IACTIVE; 0
 4	ISTOP; INEXT
    SAMPLE BLOCKS FOLLOW:
 5	DEVICE (A4)
 6- 7	FILE (A6); STATUS (1=stored in catalog)
 8-11	Sample ID (A16)
21	IOP; IOVER (1=overwrite)
22	MSCAN(1=scan); MROT(1=rotation)
    Next 5 records repeat for each range.
23-26	SANG,EANG,AINC,CTIME
27	res.