************************************************************************

DATAPP                                                         SCOPE 3.2

DATAPT                                                        JULY, 1971



           S.U.N.Y./BUFFALO CRYSTALLOGRAPHIC COMPUTER PROGRAMS


************************************************************************
     NOTE: REPLACEABLE ROUTINES IMP AND SCALE HAVE BEEN CHANGED TO IMPD
            AND SCALED RESPECTIVELY.  THESE ARE PERMANENT.

CORE:

    DATAPP:     OCTAL:  47000 + 4*N(1)*N(2)*N(3)
                WHERE N(1), N(2), N(3) ARE THE NUMBER OF GAUSSIAN GRID
                POINTS.

    DATAPT:     60 K OCTAL  (FIXED VALUE)


PROGRAM CARD:  PROGRAM DATAPP (INPUT,OUTPUT,TAPE3,TAPE4,TAPE5=INPUT,
                              PUNCH,TAPE6=OUTPUT,TAPE1=TAPE3,TAPE2)


PURPOSE:

         THIS IS THE SECOND STAGE IN PROCESSING OF X-RAY OR NEUTRON
    FOUR-CIRCLE DIFFRACTOMETER DATA.  LORENTZ-POLARIZATION FACTORS ARE
    APPLIED, ABSORPTION CORRECTIONS ARE MADE, AND THE NECESSARY QUAN-
    TITIES FOR MAKING EXTINCTION CORRECTIONS IN THE ZACHARIASEN APPROX-
    IMATION ARE CALCULATED (ZACHARIASEN, ACTA CRYST., 23, 558 (1967),
    COPPENS AND HAMILTON, ACTA CRYST., A26, 71 (1970)).  FOR DETAILS ON
    THE ABSORPTION CORRECTION, SEE ACTA CRYST., 18, 1035 (1965).

         PROGRAM DATAPP CALCULATES THE ABSORPTION FACTORS BY NUMERICAL
    GAUSSIAN INTEGRATION, WHILE PROGRAM DATAPT CALCULATES THEM BY THE
    ANALYTICAL METHOD OF DE MEULENAER AND TOMPA (ACTA CRYST., 19, 1014,
    (1965) ).  THE PROGRAMS ARE SO DESIGNED THAT THE INPUT DECK AND
    ROUTINES MAY BE SUBMITTED AS INPUT TO EITHER PROGRAM.


TIME REQUIRED:

         (THIS PROGRAM SHOULD ALWAYS BE TEST RUN ON ABOUT 20 DATA FOR
         PURPOSES OF TIMING AND VERIFYING ALL ANSWERS ARE SATISFACTORY.)

   DATAPP:

         TWO EXAMPLES MAY SERVE AS A GUIDE:

            1) NO ABSORPTION:  1302 REFLECTIONS IN 18.3 SEC CP TIME

            2) 144 POINT GRID AND 6 PLANES:  2436 REFLECTIONS IN 370
                                             SEC. CP TIME

                                                               DATAPP  2

   DATAPT:

         VERY FAST, EVEN WHEN ABSORPTION FACTORS ARE BEING CALCULATED.
         APPROXIMATELY 1.0 CP SEC/REFLECTION.



TAPES:

         TAPE 3 INPUT  OPTIONAL

         TAPE 4 OUTPUT OPTIONAL  (BIN)

         TAPE 2 OUTPUT OPTIONAL  (BCD)



INPUT:

      INPUT TO BOTH PROGRAMS IS THE SAME EXCEPT WHERE NOTED.


  1.  (1X79H)  TITLE.  PUNCH IN COLUMNS 2-80.


  2.  (7F9.6)  CELL CONSTANTS.

      ANY OF THE FOLLOWING MAY BE USED (A VALUE ` 1. IS CONSIDERED TO
      BE A COSINE):

           COLS.    1-9      A*          A*         A         A

                  10-18      B*          B*         B         B

                  19-27      C*          C*         C         C

                  28-36  COS(ALPHA*)   ALPHA*   COS(ALPHA)  ALPHA

                  37-45   COS(BETA*)    BETA*    COS(BETA)   BETA

                  46-54  COS(GAMMA*)   GAMMA*   COS(GAMMA)  GAMMA

                         FOR ANY OF THE FOUR COMBINATIONS ABOVE:

                  55-63  WAVELENGTH, IN ANGSTROMS.


  3.  ORIENTATION MATRIX

             OPTION 1.  (9F8.0)  ((WN(I,J),J=1,3),I=1,3)

                        WHERE @WN(I,J)? IS THE ORIENTATION MATRIX
                        DEFINED BY COPPENS AND BEDNOWITZ AND IS PRINTED
                        OUT BY THE ROUTINES XRAY, MAIN, AND SATT AT THE
                        HFBR.
                        SEE APPENDIX, PAGE 11.

                                    ALPHA*(TRANSPOSE) = AG(TRANSPOSE).WN

                                                               DATAPP  3

                        IF THE TRANSFORMATION MATRIX U IS DEFINED AS IN
                        THE HAMILTON INTERNATIONAL TABLES ARTICLE:

                                          A* = U.AG,

                        WHERE A* ARE THE RECIPROCAL CELL COORDINATES,
                        AND AG IS AN ORTHOGONAL SYSTEM FIXED IN THE
                        GONIOMETER HEAD, THEN THE WN MATRIX HERE IS
                        OBTAINED FROM U BY DIVIDING THE ROWS OF U BY
                        A*, B*, C*, RESPECTIVELY AND TAKING THE TRANS-
                        POSE.  IF ABSORPTION AND EXTINCTION CORRECTION
                        ARE UNDESIRED, THIS MATRIX IS IRRELEVANT.  WHEN
                        SUPPLIED, BE SURE THAT NORMALIZATION OF COLUMNS
                        TO UNITY IS EXACT.


              OPTION 2. (PREFERRED OPTION)

                        U MATRIX TO BE CALCULATED FROM SETTING ANGLES
                        FOR 3 REFLECTIONS.

                        CARD 3.1  BLANK

                        CARD 3.2  (4F9.4)

                               COL.    1-9  PHIZRO:
                                     10-18   OMZRO:  ANGLE
                                     19-27 TWOTHZO:  ZEROS
                                     28-36  CHIZRO:

                        CARD 3.3  (3F9.0,4F9.4)

                               COL.    1-9       H
                                     10-18       K
                                     19-27       L
                                     28-36    PHI:
                                     37-45     OM:  OBSERVED SETTING
                                     46-54  TWOTH:  ANGLES FOR
                                     55-63    CHI:  REFLECTION 1

                        CARD 3.4  SAME AS 3.3, FOR REFLECTION 2.

                        CARD 3.5  SAME AS 3.3, FOR REFLECTION 3.


  4.  (16I5)  CONTROL INTEGERS (ICN(I),I=1,16)

             COLS.    1-5  =  0 NO ABSORPTION CORRECTION.

                           =  1 ABSORPTION CORRECTION:  CRYSTAL BOUNDARY
                                PLANES DESCRIBED BY H, K, L INDICES AND
                                D IN CM.  (PREFERRED OPTION).

                           =  2 ABSORPTION CORRECTION:  CRYSTAL BOUNDARY
                                PLANES DESCRIBED BY OBSERVED SETTING
                                ANGLES NECESSARY TO BRING BOUNDING PLANE
                                INTO THE DIFFRACTING CONDITION, AND D IN
                                CM.

                                                               DATAPP  4

                           =  3 ABSORPTION CORRECTION:  CRYSTAL BOUNDARY
                                PLANES DESCRIBED BY EQUATION OF PLANES
                                IN SEATTLE COORDINATE SYSTEM, A, B, C,
                                AND D IN MM.

                                SEE SECTION ON BOUNDARY PLANES,
                                CARDS 7, PAGE 6.

                     6-10  =  0 NO QUANTITIES ARE CALCULATED FOR EXTINC-
                                TION.

                           = +1 QUANTITIES NECESSARY FOR EXTINCTION
                                CORRECTION IN LINUSU (S.U.N.Y./BUFFALO
                                LEAST-SQUARES PROGRAM) ARE CALCULATED.
                                (THIS OPTION DEMANDS CRYSTAL BOUNDARY
                                PLANES; SEE CARDS 7, PAGE 6).

                           = -1 VECTOR COMPONENTS BUT NOT TBAR ARE
                                CALCULATED FOR EXTINCTION.
                                (APPLICABLE IF ICN(1) = 0)

                    11-15  =  0 DO NOT CALL SCALE SUBROUTINE.

                              1 A SUBROUTINE SCALE IS CALLED WHICH
                                MAY BE USED TO SCALE DATA RELATIVE
                                TO STANDARDS COLLECTED DURING DATA
                                COLLECTION PROCEDURE.

                              2 APPLY A CUBIC POLYNOMIAL CORRECTION
                                TO DATA BASED ON STANDARD REFLECTIONS
                                A'LA ED MCGANDY

                    16-20     DATAPP ONLY.  DATAPT IGNORES THIS OPTION.

                           =  0 NORMALLY

                           =  1 CALCULATE DISTANCE BETWEEN GIVEN PAIRS
                                OF VERTICES.  (SEE CARDS 8)  VERTEX
                                CARDS FOLLOW CRYSTAL BOUNDARY PLANE
                                CARDS.

                    21-25  =  0 FOR X-RAY.

                           =  1 FOR NEUTRON DATA.
                                THIS INTEGER SPECIFIES FORM OF POLARI-
                                ZATION FACTOR.

                    26-30       DETERMINE STATUS OF BCD OUTPUT.

                           =  0 NO PUNCHED CARD OUTPUT OF REFLECTIONS,
                                NO BCD TAPE.

                           =  1 FOR PUNCHED CARD OUTPUT IN FORMAT SUIT-
                                ABLE FOR INPUT TO LINUSU OR DSORTH.

                           =  2 FOR OUTPUT ON BCD TAPE 2 IN FORMAT SUIT-
                                ABLE FOR INPUT TO LINUS OR DSORTH.  NO
                                UPDATING PERMITTED.

                              3 PUNCH AND WRITE TAPE 2

                    31-35       DETERMINES STATUS OF BINARY TAPE 4 FOR
                                LEAST-SQUARES INPUT.

                           = -1 FOR NO TAPE 4 OUTPUT.
                                                                DATAPP 5

                           =  0 FOR NEW TAPE 4 OUTPUT.

                           =  1 FOR AN UPDATED TAPE 4.  OLD TAPE IS READ
                                UNTIL END-OF-FILE; BACKSPACE OVER
                                END-OF-FILE AND ISENT = 1 RECORD, START
                                WRITING AND PLACE NEW ISENT = 1 RECORD
                                AND END-OF-FILE AT END OF NEW DATA.
                    36-40  =  0 FOR CARD INPUT AS DESCRIBED BELOW.
                                (USER MUST SUPPLY *IMP* ROUTINE)
                                SEE REPLACEABLE ROUTINES.

                           =  1 FOR INPUT ON TAPE3 AS DESCRIBED BELOW.
                                (USER MUST SUPPLY *IMP* ROUTINE)
                                SEE REPLACEABLE ROUTINES.

                    41-45  =  0 NORMALLY.

                           =  N FOR SETTING ANGLES CHECK.  IF ICN(9) = N
                                THIS CARD SHOULD BE FOLLOWED BY N CARDS
                                OF FORMAT (3F3.0,F9.3) WITH H, K, L AND
                                THE TRUE (ZERO CORRECTED) VALUE OF
                                OMEGA.  THE PROGRAM WILL CALCULATE AND
                                PRINT THE SETTING ANGLES FOR THESE RE-
                                FLECTIONS.

                       50  =  0 ALWAYS.

                       55  =  1 LAST DIGIT OF INTENSITY HANDLED
                                BY USER IN SUBROUTINE IMP

                           =  2 FOR STEP SCAN DATA FROM PROG. FILE


             THE REMAINING FIELDS ON CARD 4:  ICN(I), I = 11-16 ARE
             READ IN AND ARE AVAILABLE TO THE USER-SUPPLIED SUBROUTINES
             FOR WHATEVER PURPOSE.



  5.  OPTIONAL.  (3F3.0,F9.3)  H, K, L, OMEGA

             ICN(9) CARDS FOR ANGLES CHECK.

             COLS. 1-3   H

                   4-6   K

                   7-9   L

                 10-19   OMEGA(TRUE)


  6.  OPTIONAL.  (4I5)  (NGAUSS(I),I=1,3),NFACES

             SUPPLY ONLY IF ICN(1) IS > 0, OR ICN(2) > 0.

         DATAPP:

             SPECIFICATIONS FOR GRID FOR ABSORPTION OR EXTINCTION
             CORRECTION.  A GAUSSIAN INTEGRATION FORMULA IS USED.  THE
             FIRST THREE FIELDS DEFINE THE NUMBER OF GRID POINTS IN
             THE DIRECTIONS A,B,C.  THE PRODUCT OF THESE THREE MUST BE
             LESS THAN THE SECOND DIMENSION OF GRID IN THE MAIN PROGRAM.
             THE VERSION OF THE PROGRAM AVAILABLE ON THE CRYSTAL SYSTEM
                                                               DATAPP  6

             IS COMPILED FOR THIS DIMENSION EQUAL TO 5000.

             COLS.    1-5  NUMBER OF GAUSSIAN GRID POINTS :
                                                 ALONG A. : MUST BE EVEN
                     6-10  NUMBER OF GAUSSIAN GRID POINTS : NUMBERS 2-32
                                                 ALONG B. :
                    11-15  NUMBER OF GAUSSIAN GRID POINTS : MUST BE EVEN
                                                 ALONG C. : NUMBERS 2-32

                    16-20  NUMBER OF BOUNDARY PLANES.

         DATAPT:

              COLS.  1-15  ARE IGNORED

                    16-20  ARE ABSOLUTELY NECESSARY


  7.  OPTIONAL.  (4F10.6)  (SUPPLY IF CARD 6. SUPPLIED)

             ONE CARD FOR EACH BOUNDARY PLANE, OPTION DEPENDING UPON
             THE VALUE OF ICN(1), CARD 4, COLS. 1-5.
             THE NUMBER OF CARDS EQUAL TO COLS. 16-20, CARD 6.

      ****   IF ICN(1) = 1, THE BOUNDARY PLANES ARE GIVEN IN TERMS OF
             THE MILLER INDICES OF CRYSTALLOGRAPHIC PLANES AND THE PER-
             PENDICULAR DISTANCES IN CM OF THESE PLANES FROM AN ARBI-
             TRARY ORIGIN WITHIN THE CRYSTAL.


             COLS.   1-10     H

                    11-30     K

                    21-30     L

                    31-40     DISTANCE IN CM.

             (IF A COMPARISON IS TO BE MADE WITH ABSORPTION CORRECTIONS
             CALCULATED BY GONO9, ONE MUST NOTE THAT THE CORRESPONDING
             PLANES ENTERED IN GONO9 HAVE COEFFICIENTS H/D*, K/D*,
             L/D*.)


      ****   IF ICN(1) = 2.  THE UNIQUE OBSERVED SETTING ANGLES PHI,
             OMEGA, CHI NECESSARY TO BRING THE BOUNDING PLANE NORMAL
             INTO THE DIFFRACTING CONDITION (ON THE XY PLANE, ALONG +Y)
             ARE USED, WITH D IN CM.

             COLS.   1-10     PHI (OBS)

                    11-20     OMEGA (OBS)

                    21-30     CHI (OBS)

                    31-40     D (CM)

             ANGLE ZERO CORRECTIONS ARE MADE INTERNALLY.

                                                               DATAPP  7

      ****   IF ICN(1) = 3.  THE COEFFICIENTS A, B, C, OF THE EQUATION
             OF PLANE:
                             A*X + B*Y + C*Z - D = 0

             ARE USED, WITH D IN MM.

             COLS.   1-10     A

                    11-20     B

                    21-30     C

                    31-40     D (MM)


             *****NOTE:  FOR ICN(1) = 3, D MUST BE IN MM.*****


  8.  OPTIONAL, DATAPP ONLY.  DATAPT AUTOMATICALLY PRODUCES THIS OUTPUT.

             NEEDED IF ICN(4) = 1.

             PROGRAM CALCULATES DISTANCE BETWEEN THEORETICAL
             INTERSECTION OF VERTICES IVERT1 AND IVERT2.

             THE VERTEX NUMBERS MUST BE KNOWN.  SINCE THE PROGRAM PRINTS
             THE VERTEX NUMBERS AUTOMATICALLY,  THIS OPTION CAN BE RUN
             ONLY ON THE SECOND OR LATER PASS.  IT IS INTENDED AS A
             CHECK.  IF IVERT1=IVERT2, TERMINATE.


  9.1 (I5,7F10.5)  REFLECTION BATCH CARDS.

             COLS.    1-5     IQ  SCALE FACTOR NUMBER.  IQ WILL BE
                                  PUNCHED ON OUTPUT CARDS IF NSCALE IS
                                  SET TO 1 IN *IMP*; FOR OTHER VALUES
                                  OF NSCALE THE SCALE FACTOR NUMBER IS
                                  TAKEN EQUAL TO NSCALE.

                     6-15         NO LONGER USED.

                    16-25     C(1):  THE PROGRAM WILL CALCULATE
                                  :  SIGMA (I-B)**2 (OBSERVED
                                  :  VARIANCE), AS:
                                  :  (I + B) + C(1)**2*(I - B)**2 +
                                  :    C(2)**2*(I(CORRECTED) - I)**2.
                    26-35     C(2):  THE THREE TERMS REPRESENT THE
                                  :  STATISTICAL ERROR, A PROPORTIONAL
                                  :  ERROR AND THE UNCERTAINTY IN THE
                                  :  ABSORPTION CORRECTION.

                    36-45     MU  ABSORPTION COEFFICIENT IN RECIPROCAL
                                  CM.

                    46-55         SCALE FACTOR BY WHICH F**2 IS MULTI-
                                  PLIED.  MUST NOT BE ZERO.  1.0 IS
                                  OFTEN APPROPRIATE.

                    56-65     OMEGAZERO CORRECTION WHICH IS SUBTRACTED
                                                               DATAPP  8

                                        FROM OMEGA ON CARD TO GET TRUE
                                        OMEGA.

                    66-75     PHIZERO CORRECTION WHICH IS SUBTRACTED
                                      FROM PHI ON CARD TO GET TRUE PHI.

                    76-80     TWOTHETA MONOCHROMATOR

   9.2  (F10.5,2I10)   BATCH CARD TWO

             COLS    1-10     STARTING VALUE OF THE SCALING FACTOR
                              USUALLY 1.0 BUT IF RUN IS BEING PICKED
                              UP FROM A PREVIOUS PARTIAL RUN THEN USE
                              THE LAST VALUE PRINTED

                       20 = 0 LINEAR TWO POINT INTERPOLATION FOR SCALE

                          = 1 FOUR POINT INTERPOLATION FOR SCALE
                              CUBIC POLYNOMIAL
                       30 =   THE NO. OF STANDARD REFLECTIONS USED


  9.3 (NSTD(5X3I5)) BATCH CARD 3  INDICES OF STANDARD REFLECTIONS

                   COL 10     H FOR FIRST STANDARD
                       15     K ''   ''      ''
                       20     L ''   ''      ''
                       30     H FOR SECOND STANDARD
                       35     K ''    ''     ''
                       40     L ''    ''      ''
                       50     H FOR THIRD ETC.




 10.  OPTIONAL.  REFLECTION DATA IF READ FROM CARDS.

             INPUT IS DEFINED IN ROUTINE *IMP*.  TAPE 3 IS INPUT, OR
             TAPE 5 FOR CARDS.  USER MUST SUPPLY HIS OWN *IMP*.
             SEE REPLACEABLE ROUTINES FOR DISCUSSION.


OUTPUT:

         BINARY TAPE 4; OR CARDS AND/OR BCD TAPE 2 WITH:
             FORMAT (I1,F3.0,2F4.0,2F9.3,F3.0,6F6.3,F6.4)

             LOGICAL RECORDS ARE COMPOSED OF:

                     JDENT = 0 NORMALLY.

                           = 1 ON DUMMY RECORD FOLLOWING LAST REFLECTION

                         H   (                )
                         K   ( FLOATING POINT )
                         L   (                )

                    (F**2) = (OBSI - (SLO/SLB)*BACFK)*LP*(1/ABS)*(SCALE
                               FACTOR SPECIFIED ON BATCH CARD)*(SCALE
                               FACTOR FROM SUBROUTINE SCALE).
                             NOTE THAT F**2 MAY BE NEGATIVE.

               SIGMA(F**2) = SCALE FACTORS*LP*(1/ABS)*POISSON COUNTING
                             STATISTICS OBTAINED AS FOLLOWS:
                             SIGMA(POISSON)**2 = OBSFI + (SLO/SLB)**2*
                                                 BACFK.
                             ADDITIONAL TERMS CAN BE ADDED WITH INFOR-
                             MATION ON CARD 9.

                    SCALEN   SCALE FACTOR NUMBER FROM INPUT.

                           = IQ  COLS. 1-5, CARD 9; IF AND ONLY IF
                                    NSCALE = 1 IN *IMP*

                           = NSCALE  IF
                                    NSCALE NOT = 1 IN *IMP*

                    XN(1):   COMPONENTS, IN ANGSTROMS, OF THE UNIT
                    XN(2):   VECTOR NORMAL TO THE PLANE CONTAINING THE
                    XN(3):   INCIDENT AND DIFFRACTED BEAMS, ALONG
                             A, B, AND C.

                  XNSO(1):   COMPONENTS OF UNIT VECTOR NORMAL TO INCI-
                  XNSO(2):   DENT BEAM IN THE PLANE OF THE INCIDENT AND
                                                               DATAPP  9

                  XNSO(3):   DIFFRACTED BEAMS.

                      TBAR   MEAN PATH LENGTH FOR THIS REFLECTION--
                             WEIGHTED BY ABSORPTION.

                             (THE LAST SIX QUANTITIES MAY BE USED IN
                             CALCULATION OF AN ANISOTROPIC EXTINCTION
                             CORRECTION (COPPENS AND HAMILTON, (1968).)



REPLACEABLE SUBROUTINES:     (NOTE NAME CHANGES FOR RANDOM FILE SYSTEM)

             SUBROUTINE IMPD(FH,FK,FL,S,B,SCB,OM,PHI,SLO,SLB,
                            OBSFI,BACFK,IDENT,NSCALE,ICN,NBACK)
             DIMENSION ICN(16)

                   A CALL IS MADE TO THIS ROUTINE TO READ EACH REFLEC-
                   TION IN TURN.

                        FH   :
                             :
                        FK   :    MILLER INDICES, REAL
                             :
                        FL   :

                        S         PEAK INTENSITY

                        B         TOTAL INTENSITY OF ALL BACKGROUNDS

                        SCB       SCALE FACTOR: USUALLY = 1.

                        OM        OBSERVED OMEGA

                        PHI       OBSERVED PHI

                        SLO       PEAK SCAN LENGTH TIME (SEC)

                        SLB       TOTAL BACKGROUND COUNTING TIME (SEC)

                        OBSFI     IDENTICAL TO S

                        BACFK     IDENTICAL TO B

                        IDENT     DATA TERMINATION SIGNAL

                        NSCALE    A SCALE FACTOR NUMBER, TRANSFERRED
                                  TO OUTPUT

                        ICN       ICN(16) ARE THE CONTROL INTEGERS

                        NBACK     NUMBER OF BACKGROUNDS OBSERVED
                                  (NUMBER OF TERMS CONTRIBUTING TO B)


                   ICN(16) ARE THE CONTROL INTEGERS WHICH MAY BE USED
                   BY THE PROGRAMMER.  ONLY THE FIRST TEN HAVE
                   SPECIAL MEANING IN THE PROGRAM, THE OTHERS PROVIDE
                   SOME FLEXIBILITY IN DATA MANIPULATION.
                                                               DATAPP 10

                   FOR IDENT:

                              IF(IDENT .EQ. 1)  3 NEW BATCH CARDS PLUS NEW
                                                CALLS TO IMPD WILL BE
                                                MADE.

                              IF(IDENT .EQ. 2)  RUN IS TERMINATED.

                              IF(IDENT .EQ. 3)  A COMPLETE NEW RUN WITH
                                                NEW TITLE, ETC., IS
                                                STARTED.

                              IF(IDENT .GT. 3)  NEW CARD 10 PLUS NEW
                                                CALLS TO IMPD WILL BE
                                                MADE.



                   SET FH = FH + 100000, IF THIS IS A STANDARD REFLEC-
                   TION.



             SUBROUTINE SCALED(IH,IK,IL,ISIG,M,NSCALE,NREJ,
                              JM,H1,K1,L1,H2,K2,L2,SCLA,NLINES)

                   THIS ROUTINE IS CALLED SHORTLY AFTER IMPD FOR EVERY
                   REFLECTION.

                          IH,IK,IL ARE INTEGER MILLER INDICES OF REFLEC-
                                   TION.

                              ISIG IS THE NET PEAK COUNT, M IS THE INTE-
                                   GRATED BACKGROUND COUNT.

                            NSCALE IS THE SCALE FACTOR NUMBER AS SUP-
                                   PLIED BY IMP.

                              NREJ MAY BE RETURNED NOT EQUAL TO 0, AND
                                   REFLECTION WILL BE REJECTED.

                                JM IS SERIAL COUNT NUMBER OF REFLECTION,
                                   THIS CAN BE USED TO EXCLUDE INTENSITY
                                   STANDARD REFLECTIONS FROM FINAL LIST.

                              SCLA IS A SCALE FACTOR--INITIALLY 1.0--
                                   WHICH MAY BE CALCULATED BY THIS ROUT-
                                   INE AND MULTIPLIES THE SCALE FACTOR
                                   ON THE INPUT CARDS AND THAT SPECIFIED
                                   ON THE BATCH CARD.


                   THE ROUTINE SUPPLIED DOES THE FOLLOWING:

                       1)  SETS NSCALE = 1.

                       2)  IF THE THREE STANDARD REFLECTIONS HAVE
                           OCCURRED TOGETHER IN ORDER AFTER THE FIRST
                           SUCH OCCURENCE, THE OLD SCALE FACTOR IS
                                                               DATAPP 11

                           MULTIPLIED BY:

                        OLD TOTAL NET PEAK COUNT FOR THE TWO REFLECTIONS
                        ------------------------------------------------
                        NEW TOTAL NET PEAK COUNT FOR THE TWO PEFLECTIONS

                           INITIAL SCALE FACTOR IS 1.0.


                       3)  IF THIS FACTOR LIES BETWEEN 0.98 AND 1.02,
                           THE ROUTINE RETURNS WITH THE OLD SCALE FAC-
                           TOR.  IF IT IS OUTSIDE THIS RANGE, THE ROU-
                           TINE RETURNS WITH THE NEW SCALE FACTOR.


DEFINITION OF THE WN MATRIX IN DATAPP, MULREF, AND ANDA PROGRAMS:


             THE WN MATRIX RELATES THE RECIPROCAL LATTICE AXES A*, B*,
         AND C* TO THE ORTHOGONAL RIGHT-HANDED GONIOMETER HEAD AXES X,
         Y, AND Z.
             AT ZERO VALUES OF THE SETTING ANGLES PHI, CHI, AND OMEGA,
         THE AXES ARE DEFINED AS FOLLOWS:  Y LIES IN THE PLANE OF THE
         INCIDENT AND DIFFRACTED BEAM AND IN THE PLANE OF THE CHI CIRCLE
         IN A DIRECTION SUCH THAT THE INCIDENT BEAM ARRIVES AT THE ORI-
         GIN (CRYSTAL) FROM THE POSITIVE (X), POSITIVE (Y) DIRECTION,
         (X IS PARALLEL TO THE CHI AXIS, Z IS PARALLEL TO THE PHI AXIS,
         SUCH THAT THE COORDINATE SYSTEM IS RIGHT-HANDED).

             IF (X), (Y), AND (Z) ARE UNIT VECTORS PARALLEL TO THE
         GONIOMETER HEAD AXES X, Y, Z, THEN WN IS DEFINED BY:

         ( (X),(Y),(Z) ) WN = @ (A)*/ABS(A*),(B)*/ABS(B*),(C)*/ABS(C*) ?

                          OR:

           AG(TRANSPOSE).WN = ALPHA*(TRANSPOSE)


             THEREFORE:

                               ( COS(A*,X)  COS(A*,Y)  COS(A*,Z) )
                      WN   =   ( COS(B*,X)  COS(B*,Y)  COS(B*,Z) )
                               ( COS(C*,X)  COS(C*,Y)  COS(C*,Z) )















                                                               DATAPP 12

                                                 Y
                              *                  :   INCIDENT BEAM  *
                                *                :                *
                 DIFFRACTED BEAM  *              :              *
                                    *            :            *
                                      *          :          *
                                        *        :        *
                                          *      :      *
                                            *    :    *
                                              *  :  *
                                                *:*
                                                 :.  ..  ..  ..  ..  ..

                                                                       X



             NOTE CAREFULLY THAT THIS WN MATRIX IS RELATED TO THE
         HAMILTON U MATRIX (U(H)) BY THE TRANSFORMATION:

                                   U(H)(1,J) = A*.WN(J,1)

                                   U(H)(2,J) = B*.WN(J,2)

                                   U(H)(3,J) = C*.WN(J,3)

                                             OR
                                        U(H) = WN(TRANSPOSE).N

                                                   ( A*   0   0 )
                                               N = (  0  B*   0 )
                                                   (  0   0  C* )

END