I-1

******************************************************************************
**************  DOCUMENTATION FOR EXAFS DATA ANALYSIS PACKAGE ****************
******************************************************************************
				REVISED 2-FEB-84

INTRODUCTION TO THE EXAFS DOCUMENTATION PACKAGE

     The package consists of two main programs named EXAPLT and EXAFIT.  In

addition, utility programs PHASE CONHLD, MCMAST, and CURSRT are included.

These are described briefly here, and in full detail in the following

sections.

	EXAPLT	This is the main analysis program that carries out all

		analysis steps from raw data through Fourier transforms

		in preparation for non-linear curve fitting.  It includes

		several special features for analysis of the phase of

		the EXAFS oscillations.  The program is highly interactive

		and can write disc files of data an various stages of

		analysis.

	EXAFIT	This program carries out the non-linear curve fitting

		to a model EXAFS equation.  Files written by the EXAPLT

		program are taken as input to EXAFIT.

	PHASE	This is a utility program to set up and maintain disc

		files that contain tables of reference phase functions

		that are obtained either from theoretical calculations

		or from empirical measurements on reference materials.

		The disc tables are used by both EXAPLT and EXAFIT.

	CONHLD  This is a utility program to set up on the system device

		the file CONST.HLD for use by EXAPLT.  Normally this program

		will be executed only once in setting up the EXAFS package;

		CONST.HLD is maintained by EXAPLT.

	MCMAST	This is a utility program to set up on the system device 

		the file MCMSTR.TBL for use by EXAPLT.  Normally this program

		will be executed only once in setting up the EXAFS package;

		MCMSTR.TBL is maintained by EXAPLT.


I-2

	CURSRT	This is a utility program for testing graphic input and output

		operations on the graphic display device.  Graphic terminals

		that can run this program can be expected to work with the

		EXAFS package programs.


EP-1

***************************************************************************
********** DOCUMENTATION FOR THE EXAPLT, EXAFS ANALYSIS PROGRAM ***********
***************************************************************************
                           REVISED  4-FEB-83



INTRODUCTION: The EXAPLT PROGRAM is a FORTRAN IV program designed to read

            in raw EXAFS (Extended X-ray Absorption Fine Structure) data in

            the OLD or NEW KIRBY SSRL FORMAT and provide a set of analysis

            options (SMOOTHLINE, FOURIER TRANSFORM FILTERING, PHASE ANALY-

            SIS, AND PHASE REMOVAL) which can be performed on the data via

            graphical interaction.  The resulting output from each analysis

            option can be saved on disk in a special format for later recall

            or be used as input for the next option chosen. The EXAPLT program

            provides flexible graphics so the user can conveniently interact

            with the data and control the the graphical presentation of the

            results.

STRUCTURE:    The EXAPLT PROGRAM is modular in nature, and consists of options

            that can be thought of as operators that act on a set of data

	    stored in an input space and deliver the results of the operation

	    to an output space.  The input space consists of a pair of storage

	    arrays X and Y, and the output space a pair V and W.  After any

            operation the contents of V and W are plotted on the screen, but

            X and Y are left unchanged.  This means that the program user,

            after viewing the results of an operation, has the choice of

            stepping back to the results of the previous operation, either

            to try the operation again with different parameters, to correct

            errors, or to try another option.  This feature gives the EXAPLT

            program a powerful flexibility in that the outcome of trying any

            option can help the user decide how to proceed.  When the outcome


EP-2

            of an option is satisfactory, the user can elect to retain the

            results with the KE option.  This loads the contents of the U,V 

            arrays (output space) into the X,Y arrays (input space) in pre-

            paration for further processing.  Not all options produce changed

            output data; options such as XP, CS, and DF that effect only the

            display of the data in V,W do not alter either X,Y or V,W.  If an

            option that changes V,W has been executed but is not retained by

            selecting KE then PL will restore the arrays to the condition

            prior to that latest operation and replot the data arrays. Other-

            wise PL just replots the results of the current step.   

OPERATION:    The EXAPLT program should be run from the system device in order

            to not interfere with I/O on the default device.  Four files, in 

            addition to data files, (CONST.HLD, MCMSTR.TBL, TEOLEE.PHT, and

            PARAM.PHF) are required for access by EXAPLT during execution of

            several of the options.  The CONST.HLD file contains current

            status information about the data being analyzed and, therefore,

            should be maintained on the system device.  The file, MCMSTR.TBL, 

            contains tables of McMaster coefficients of X-ray cross sections

            useful for for computing an energy dependent absorption normaliza-

            tion which is an option in the smoothline treatment.  In the de-

            fault treatment, the EXAFS oscillations are normalized to an ener-

            gy independent absorption step.  The MCMSTR.TBL file should be

            maintained on the system device, also.  The other two files are

            phase tables, required as input during phase options, and these

            can be maintained on the default device or an interchangable de-

            vice such as floppy disk.  When a prompt symbol >[BELL] occurs on

            the screen or teletype the program is waiting for an instruction.

            A list of valid instuctions (two-letter keywords) is given below,

            with short descriptions for each.  A more detailed description of

            each instruction is given further on.


EP-3

HARDWARE:     Hardware requirements for the EXAPLT program call for at least a

            16 bit PDP,LSI 11 processor with extended memory capability for

            addressing 128K words.  A Tektronix 4010,14,25 or equivalent

            graphics terminal, supporting the Tektronix Terminal Control

            System (TCS) with graphical curser input, is necessary, preferably

            including a screen hardcopy unit.   A hard disk or dual density

            floppy drive is a prerequisite to installation. A line printer

            such as VERSATEC 1200, which has optional screen copy hardware,

            provides a versatile print/plot mode ideal for the fast output of

            the EXAPLT program.  A floating point unit in the processor is

            essential.


INSTRUCTIONS: Two-letter EXAPLT options accepted in response to >[BELL] prompt

                    EX --- Exit from EXAPLT program

                    RE *-- Read in raw EXAFS data file, two formats

                    OP *-- Options of channels to ratio and logarithm of ratio

                    PL --- Plot of current output array with current captions

                    EN *-- Converts stepnumber to energy, input beamline specs

                    SL **- Remove smoothline background, cubic spline, and

                           optional McMaster treatment

                    KV --- Converts energy to wave vector representation

                    FT **- Computes forward FFT,Magnitude of transform plotted

                    BT -*- Computes inverse FFT of a chosen window of data

                    KE --- Load current output array and captions into input

                           array. Use after EN,ES,SL,KV,DG,FT,BT,PH before

                           continuing to next analysis option.

                    XP -*- Expand a chosen section of a plot using interactive

                           curser. Stores the new plot window in replot stack

                           (up to 3 sets maintained in stack).


EP-4
                    RP **- Replots any of the three current plot windows de-

                           termined in XP or IS. Cleared when PL or rescale of

                           the data occurs.

                    IS *-- Terminal input of up to three plot window sets into

                           replot stack.

                    ES **- Terminal or graphic edge shift calibration

                    DG -*- Deglitching of data by pairs

                    PT -*- Labels point coordinates via interactive curser.

                    WF --- Writes current output arrays into a file on the de-

                           fault device with current headings, captions and

                           analysis map.  Special format filename depends on 

                           current status of output data ( xxxxxx.*xx ) where

                                  * = R   Raw data ratio file

                                  * = L   Log of ratio file

                                  * = A   Absorption vs Energy

                                  * = X   (XANES) Absorption vs Energy

                                  * = E   Chi vs Energy

                                  * = K   Chi vs Wave Vector k

                                  * = F   Magnitude vs Radius

                                  * = B   Backtransform k**nChi vs k

                    PR --- Writes above file to line printer instead of to

                           default storage device.

                    RF *-- Reads in a special format WF file from default

                           device and updates all arrays, captions, and 

                           parameters.

                    CS --- Produces hardcopy image of graphic screen.

                    PM --- Writes current file header map, which logs the

                           analysis parameters and constants, to the printer.

                    LM --- Does the same as PM except writes to the active

                           consol screen.


EP-5
                    DF --- Computes differential of input array and plots it.

                           Ideal for locating the edge for precise absorption

                           edge calibration when using ES.

                    PF **- Initiates phase shift comparison and fitting al-

                           gorithms.  Can determine R and E0 for a given phase

                           function.  The experimental phase can be compared

                           to a phase stored in the phase tables.

                           Details of other options available in PF decribed

                           later 

                    PH *-- Prepares an array for subsequent phase removal step

                           prior to Fourier transforming. Uses phase tables.

                           The phase removal then occurs invisibly in the FT

                           routine, however, the imaginary part of the trans-

                           form is plotted with the magnitude for this option.

                    AF *-- Generates the and plotting of backtransform

                           envelopes and the calculation and plotting of the

                           log of the ratio of amplitudes vs k**2 after a

                           successful BT option.  The reference amplitude for

                           this algorithm may be input from terminal, tables,

                           or interpolated from disk data file.  Least squares

                           fitting to the Ln ratio curve, provides an estimate

                           of the relative disorder.


                    FC **- An option used on fluorescence spectra from concen-

                           trated samples.  An absorption correction factor

                           may be applied to the absorption spectrum based on

                           the value of the stepheight determined in the SL

                           option.



EP-6
                    ED *-- An option to display several near edge spectra and

                           difference them if desired.  Up to three edge

                           may be read in from disk files to be used in

                           differencing or display.                         


                    TI *-- An option to interpolate the amplitude or phase

                           from the Inverse Fourier Transform and enter the

                           interpolated values into the TEOLEE.TBL tables.

                           The range of interpolation must be coincident with

                           the full TEOLEE range (3.7795-15.1178).


                    *--    Alpha-numeric input required

                    -*-    Graphic curser input required

                    **-    Both required


EP-7

DESCRIPTIONS: Detailed descriptions and examples of each two-letter option


            >[BELL]

            EX<ret>

                    The EX option terminates the execution of the EXAPLT pro-

                  gram and returns to system monitor.


            >[BELL]

            RE<ret>

                    The RE option reads all columns of data present in the

                  specified raw data file.  Reads both 'old' and 'new' Kirby

                  SSRL formats.  Automatically enters the OP option. An error

                  message is displayed if the specified file name is not found

                  on the default device.

                  ERROR -- FILE NOT FOUND

                  RT-11 file names must be in the format  (xxxxxx.xxx)


EP-8
            >[BELL]

            OP<ret>

                    The OP option allows user to choose the channels to ratio

                  and whether the natural logarithm of the ratio is desired.

                  Sample dialog:


                  *-      OPTIONS FOR THE OUTPUT DATA ARE AS FOLLOWS:

                  *-             <CR> = RETURN TO MAIN PROGRAM

                  *-               1  = INPUT CHANNEL #1
                  
                  *                . . .

                  *                6  = INPUT CHANNEL #6 [unity]

                  -               -1  = INVERSE OF CHANNEL #1

                  *       RATIO OF CHANNELS I(KOPT)/I(LOPT)

                  *       ENTER (KOPT/LOPT) OPTIONS: 1/2<ret>

                          (desired channels 1 and 2 are ratioed)

                  -       ENTER (1 OR -1) OPTION: 1<ret>

                          (channel 1 which is already ratioed in 'old' format)

                  *-      DO YOU WANT TO TAKE THE LOG? (Y/N) :  Y<ret>


                  - Old format dialog

                  * New format dialog


                  The selected option is automatically plotted. 


            >[BELL]

            PL<ret>

                    The PL option copies the X,Y data arrays to V,W and

		  plots V,W  on calculated scaling. Current captions and

		  labelling is controlled automatically.


EP-9
            >[BELL]

            EN<ret>

                    The EN option converts stepnumber to an energy scale which

                  is 0. at the X-ray energy of the absorption edge. Sample

                  dialog:


                  PRESENT MONOCHROMETER STEPS/DEG. :   2000.0<ret>

                  PRESENT CRYSTAL LATTICE SPACING : 1.9200<ret>

                  STEP NUMBER OFFSET : 0.0<ret>

                  EDGE ENERGY (EV'S) : 8978.2<ret>

                  ANY CHANGES ? (Y/N) : Y<ret>


                  (inputs are expected as real numbers with decimal points;
                  default is just <ret>)


                  PRESENT MONOCHROMETER STEPS/DEG. : <ret>

                  PRESENT CRYSTAL LATTICE SPACING : <ret>

                  STEP NUMBER OFFSET : <ret>
 
                  EDGE ENERGY (EV'S) : 8978.8<ret>

                  ANY CHANGES ? (Y/N) : N<ret>


                  (this example changed the value of the edge energy only)

                  The data is rescaled and plotted on the energy scale de-

                  termined by the beam line parameters above.


EP-10
            >[BELL]

            SL<ret>

                    The SL option calculates a smoothline background to be

                  subtracted from the absorption data. The result is rescaled

                  and plotted.  The smoothline divides the data between chosen

                  endpoints into multiple regions (3 is default) and a poly-

                  nomial spline is fit into each region with continuity of

                  derivatives at the endpoints of the regions. 9 is the max-

                  imum allowable number regions the user can chose.  Responses

                  to the first graphical curser prompt are:


                          (1)  N<ret>   end points chosen are NOT stored for

                                        later use.  The normal default of

                                        reponding with ANY CHARACTER will

                                        store the endpoint parameters and the
 
                                        step height values for later use

                                        with the response 'P'(previous).


                          (2)  R<ret>   The number of smoothline regions can

                                        be input if the default of 3 regions

                                        is not desired.  The graphic curser is

                                        returned for input of a number between

                                        2 and 9 inclusive then <ret>.  The 

                                        curser is returned again for end point

                                        selection.


EP-11
                          (3)  P<ret>   This response is appropriate only for

                                        the first time the graphic curser ap-

                                        pears. It obtains previously stored

                                        end point values and the step minimum

                                        from disk file automatically and pro-

                                        cedes directly through the computation

                                        and plotting of the smoothline back-

                                        ground removal.


                          (4)  L<ret>   This response requires positioning of

                                        of the graphic curser to locate the

                                        first end point. The response 'L' as-

                                        sumes the last data point as the other

                                        end point and begins immediate compu-

                                        tation of the smoothline.


                          (5)  (any char.)<ret>  position curser and respond

                                        with any character except N,R,P,L and

                                        a cross appears at the chosen point.

                                        The curser is then returned for the

                                        selection of the other end point.

                                        SL parameters and endpoints are stored

                                        on disk file for later recall.


EP-12
                  Except for the 'P' response, the curser will be returned for

                  selection of the pre-edge minimum in the data for extrapo-

                  lation of the step height.  At this point the user may re-

                  spond to the graphic curser with any character, however, an

                  optional MCMASTER TREATMENT of the step height normalization

                  may be obtained by responding with 'M'.  The MCMASTER coef-

                  ficients will then be obtained from the MCMSTR.TBL file af-

                  ter the next curser is responded to.  For all responses, the

                  step height is printed on the plot.  After the step height

                  selection, another graphic curser will appear allowing the

                  user to make a hardcopy of the screen containing all of the

                  smoothline information.   A response of 'E' to this final

                  curser will terminate the graphic smoothline steps. A 

                  response of 'X' will also terminate the graphic steps but

                  output of the smoothline option will be a normalized 

                  XANES plot rather than a CHI vs ENERGY plot. Any other

                  response to this final curser will cause the sequence of

                  steps for the selection of STEP MINIMUM, MCMASTER, and XANES

                  to be repeated.

                           (6)  M<ret>  is the reponse to the step height cur-

                                        ser after locating the pre-edge min-

                                        imum to initiate a MCMASTER TREATMENT

                                        of the step height determination. 

                                        After response to the final curser

                                        the screen will clear and a dialog

                                        prompting for the Mcmaster coef-

                                        ficients will appear (see sample 

                                        dailog below).


EP-13
                           (7)  E<ret>  is the response to the graphic curser

                                        which is returned after the step

                                        height calculation. This response

                                        ends the smoothline step unless the

                                        MCMASTER TREATMENT is specified by

                                        'M' response to the previous curser.

                                        In which case, this 'E' response

                                        begins the dialog for obtaining the

                                        MCMASTER coefficients.


                           (8) X<ret>   is the response to the final SL curser

                                        which will envoke the display of the

                                        normalized edge spectra or XANES

                                        rather than the display of the CHI

                                        vs ENERGY plot.  The XANES may be

                                        further treated as an ABSORPTION

                                        vs ENERGY data file but with a 

                                        xxxxxx.Xxx extension name instead

                                        of a xxxxxx.Axx extension name.

                                        Any other response returns the cursers

                                        again for a repeat of the step height

                                        determination sequence.


EP-14
                  (1) and (3) must be used prior all other responses if the

                  number of smoothline regions desired is other than 3.

                  A sample dialog for the MCMASTER TREATMENT is given here:

                  FOR MCMASTER TREATMENT, YOU MUST SPECIFY THE MCMASTER
                  COEFFICIENTS OF THE ABSORBER EDGE AND THE BACKGROUND EDGE.
                  TYPE ATOMIC NO. OF ABSORBING ELEMENT AND EDGE NO.
                  (11-103),(K=0,L=1,M=2,N=3) AND RETURN
                  NATOM,NEDGE ? 78,1<ret>
                  THE MCMASTER COEFFICIENTS FOR THE
                  PT L EDGE ARE: 17.3636   -2.2111     -.0731     0.0000
                  OK? Y<ret>
                  TYPE ATOMIC NO. OF BACKGROUND ELEMENT AND EDGE NO.
                  (11-103),(K=0,L=1,M=2,N=3) AND RETURN
                  NATOM,NEDGE ? 78,2<ret>
                  THE MCMASTER COEFFICIENTS FOR THE 
                            ARE:  0.0000    0.0000     0.0000     0.0000
                  OK? N<ret>
                  MCMASTER TABLE ENTRY NOT SPECIFIED OR REQUIRES CHANGE
                  ENTER NAME SPECIFYING THE X-RAY ABSORPTION EDGE : 
                  PT M EDGE<ret>
                  TYPE COEFFICIENT CHANGES WITH SEPARATING COMMAS
                  16.7024,-2.71631,0.,0.
                  THE MCMASTER COEFFICIENTS FOR THE
                  PT M EDGE ARE: 16.7024   -2.7163     0.0000     0.0000  
                  OK? Y<ret>


                  In this case the McMaster coefficients were obtained for 

                  a normalization of a Pt L edge.  The Pt L edge Mcmaster

                  coefficients were located in the MCMSTR TABLE on disk and

                  displayed for verification.  The coefficients for the back-

                  ground Pt M edge were not previously entered into the table

                  so the user must input the entry name and table values.

                  The typed coefficients are again displayed for verification

                  prior to the computation of the step height normalization.

                  A reponse of 'N' allows the user to modify the coefficients

                  for that table entry.


EP-15
            >[BELL]

            KV<ret>

                    The KV option makes the conversion of energy to photo-

                  electron wave vector representation (Reciprocal Angstroms).

                  The result is plotted with current headings and captions.


            >[BELL]

            FT<ret>

                    The FT option computes a forward FFT of a desired re-

                  gion of data in k-space.  The routine also interpolates

                  the data on an even grid of 96./(N) where N is chosen by

                  the user to be 2048, 4096, or 8192 prior to the transform.

                  If the phase removal option is in effect, a set of ins-

                  structions, invisible to the user, removes the effect of

                  a complicated phase shift. The transform magnitude as a

                  function of the radial harmonics is plotted.  Also, when the

                  phase removal option is in effect, the imaginary part of the

                  transformed data is plotted along with the magnitude. A

                  choice of windowing factor (% Hanning Window) and weighting

                  factor k**n are input by the user.


EP-16
                  Sample dialog :


                  (graphic curser is presented for selection of transform

                  range in k-space, acceptable responses are:)


                  N<ret>            Endpoints and input parameters will not be

                                    stored for later use. The default is save.

                                    Curser returns for selection of other end-

                                    point.

                  P<ret>            Previously saved endpoints and parameters

                                    are used for the transform.

                  (any char)<ret>   Locate curser and respond with any charac-

                                    ter except N and P to choose endpoints.


                  (After endpoint selection the terminal prompts for % window-

                  ing, k weighting and the number of points to be transformed)

    
                  %  10<ret>

                  K**  1<ret>

                  #  4096<ret>      NOTE: just a <ret> at this prompt causes
                                          the default of 4096 to be chosen.
					  a <1> at this point let you repeat 
					  the dialog and reselect the 
					  endpoints.		  
                  (This example sets up a forward transform of 4096 points

                  with the outside 10% of the data windowed by a Cosine

                  Hanning Window)

                  The resulting radial transform scaled and plotted.


EP-17
            >[BELL]

            BT<ret>

                    The BT option performs a an inverse (or back) FFT on

                  a determined region of the radial transform data. This

                  Fourier filtering step uses graphical curser input only.

                  No windowing is applied on the inverse transform, but a

                  back-transform window may be an option in the future.  When

                  the first curser appears the acceptable responses are 'N',

                  'P', and ' (any char) ' with the same meaning as in the

                  forward transform routine.  After selecting two endpoints

                  a third curser appears to hold the screen for hardcopy (if

                  desired).  At this time the endpoints may be reselected by

                  responding 'R' to the third curser.  The selection process

                  is repeated as above.  Any other response resumes the com-

                  putation of the backtransform.  The result K**N*CHI vs K is

                  plotted.  N is the weighting chosen in the FT option.


            >[BELL]

            KE<ret>

                    The KE option keeps the current output arrays by loading

                  them in to the input arrays in preparation for the next

                  step.  In this input-output array mode certain steps may be

                  executed repeatedly until a desired form of the data is ob-

                  tained.  The ability to back up and try again is of parti-

                  cular value when testing the outcome of various analysis op-

                  tions, such as SMOOTHLINE and FOURIER TRANSFORM steps.

                  NOTE: failure to keep the output array before the next step

                  causes the previous input array to go to the next option.

                  This may result in fatal errors some of the time.  In order

                  to continue, KE must be used after: EN,ES,SL,KV,DG,FT,BT,PH,

                  and FC. Auto-keep is being developed for future versions.


EP-18
            >[BELL]

            XP<ret>

                    The XP option uses the graphic curser to determine a

                  region of a plot to expand.  The new plot window is stored

                  in a replot stack having three levels.  In addition, up to

                  3 sets of plot windows can be stored and recalled from disk

                  file. Curser appears and the acceptable options are:


                  (any char)<ret>  Locate curser at desired lower left corner

                                   of the new expand window. A box corner is

                                   drawn. Curser is returned again for selec-

                                   tion of upper corner of the expand region.


                  S<ret>           Locate curser at desired lower left corner

                                   of the new expand window.  Response of 'S'

                                   indicates that the windows values will be

                                   stored in one of three storage locations

                                   on disk.  The response to the second curser

                                   determines which storage location is used.


                  1<ret>           Window values (1) recalled from disk when

                                   this response is given to the first curser.

                                   Window values (1) stored on disk when this

                                   response is given to the second curser af-

                                   ter a reponse of 'S' to the first curser.


                  2<ret>           Follows the same procedure.


                  3<ret>           Follows the same procedure.



                  Screen clears and expanded plot appears.   PL returns the

                  original plot.


EP-19
            >[BELL]

            RP<ret>

                    The RP option replots any of the last three expanded plots

                  where the original plot has not been been rescaled or PL has

                  not been executed.  The replot stack is reinitialized when

                  PL is executed.  The replot stack is particularly useful for

                  quickly obtaining various scaled blowups of the absorption

                  edge.  A prompt @ is given and the acceptable responses are:


                  *<ret>     most recent expanded plot

                  *-1<ret>   2nd most recent expanded plot

                  *-2<ret>   3rd most recent expanded plot


                  The screen is cleared and the data is replotted on the 

                  chosen scale.


            >[BELL]

            IS<ret>

                    The IS option allows the user to enter sets of plot win-

                  dows from the terminal keyboard into the replot stack.  The

                  stack holds three sets of windows for replotting until the

                  stack is reinitialized by new scaling or execution of PL.

                  New entries to the stack are prompted for and the new scale

                  is used in the replotting.


EP-20
            >[BELL]

            ES<ret>

                    The ES option produces a shift in the V output array of

                  the data so that the horizontal scale is zero at the point

                  specified by the graphic curser.  This is a particularly

                  useful option for energy edge calibration.  When the curser

                  appears the acceptable responses are:


                  (locate curser and type:)

                  N<ret>           The edge shift is not stored for later use.

                  P<ret>           Recalls previous edge shift

                  I<ret>           Terminal input of edge shift value

                  L<ret>           Terminal input of edge shift value loaded

                                   into storage location on disk, no edge

                                   shift is executed on the data.

                  (any char)<ret>  Normal execution of edge shift, stores

                                   edge shift in disk file.


                  ES always produces a new plot on the shifted scale but 

                  will only be retained after using the KE option.


            >[BELL]

            DG<ret>

                    The DG option uses the graphic curser for interactive

                  deglitching of the data.  DG allows easy multiple deglit-

                  ching.  The deglitching is terminated by the 'E' response

                  after an integral number of pairs of cut points are de-

                  termined using the graphic curser.  The deglitched regions

                  are replaced by a linear interpolation between pairs of cut

                  points and the deglitched data is replotted for inspection.

                  The KE option retains the deglitched data.


EP-21
            >[BELL]

            PT<ret>

                    The PT option uses the graphic curser to label the (X,Y)

                  coordinates of points on the plot.  The printed coordinates

                  usually avoid being written on the data.  Locate the curser

                  and return any character key in response.



            >[BELL]

            WF<ret>

                     The WF option writes a special format file to the de-

                  fault device for later recall using the RF option.  The file

                  contains the current input array and header to update the

                  parameters and captions.  The filename used for the file

                  depends on the current status of the data.  The format is

                  xxxxxx.*xx where



                        * = R        Raw ratio file

                        * = L        Log ratio file

                        * = A        Absorption vs Energy

                        * = X        (XANES) Absorption vs Energy

                        * = E        Chi vs Energy

                        * = K        Chi vs Wave Vector K

                        * = F        Fourier Transform Magnitude vs R

                        * = B        Backtransform K**n*CHI vs K

			* = P        Phase function extracted in PF

                  The special format files can be recalled from disk in either

                  the EXAPLT or EXAFIT programs.




EP-22

            >[BELL]

            PR<ret>

                    The PR option writes the same special format file to the

                  printer instead of the default device.  The header contains

                  the current parameters, captions, and data.



            >[BELL]

            RF<ret>

                    The RF option reads in a special format data file and up-

                  dates all arrays and labels.  The file name must be one of

                  the following  xxxxxx.*xx , where acceptable characters in

                  place of * are R,L,A,X,E,K,F, and B .  An error message is

                  displayed if the filename is in error or the filename is

                  not on the default device.

                  ERROR -- FILE NOT FOUND



            >[BELL]

            CS<ret>

                    The CS option initiates a hard copy of the the graphic

                  terminal screen if a hardware screen copy unit is available.

                  A pause of about 20 seconds occurs before the > prompt

                  reappears. This pause is for compatibility with slow

                  hardcopy units.




EP-23

            >[BELL]

            PM<ret>

                    The PM option prints to the line printer a copy of the

                  the current header map only.  The header contains the

                  current parameters, captions, and data map.



            >[BELL]

            LM<ret>

                    The LM option lists to the terminal screen a current map

                  header. The header contains the current analysis parameters,

                  captions, and data map. 




            >[BELL]

            DF<ret>

                    The DF option computes a divided difference differential

                  of the W output array and plots the V,dW arrays on the new

                  scale.  Ideal to use for locating the maximum slope assoc-

                  iated with the absorption edge for the calibration of the 

                  edge. This differential cannot be kept and PL returns to the

                  original V,W plot.


EP-24

            >[BELL]

            PF<ret>

                    The PF option provides most of the EXAFS phase analysis

                  and is used after the phase of the EXAFS oscillations is 

                  extracted in the back-transform BT.  The choices within the

                  phase analysis and fitting coding are numerous. The plotting

                  for this option is self-contained in the PF module so that

                  consecutive executions of the PF option is possible.  The 

                  phase tables are accesssed frequently during the execution

                  of PF coding and should be maintained on the default device.

                  The choices within PF include display of phase data and

                  functions, list of phase data and fitting of phase data.
		
		  The user may choose to display the experimental phase,

		  display a phase stored in the tables TEOLEE.PHT, PARAM.PHF,

		  or display both at the same time.  The PHASE PROGRAM is

   		  used to construct the phase tables and the entries therein.

		  It is also possible to store the phase in a normal 

		  EXAFS file.

		  The user may choose to perform three types of fits to

                  the phase data.  One is a linear least-squares fit of a

                  parameterized phase function 

                           phi(k) = 2kR + A0 + A1k' + A2k'**2 + A3/k'**3

                  to the experimental data, where the An's are determined by

                  by the best least-squares fit, provided that the values of

                  R and E0 (k'=sqrt[k**2 - .262467]) are known by the user.

                  The coefficients An and E0 can be displayed on the screen

                  and if desired can be entered into the phase tables for

                  later reference.  The second type of fit is a non-linear


EP-25

                  least-squares iterative fit of a known phase function

                  (only parameterized table or terminal input) to the data in

                  order to determine R and E0.  Of course, a change in R is

                  equivalent to a change in the slope of phi(k) which has a

                  large effect on the phase function a larger values of k. The

                  change in E0 is proportional to 1/k in the phase and thus 

                  has its greatest effect at smaller values of phi(k).  In

                  this respect the two parameters are at most weakly coupled,

                  and therefore ought to converge to a reasonable fit within

                  a few iterations.  The last type of fitting in the phase 

                  module is linear least squares fitting to a phase residual

                  (difference between an experimental phase and a known phase

                  from the tables or input from the terminal) for modeling

                  disorder effects on the EXAFS phase.  The phase residual is

                  modeled by linear and cubic terms (Eisenberger et.al.)

                          delphi(k) =  C1k + C3k**3

                  where the coefficients  C1 and C3 model the effects of dis-

                  order on the EXAFS phase.  C1 is related to the thermal ex-

                  pansion of the nearest-neighbor bonds. This fitting method

                  is informative provided that reference phase shifts are well

                  characterized and fit the data well for small disorder.


EP-26
                  Sample PF dialog:


                  (D)ISPLAY ONLY OR DISPLAY AND (F)IT ? D<ret>
		  (L(ist) will list the phase data on the printer)
                  (E)XPERIMENTAL OR (T)HEORETICAL PHASE OR (B)OTH ? B<ret>
                  (S at this point will interpolate and store the phase at
		   N points, specified in a specific dialog)
                  DO YOU WANT TERMINAL (I)NPUT OF YOUR KNOWN PHASE OR A
                  (P)ARAMETERIZED OR (T)ABULAR PHASE FROM DISK TABLES ? T<ret>
                  (S at this point gives the possibility to shift the phase
		   at 2 PI)
 		  PLACE TABLES DISK IN DISK DRIVE AND THEN
                  SPECIFY ABSORBING ELEMENT, QUANTUM NO. L : PT,2<ret>
                  SPECIFY SCATTERING ELEMENT : PT<ret>
                  ABSORBER:
                  PT2      xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx
                  xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx
                  xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx
                  SCATTERER:
                  PT       xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx
                  xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx
                  xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx xxxxxxxx
                  OK? Y<ret>
                  TYPE IN E0 FOR YOUR TABLE: 0.0<ret>
                  TYPE IN R1 FOR YOUR TABLE: 2.774<ret>


                  This example shows the dialog for displaying both Pt

                  experimental and reference tabular phase shifts on 

                  the same plot.  The phase tables are accessed for the

                  entries PT2 and PT to construct the reference phase

                  shift and is shifted appropriately by E0 if specified 

                  by other than zero. The R1 value is specified for the

                  subtraction of 2kR1 from the experimental EXAFS phase.

                  Error messages occur if the phase tables are not found

                  on the default disk or if a particular entry is not found

                  in the tables.  The PF option will then terminate and the

                  > prompt will reappear.  A successful table search will

                  result in the display of the table entry values for 

                  verification.  Table entries can only be modified in the

                  PHASE PROGRAM, so the user must exit EXAPLT if changes are

                  desired.  We suggest that the reference phase shifts be

                  loaded into the tables and carefully verified before the

                  PF option is used in EXAPLT.  


EP-27

            >[BELL]

            PH<ret>

                    The PH option sets up the phase removal of a known phase

                  shift from the data prior to Fourier transforming.  Access

                  to the phase tables is required.  The user is prompted to

                  choose the input phase shift to be entered from tables or 

                  manually from the terminal keyboard.  The phase shift to be

                  removed is stored in an array which is passed invisibly

                  to the Fourier transform.  The PH option should be used

                  after the conversion to the wave vector representation and

                  before the Fourier transform.  The dialog is similar to the

                  phase table dialog in the PF option, however, the user must

                  specify whether to remove or add effects of scattering phase

                  shifts.  The Chi vs K oscillations are then replotted 

                  in preparation for the Fourier transform, however, it is

                  necessary to use the KE option to keep the phase shift array

                  prior to using PF.  If the phase shift was determined from

                  tabular entries then the range of data available for trans-

                  forming is limited to the range of the tabular phase func-

                  tion in k (~ 3.8 - 15.2).  The phase removal option proceeds

                  invisibly to the user during the Fourier transforming until

                  the plot is made.  In this option the imaginary part of the

                  Fourier transform is plotted along with the magnitude of the

                  Fourier transform.


EP-28

            >[BELL]

            AF<ret>

                    The AF option provides a comparison of experimental and

                  reference/empirical amplitudes by simple display of the

                  envelopes or by the LN RATIO of the amplitudes technique. 

                  A reference amplitude may be input from the terminal in

                  functional form  AMPL(K)=N/KR**2*F(K)*exp(-2K**2R**2)  with

                  F(K)= A/(1+B**2(K-C)**2), tabular form from disk tables, or

                  interpolated from an input   K**N*CHI file (xxxxxx.Bxx) on

                  disk.  The internal options in AF allow display of the

                  the amplitude envelopes or the LN RATIO of amplitudes

                  vs k**2 and provide least squares curve fitting to obtain

                  the coefficients of

                                LN RATIO= C0+C2K**2+C4K**4

                  where the intercept C0 is  LN( N/R**2 / No/Ro**2 ), the

                  slope C2 = -2 SI**2 (SI**2 is associated with the EXAFS

                  DEBYE WALLER FACTOR in the case of small disorder) and

                  and the quadratic term C4 is an increasing effect of large

                  disorder.  Coding is provided for scaling and weighting the

                  reference amplitude prior to displaying the envelopes or

                  computing the LN RATIO.  A response to the weighting dialog

                  of  /<ret> assumes a default of no weighting of the

                  reference amplitude.  For some cases, it may be useful to 

                  fix C0 and only determine C2 and C4 from least squares fits.

                  Coding is provided for this.  Manual fit of the coefficients

                  C0, C2, and C4 is an option as well as the selection of the

                  fit range in K**2.  



EP-29

                    The selection of 'Beat-adjustment' analysis in AF allows

                  the extraction of the backscattering amplitude of a single

                  shell from the backtransformed data of two close-lying 

                  shells of the same backscatterer type.  The approximate

                  formula used is

                  AMP(1 shell)= AMP(2 shells)/CORRECTION

                  where

                  CORRECTION= SQRT{1+C**2+2COS[2(R2-R1)K]}

                  and

                  C=(R1/R2)**2 * EXP[-2(SIGM2-SIGM1)*K**2].

                  The necessary input for this adjustment is R1,R2 (first and

                  second shell bond distance) and SIGM1,SIGM2 (first and 

                  second shell disorder factor).



EP-30

            >[BELL]

            FC<ret>

                    The FC option provides an absorption dependent correction

                  to a fluorescence spectrum which has been removed off of the

                  background absorption level using the 'X' option (XANES) in

                  in SL.  After FC is selected the plot clears and a dialog

                  appears which prompts for the fluorescence correction

                  factor "A".   A is determined from density and thickness

                  relationships in the fluorescence sample.  This correction

                  reduces the measured absorption in proportion to the

                  absolute absorption above the background.  In dilute

                  concentrated samples or thin samples the correction is

                  negligible.  If Mcmaster treatment of the XANES was chosen

                  in 'SL' then the same Mcmaster stepheight must be used

                  to reconstruct the absorption height.  The Mcmaster

                  coefficients obtained with the same dialog as in 'SL'.

                  The corrected spectrum is then replotted for

                  inpection or furthur processing. 



EP-31

            >[BELL]

            ED<ret>

                    The ED option provides a multiple curve plotting step

                  for simultaneously displaying up to four edge or near edge

                  absorption or fluorescence spectra.  In addition, the

                  difference spectra may be displayed rather than the edge

                  spectra.  Difference spectra are simply the normalized

                  absorption spectra with a reference absorption spectrum

                  subtracted.  The energy scales may be shifted to account for

                  chemical differences (shifted peak positions). Normally, the

                  choice of energy coincidence is made based on minimizing the

                  the area under the difference curve in a specific energy

                  region.  A sample dialog is provided:

                  Assume for this dialog that the data file in the EXAPLT
                  program is a CUO (copper oxide) absorption edge. It is then
                  file #0 for the ED option.

                  (P)LOT EDGES OR (D)IFERENCE EDGES? : D<ret>
                  ENTER NUMBER OF INPUT FILES (0-3 ;DEFAULT=0) : 3<ret>
                  ENTER REFERENCE FILE NUMBER (0-3) : 3<ret>
                  TYPE ENERGY RANGE  EMIN,EMAX ;DEFAULT (/)=MAX RANGE: /<ret>
                  PLEASE WAIT A MOMENT FOR SPLINE COMPUTATION
                  TYPE INPUT FILE NAME #1 : CUCL.X35<ret>
                  TYPE EDGE SHIFT #1 : 0.<ret>
                  PLEASE WAIT A MOMENT FOR SPLINE COMPUTATION
                  TYPE INPUT FILE NAME #2 : CUCL2.X35<ret>
                  TYPE EDGE SHIFT #2 : -3.5<ret>
                  PLEASE WAIT A MOMENT FOR SPLINE COMPUTATION
                  TYPE INPUT FILE NAME #3 : CUFOIL.X05<ret>
                  TYPE EDGE SHIFT #3 : 0.<ret>
                  PLEASE WAIT A MOMENT FOR SPLINE COMPUTATION


                  This discribes an example of multiple display of 4
                  difference spectra.  The difference spectra will be
                  plotted as follows:

                  difference curve #0  CUO   -  CUFOIL   unshifted

                  difference curve #1  CUCL  -  CUFOIL   unshifted

                  difference curve #2  CUCL2 -  CUFOIL   shifted by -3.5eV

                  difference curve #3  CUFOIL-  CUFOIL   unshifted




EP-32

                  A similar dialog occurs for the edge plot mode, but

                  the prompt for reference file number does not occur.

                  Scaling is provided in the coding and error messages

                  for file specification errors.  Only those files

                  prior to a file specification error will be plotted

                  or differenced.  To re-display the edges simply

                  respond with  'ED' to the next > prompt after the

                  initial edge display.  A response of 'PL' causes

                  a return to the state prior to the first 'ED' response.

                  If difference spectra are displayed then a 'KE' response

                  after a successful display will retain the difference 

                  curve #0 for further processing.


                  ERROR - FILE NOT FOUND OR ERROR SPECIFYING FILE

                  ERROR - WRONG FILE TYPE FOR EDGE OR DIFFERENCE DISPLAY



EP-33

            >[BELL]

            TI<ret>
                     The TI option contains coding for interpolating the

                  amplitude or phase constructed from the inverse Fourier

                  transform step.  The interpolation is over the TEOLEE

                  range and can be stored as an entry in TEOLEE.TBL tables.

                  The phase and amplitude data must coincide with the range

                  in K (3.7795-15.1178) for the interpolation to execute.

                  Prompts for amplitude weighting and the removal of 2KR

                  from the phase are similar to the 'AF' and 'PF' options.

                  There is a prompt for Table Entry Name (2-letter element

                  name) for each entry.  The coding allows a new entry to

                  supercede an old entry only when you specify it. Coding

                  for 'beat-adjustment' in two shell amplitudes is iden-

                  tical to the 'AF' option. 




EP-34

NOTES:   This section is for comments and suggestions

            BE SURE TO REMEMBER THE KE OPTION AFTER EN,DG,ES,SL,KV,FT,BT,PH,FC


            THE VALUES STORED IN THE HEADER (MAP) FILE, USED FOR THE HEADER OF

            THE SPECIAL FORMAT FILES WRITTEN TO DISK AND AS A RECORD OF THE

            ANALYSIS, COULD POTENTIALLY DIFFER FROM THOSE ACTUALLY USED IN THE

            DATA ANALYSIS IF THE 'N' (NOSAVE) RESPONSE IS USED WITHOUT DIS-

            CRETION.


            SPECIAL FORMAT FILES SHOULD BE WRITTEN AT KEY PLACES IN THE ANALY-

            SIS SO THAT IF FATAL ERRORS OCCUR, THE ANALYSIS CAN BE RESUMED

            RATHER THAN STARTED FROM SCRATCH AGAIN.  WE SUGGEST WRITING AT THE

            ABSORPTION VS ENERGY STAGE AND AT THE CHI VS K STAGE.  THIS WAY

            ANALYSIS OPTIONS SUCH AS SMOOTHLINE AND FOURIER TRANSFORMING MAY

            MAY BE RETRIED WITH MINIMUM LOSS OF TIME AND EFFORT.


            IF A FOURIER TRANSFORM IS WRITTEN TO THE DISK FILE THEN IT MAY

            ONLY BE RECALLED TO THE PROGRAM FOR DISPLAY.  THE LARGE COMPLEX

            FOURIER TRANSFORM ARRAY IS NOT RESTORED, ONLY THE MAGNITUDE. 

            ANY SUBSEQUENT BACK-TRANSFORM, REQUIRING THE USE OF THE COMPLEX

            ARRAY GENERATED IN THE FORWARD TRANSFORM, CANNOT BE SUCCESSFULLY

            EXECUTED.  THIS MEANS THAT PHASE AND AMPLITUDE INFORMATION IS ONLY

            OBTAINED AFTER A SEQUENCE OF FORWARD AND INVERSE TRANSFORMS IS

            EXECUTED.  COMPLEX PHASE AND AMPLITUDE IS NOT RESTORED BY SIMPLY

            READING IN A BACKTRANSFORMED (.B*) FILE  


            ERRORS OCCUR WHEN 8 OR 9 REGIONS IS SPECIFIED IN 'SL' , THIS PROB-

            LEM HAS NOT BEEN CORRECTED




EP-35

            PT DISPLAYS THE COORDINATES OF THE CHOSEN SCREEN POINT AND IT

            GENERALLY AVOIDS WRITTING ON THE GRAPHICAL DATA.  SOMETIMES IT

            FAILS WHEN THE SCREEN IS VERY CROWDED AND PRODUCES UNPREDICTABLE

            RESULTS AND SOMETIMES GOES INTO AN INFINITE SEARCH LOOP.  USE

            WITH CARE AND ON A LESS CROWDED SCREEN.


            A SPECIAL FLAG CONTROLS THE OVERPLOTTING OF THE IMAGINARY AND 

            MAGNITUDE OF THE FOURIER TRANSFORM IF THE PHASE REMOVAL  (PH)

            IS IN EFFECT.  IF THE TRANSFORM IS RETAINED WITH (KE) THEN A

            SUBSEQUENT (BT) MUST BE EXECUTED TO CLEAR THE FLAG, OTHERWISE THE

            OVERPLOTTING WILL CONTINUE TO OCCUR EVEN IF NEW DATA IS READ IN

            AND OTHER OPTIONS EXECUTED.  IF THE PHASE REMOVED TRANSFORM IS NOT

            RETAINED WITH (KE) THEN SIMPLY TYPE (PL) TO RESTORE NORMAL

            PLOTTING.



EP-36


                        INDEX OF EXAPLT DOCUMENTATION

                                                             Pages

Introduction                   ..............................   1
Structure                      ..............................   1,2
Operation                      ..............................   2
Hardware                       ..............................   3
Instructions                   ..............................   3,4,5,6
Description of Options

AF --- Amplitude fitting       ..............................   28,29
BT --- Back transform          ..............................   17
CS --- Copy screen             ..............................   22
DF --- Edge differential       ..............................   23
DG --- Deglitghing             ..............................   20
ED --- Edge differencing       ..............................   31,32
EN --- Energy conversion       ..............................   9
ES --- Energy shift            ..............................   20
EX --- Exit                    ..............................   7
FC --- Fluorescence correction ..............................   30
FT --- Forward transform       ..............................   15,16
IS --- Stack input             ..............................   19
KE --- Keep                    ..............................   17
KV --- Wave Vector conversion  ..............................   15
LM --- List map                ..............................   23
OP --- Option                  ..............................   8
PF --- Phase fitting           ..............................   24,25,26
PH --- Phase removal           ..............................   27
PL --- Plot                    ..............................   8
PM --- Print map               ..............................   23
PR --- Print file              ..............................   22
PT --- Point coordinates       ..............................   21
RE --- Read raw data files     ..............................   7
RF --- Read special files      ..............................   22
RP --- Replot Stack            ..............................   19
SL --- Smoothline Background   ..............................   10,11,12,13,14
TI --- Table Interpolation     ..............................   33  
WF --- Write special files     ..............................   21
XP --- Expand plot             ..............................   18

Notes and comments             ..............................   34,35
Index                          ..............................   36


EF-1

***************************************************************************
******** DOCUMENTATION FOR THE EXAFIT, EXAFS CURVE FITTING PROGRAM ********
***************************************************************************
                        Revised  05-Nov-82


INTRODUCTION: The EXAFIT PROGRAM is a non-linear, multi-shell least squares

            curve fitting program for modeling EXAFS oscillations in wave

            vector (K) space.  The EXAFIT program is written entirely in 

            Fortran IV.  The model EXAFIT function is given by

 
            K**M+1 X(K) = K**M SUM [ Ni/Ri**2  Ai/{1+Bi**2(K-Ci)**2}

                        x exp{-2Ri/(GiK+Hi)} exp{-2(KSIi)**2}

                        x sin(2KRi+P0+P1K+P2K**2+P3K**-3) ].


            The EXAFIT program, modeled after the Lytle EXAFS fit program

            (currently running in batch mode on an IBM 370), has been re-

            developed and adapted to run in an interactive RT-11 environment.

            This program, which stands alone except for the input data files,

            occupies ~ 20K of core memory (program and overlay storage) and

            more than 30K of extended memory (array storage).  The EXAFIT pro-

            gram requires much less user interaction than is required in the

            EXAPLT program with the bulk of the user intervention occuring

            during the setup of the fits.  In setting up the fits the user is

            prompted to choose which parameters to vary and is then prompted

            to provide best estimate values for these parameters. The capabil-

            ity to store a setup for later recall is one of the convenient

            features of this RT-11 adapted curve fitting program.

                The chosen parameters are refined by an iterative least-

            squares procedure until a desired degree of fit is achieved or

            until divergence of fit occurs.  To maintain convergence of the

            varied parameters, a damping factor is applied to the system of


EF-2


            independent equations, the magnitude of which is selected by the

            user.  Where initial estimates may be poor, a larger damping

            factor assures that the refinements don't overcorrect and diverge.

            The damping factor can be relaxed as a good fit is approached.


OPERATION:    The EXAFIT PROGRAM should run from the system device so as not

            not to interfere with the program I/O.  The input data files to be

            read into the EXAFIT program during the setup should be maintained

            on the default I/O device.  Room should be left on the default

            device for several setup storage files and for scratch storage of

            the coefficient matrix regenerated for each iteration.  This space

            amounts to less than 100 blocks in most cases.   The only accept-

            able data files to be read into the EXAFIT program are the spec-

            ially formatted data files produced in the EXAPLT or TESTFN pro-

            grams.  A utility program is necessary for adapting any other file

            formats into the special file format.


HARDWARE:     Hardware requirements for the EXAFIT program call for at least a

            16 bit PDP,LSI 11 processor with extended memory capability for

            accessing 128K words.  A Tektronix 4010,14,25 or equivalent term-

            inal supporting the Tektronix Terminal Control System (TCS) is

            necessary, preferably including a compatible screen copy unit. 

            A hard disk or dual density floppy drive is a prerequisite to

            installation.  A line printer such a VERSATEC 1200, which has

            optional screen copy hardware, provides a versatile print/plot

            mode ideal for the fast output of the EXAFIT program.  Floating

            point hardware in the processor is essential.


EF-3

SETUP:        The setup routine in the EXAFIT program is an important routine

            for user interaction because it includes the selection of all the

            fit parameters, input of the data, output of the setup map, and

            the storage of setup parameters.   The setup coding is modeled

            after the card image stack (1-8) used for batch mode execution of

            Lytle's EXAFS fit program, however, in this program the user

            selects the desired card image and then is interrogated to input

            the parameters to complete the card setup.  The efficiency of the

            card setup is improved by the ability of the user to recall a

            previous setup and to default through the interrogation.  The card

            setup coding is terminated by selecting CARD 0 and control is

            passed to read in the data, to print the map, and to execute the

            fits.



EXECUTION:    The input card parameters depend on the card image chosen (0-8,

            0 - terminates card input).  The cards and their associated par-

            ameters will be presented one-by-one below.  First, the dialog

            leading to the card setup will be discussed.  Be careful that the

            default device contains all of the necessary data files and stored

            setup files (if any) prior to program execution.  Sample dialog:

            (Run the EXAFIT PROGRAM)


                 .R EXAFIT<ret>             ;begins execution

                 DO YOU WANT TO READ CARD SETUP PARAMETERS FROM DISK?

            (The response to this question determines whether a previously
            stored setup is placed active.  To stop or exit the EXAFIT program
            just type a   ^C at any time)

                 N<ret>                     ;no previous setup desired, 
                                            control passed to card selection
            ****

                 Y<ret>                     ;previous setup desired


EF-4

                 DO YOU WANT TO LOOK AT A TABLE OF SETUP DATA FILES?

            (The response of N<ret> to this question, skips to the next
            question)

                 Y<ret>                     ;setup file table listed on 
                                            terminal


                 TABLE OF CURRENT SETUP FILES ON DEFAULT DISK

                 SETUP FILE 1        CUFOIL.B01
                 SETUP FILE 2        FEFOIL.B02
                 SETUP FILE 3        < UNUSED >
                 SETUP FILE 4        < UNUSED >
                 SETUP FILE 5        < UNUSED >
                 SAVE SETUP FILE FOR ABNORMAL TERMINATIONS:
                 SETUP FILE 6        

            (In this example the setup files for fits to CUFOIL.B01 and
            FEFOIL.B02 are the only ones residing on the default device
            and only one of them may be chosen to be active.  If no setup
            files are found on disk then an error message occurs
            NO SETUP FILES ON DEFAULT DISK
            and the program is restarted from the beginning)


                 TYPE NUMBER OF SETUP FILE FOR INPUT (1-5)


            (Again, only 1 or 2 are acceptable choices other choices cause
            an error message
            SETUP FILE     "N"  NOT FOUND ON DISK
            and prompt for another look at the setup table)

                 1<ret>                    ;setup file for CUFOIL chosen

            ****

            (At this point control is passed to the card selection and setup 
            coding.  Card 1 is usually chosen first because certain parameters
            chosen in Card 1 affect the other cards. One example is the number
            shells to be fit.)


                 TYPE INPUT CARD NUMBER (0-8) : 1<ret>



            A list of the each specific card dialog is contained in the next

            section.


EF-5

CARDS:        This section contains specific card descriptions and sample

            dialog.  In most cases, the card parameter values displayed can

            be defaulted or changed by typing to the terminal.  For virtually

            every prompt the response /<ret> constitutes a default to the

            displayed parameter value.

             

            CARD 1 dialog:


                 CASENAME:  CUFOIL.B01 TYPE CHANGE: /<ret>

            (Casename specifies input data file to be fit)

                 NO. OF SHELLS:   1 TYPE CHANGE: /<ret>

            (This number determines the number of shells [ the EXAFS function,
            above, is summed over the number of shells with a maximum of 10 ].
            Normally 1 or 2 shells is specified.)

                 NO. OF DAMPS PER ITERATION:  10 TYPE CHANGE: /<ret>

            (This number specifies the number of times a damping factor is
            applied during one iteration.  In this example the damping factor
            is varied 10 times from a minimum value of 1.0 to a maximum value
            (>1.0) specified by the user.  For each iteration, the results of
            each damping factor application are tested for best fit and are
            used to seed the next iteration.)

                 NO. OF ITERATIONS:  10 TYPE CHANGE: /<ret>

            (This parameter has no other purpose than to limit the iteration
            process.  In general, a fit converges within 10 iterations, how-
            ever, it is conceivable that a complicated multi-shell fit could
            take many iterations.  Our experience has been that 10 iterations
            provides a good stopping point from which to evaluate whether to
            continue the iteration process.)


EF-6

                 FIT INCREMENT:   5 TYPE CHANGE: /<ret>

            (This number determines the grid on which the model EXAFS function
            is calculated.  In this example every 5th data point is used in
            the calculation.  Of course, the time of calculation is propor-
            tional to the number of points to be calculated so it is recom-
            mended that 4 or more be specified unless the data contains ra-
            pidly varying oscillations.)
 

                 DAMPING FACTOR:  0.100 TYPE CHANGE: /<ret>

            (The damping factor specified here is not actually the maximum
            damping factor applied to the iterations but rather is the number
            added to 1.0 to obtain the maximum damping factor.)


                 PERCENT CHANGE STOP:   0.010 TYPE CHANGE: /<ret>

            (This number determines the desired goodness of fit.  When all
            parameters change by less than this specified percent the itera-
            ting is terminated.  A reasonable range of values is 0.010 to
            0.100 percent where smaller values increases the number of
            iterations required for the fit.)

                 MULTPLY DATA BY Q*K**N
                 Q:    1.000 TYPE CHANGE: /<ret>
                 N:    0.000 TYPE CHANGE: /<ret>
                 WEIGHTING*CHI=K**M*SUM[ ]
                 M:  -1 TYPE CHANGE: /<ret>

            (These parameters determine the weighting of both the data and
            the model EXAFS function.  The combinations of the weightings are
            important when using standard or reference spectra for determining
            the amplitude envelope in a given shell.  For most every applica-
            tion Q=1.0 [fits to fractional contributions to the oscillations
            (Q<1.0) could be instructive in a few instances].   The exponent N
            determines the power weighting of the input data for the fit.
            Larger values of N accentuate the fits to the data at higher k.
            M determines the weighting applied to the sum over shells in the
            calculated EXAFS function.   In CARD5 the user determines the 
            separate weighting of each shell as Qi*K**Ni.  The user should be
            aware that an implicit K**1 weighting is applied in the calcula-
            tion of each shell and, therefore, should carefully chose the
            parameters Qi,Ni in CARD5 to weight each shell the same as the
            data.  M should be chosen to compensate for the implicit K**1
            weighting of all the shells.  This convention should avoid the
            potential of confusion when attempting to balance the weighting
            of the data and the calculated EXAFS function.)


EF-7

                 TESTCASE? N TYPE CHANGE: /<ret>

            (The generation of test EXAFS files from the model function, 
            which is computed in the EXAFIT program, is still in the develop-
            mental stage.  If the user requires a test case then one can be
            created separately using the TESTFN program.)

                 SETUP MAP? Y TYPE CHANGE: /<ret>

            (A printout of the current setup is produced in a card image
            format similar to Lytle's program.)

                 STORE SETUP? Y TYPE CHANGE: /<ret>

            (The current card setup can be stored to disk in one of 5
            storage locations.)



            After the last <ret> the setup up of CARD 1 is complete and the

            input file specified for casename is read in.  A error message

            occurs if no case name is specified in CARD 1

            NO CASE NAME IN CARD 1

            Another error message can occur during a read of the casename

            or file not found. In this case the error is terminal to the

            EXAFIT program but not before the setup card parameters are

            saved.

            ABNORMAL TERMINATION: SETUP DATA RECOVERED IN SETUP FILE 6
            AFTER EXITING THE EXAFIT PROGRAM, RENAME THIS FILE OR DELETE IT!


EF-8
    
        CARD 2 dialog:



                 MAXIMUM K-RANGE AVAILABLE
                 XKMIN:       3.560
                 XKMAX:      18.356
                 K-RANGE TO FIT
                 KMIN:       3.700<ret>
                 KMAX:      15.500<ret>

            (The maximum range of the input data is displayed on the terminal
            and should be accurate provided that CARD 1 was setup prior to
            CARD2. Spurious results may occur if CARD 1 is not executed first.
            The user specifies the fit range which must be a sub-range of the
            maximum available range.  A default /<ret> or input of numbers
            outside the allowable range produces a default to the maximum
            range.)
 
            The dialog for CARD 2 setup is completed.



            CARD 3 dialog:



                 PARAMETERS TO VARY IN THE FIT
                 SHELL:   1
                 N ? N    TYPE CHANGE: /<ret>
                 A ? N    TYPE CHANGE: /<ret>
                 R ? N    TYPE CHANGE: Y<ret>
                 SI? N    TYPE CHANGE: /<ret>
                 B ? N    TYPE CHANGE: /<ret>
                 C ? N    TYPE CHANGE: /<ret>
                 P0? N    TYPE CHANGE: /<ret>
                 P1? N    TYPE CHANGE: /<ret>
                 P2? N    TYPE CHANGE: /<ret>
                 P3? N    TYPE CHANGE: /<ret>
                 G ? N    TYPE CHANGE: /<ret>
                 H ? N    TYPE CHANGE: /<ret>
                 E0? N    TYPE CHANGE: Y<ret>


            (For multiple shell fits the dialog is repeated.  In this
            example the parameters R1 and E0 are to be varied in the fit.
            The index on the R is the shell index.  E0 is specified only in
            the first shell.  E0 is equivalent to an ENERGY EDGE SHIFT and is
            refered to as the "inner potential" in the EXAFS literature.  E0
            has the effect of changing the K-scale of input data to match the
            K'-scale of the calculated data, where K'= sqrt(K^2-.262467E0).

            This completes the dialog for CARD 3 setup.


EF-9
            CARD 4 dialog:


                 TRIAL PARAMETERS
                 SHELL:  1
                 N :  0.00000E-01   TYPE CHANGE: 12.0<ret>
                 A :  0.00000E-01   TYPE CHANGE: 1.0<ret>
                 R :  0.00000E-01   TYPE CHANGE: 2.556<ret>
                 SI:  0.00000E-01   TYPE CHANGE: 0.000<ret>
                 B :  0.00000E-01   TYPE CHANGE: 1.0<ret>
                 C :  0.00000E-01   TYPE CHANGE: 1.0<ret>
                 P0:  0.00000E-01   TYPE CHANGE: 1.0<ret>
                 P1:  0.00000E-01   TYPE CHANCE: 1.0<ret>
                 P2:  0.00000E-01   TYPE CHANGE: 1.0<ret>
                 P3:  0.00000E-01   TYPE CHANGE: 1.0<ret>
                 G :  0.00000E-01   TYPE CHANGE: 0.0<ret>
                 H :  0.00000E-01   TYPE CHANGE: 1000.0<ret>
                 E0:  0.00000E-01   TYPE CHANGE: 5.0<ret>


            (The dialog is repeated for multiple shell fits.  In this
            example the setup of CARD 4 is for a 1-shell fit to the CUFOIL
            EXAFS oscillations where the parameters have their respective
            meanings in the model EXAFIT equation above.  However, there are 
            special cases which exist when either A=B=C=1. or P0=P1=P2=P3=1.
            When A=B=C=1.0, the parameterized scattering amplitude factor
            A/{1+B^2(K-C)^2} is not used in the model calculation, but rather
            a reference amplitude which can be specified in CARD 5 and CARD 7.
            The scattering amplitude envelope can be obtained from a reference
            or standard data file in specified in CARD 5 or obtained from a
            table of K,AMPLITUDE pairs entered in CARD 7.  When all of the 
            phase shift parameters (P's) are 1.0 the scattering phase shift is
            determined from a table of K,PHASE SHIFT values entered in CARD 8.
            When A,B,C and the P's are not all equal to 1.0 then the respec-
            tive CARDS 5,7 and 8 are ignored.)

            This ends the setup of CARD 4.


EF-10

            CARD 5 dialog:


                 REFERENCE ENVELOPE DATA
                 SHELL:  1
                 NO. OF ENVELOPE POINTS [0 to 100]:   0 TYPE CHANGE: /<ret>
                 CASE MEMBER:              TYPE CHANGE: CUFOIL.B01<ret>
                 WEIGHTED BY Q1*K**N1
                 Q1:      0.000 TYPE CHANGE: .544<ret>
                 N1:      0.000 TYPE CHANGE: 0.0<ret>


            (In this example the reference envelope is obtained from the
            CUFOIL.B01 data.  To maintain compatible weightings between the
            input data and the calculated function, the weighting of the
            reference envelope must be Q1*K**N1.  The prefactor Q1, deter-
            mined to be R**2 /N (R=2.556 and N=12), cancels exactly the N/R**2
            dependence of the EXAFS amplitude in the reference file.  If no
            case member or reference file is specified and A=B=C=1.0 then a
            tabular amplitude is assumed.  In this case, the NO. OF ENVELOPE
            POINTS must be specified in CARD 5 to be greater than zero.  The
            user must then enter the same number of K,AMPLITUDE envelope pairs
            in setup CARD 7.)


            This ends the setup dialog for CARD 5.



            CARD 6 dialog:


                 TESTCASE NAME:            TYPE CHANGE: /<ret>

            (The testcase name determines the file name for writing a test
            EXAFS function to disk.  The test EXAFS function is the same
            as the calculated function used in the fit.  Presently, the coding
            to do this is in the developmental stage, therefore, CARD 6 is not
            effective at this time.)


            This ends the setup dialog for CARD 6.



EF-11

            CARD 7 dialog:


                 INPUT OF ENVELOPE PAIRS
                 SHELL:  1
                 ENVELOPE PAIR 1   0.00000E+00,0.00000E+00
                 TYPE CHANGES: 3.7,.535<ret>
                       .
                       .
                       .
                 ENVELOPE PAIR 25  0.00000E+00,0.000000E+00
                 TYPE CHANGES: 15.5,.0912<ret>


            (This dialog may be repeated if multiple shells of tabular
            envelopes are specified.  This example illustrates the dialog
            for one shell with 25 (maximum of 100) pairs of points specified
            in CARD 5.  The envelope pairs are typed in as K,AMPLITUDE. The
            EXAFIT program interpolates the envelope points onto the cal-
            culated function scale.)


            This ends the dialog for CARD 7.



            CARD 8 dialog:


                 INPUT PHASE SHIFT
                 SHELL 1 HAS   0 PAIRS OF POINTS   TYPE CHANGE: 17<ret>
                 PHASE SHIFT PAIR:  1    0.00000E+00,0.00000E+00
                 TYPE CHANGES:  3.7795,24.2716<ret>
                       .
                       .
                       .
                 PHASE SHIFT PAIR: 17    0.00000E+00,0.00000E+00
                 TYPE CHANGES: 15.1727,17.8061<ret>


            (The dialog may be repeated if multiple shells of tabular phase
            shifts are specified.  This example prompts for the number of 
            of phase shift pairs (maximum of 20) and accepts the typed
            K,PHASE SHIFT pairs up to the number of pairs specified.)

  
            The dialog for setup CARD 8 is complete.



EF-12

              The normal setup of the cards is now complete.  The user may

            specify a card number which has already been set up in order

            to check his work or make further changes.  After the user is

            satified that all of the setup cards are complete then CARD 0 is 

            specified. CARD 0 terminates the setup input and passes control

            to input the reference files and print or store the setup.  If an

            I/O error occurs while attempting to read in the reference file
    
            then the error is usually terminal to EXAFIT program.  The setup

            file is usually recovered, prior to the halt, in setup file 

            number 6 (SAVE FILE FOR ABNORMAL TERMINATIONS).




EF-13


OUTPUT:       The disk and printer output follow the input of the reference

            files.   If the storage of the setup file was specified in CARD 1,

            then the output of the current setup file to disk is automatially

            assumed.  If disk storage was not specified in CARD 1, then the

            the user is queried again to confirm that he does not want to save

            the setup.  This double check is used to protect the user from

            losing the setup after spending a large amount of time to setup a

            fit.

                 AFTER ALL YOUR WORK TO SETUP THIS FIT,
                 DO YOU WANT TO SAVE THE CARD SETUP PARAMETERS?

            (The response of N<ret> passes control to the setup printout)

                 Y<ret>

                 ****

                 DO YOU WANT TO LOOK AT A TABLE OF SETUP DATA FILES?

                 Y<ret>

                 TABLE OF CURRENT SETUP FILES ON DEFAULT DISK

                 SETUP FILE 1       CUFOIL.B01
                 SETUP FILE 2       FEFOIL.B02
                 SETUP FILE 3       < UNUSED >
                 SETUP FILE 4       < UNUSED >
                 SETUP FILE 5       < UNUSED >
                 SAVE SETUP FILE FOR ABNORMAL TERMINATIONS:
                 SETUP FILE 6
                 TYPE NUMBER OF SETUP FILE FOR STORAGE

                 3<ret>

            (In this example the setup file is stored in a previously
            unused setup file location and is now available for later recall.)

            ****


              The second output at this stage is the printout of the setup

            map, if specified in CARD 1.  The setup map contains all of the

            current setup specifications. 


EF-14

            Sample map:




                                           ***** EXAFIT PROGRAM FOR RT-11 *****                                          28-MAY-81

INPUT CARD PARAMETERS FROM SETUP

CARD 1      :MEMBER TO FIT
CUFOIL.B01    1   10   10    5 1.000E-01 1.000E-02 1.000E+00 0.000E+00    0  FFT

CARD 2      :RANGE OF FIT  KMIN,KMAX
 3.700E+00 15.500E+00

CARD 3      :PARAMETERS BEING VARIED (T=TRUE,YES   F=FALSE,NO)
/  NUMBER /  A      /   R     / SIGMA   /   B     /   C     /   P0    /   P1    /    P2    /   P3    /   G     /   H     /  E0
FFFFFFFFFFFFFFFFFFFFTFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFT

CARD 4      :VALUES OF THE FIT PARAMETERS
N     1.200000E+00
A     1.000000E+00
R     2.556000E+00
SI    0.000000E-00
B     1.000000E+00
C     1.000000E+00
P0    1.000000E+00
P1    1.000000E+00
P2    1.000000E+00
P3    1.000000E+00
G     0.000000E-00
H     1.000000E+03
E0    5.000000E+00

CARD 5       :ENVELOPE MEMBER INPUT FROM DISK
    1    25 CUFOIL.B01  5.440E-01 0.000E-00

CARD 6       :TESTCASE MEMBER

CARD 7       :ENVELOPE PAIRS ENTERED FROM TERMINAL

CARD 8       :PHASE PAIRS ENTERED FROM TERMINAL
SHELL    1     NO. OF PHASE PAIRS   17

  3.7795E+00  2.4272E+01    ...
         .
         .
         .



            This completes the printout of the setup map.  The iterating stage

            begins.


EF-15

ITERATING:    In the EXAFIT program, the iterating begins with the 0th

            iteration using the initial unrefined estimates.  The iterating

            continues for the maximum number times specified in CARD1 or until

            a converged solution or diverging solution occurs.   At the 0th

            iteration, the initial guess parameters are displayed on the

            printer:




EXAFIT PROGRAM TO FIT ANALYTICAL MODEL FUNCTION TO CUFOIL.B01 EXAFS DATA

NOMINAL PARAMETERS                              SHELL  1                         EDGE ENERGY SHIFT (5.00000E+00)

SHELL  N       A       R      SIGMA**2      B         C          P0         P1       P2         P3         G         H
 1  12.00    1.0000  (2.5560)  0.00000    1.0000    1.0000     1.0000     1.0000   1.0000      1.0000    0.000    1000.000

** PARENTHESES INDICATE ESTIMATED VALUES TO BE REFINED BY THIS PROGRAM **

** IMPROVED VALUES ARE TABULATED BELOW **



            The refined parameter values are displayed on the printer as well

            as the standard deviation of fit after each iteration:



THE BEST RESULTS FOR THIS ITERATION ARE:
                                                                                 THE EDGE SHIFT IS :   (5.26000E+00)       
SHELL  N       A        R      SIGMA**2      B         C         P0         P1       P2         P3         G         H
 1  12.00    1.0000  (2.5473)  0.00000     1.0000    1.0000    1.0000     1.0000   1.0000      1.0000     0.000   1000.000
THE STANDARD DEVIATION OF THIS FIT IS :  1.3395E-02


EF-16

            An additional line is printed for an iteration in which the para-

            meters varied by less than the percent specified in CARD 1.  The

            iterating is then terminated :



AT THIS ITERATION, ALL PARAMETERS CHANGED BY LESS THAN THE DESIRED PERCENTAGE (  0.0100%)



             For an iteration in which a diverging standard deviation occurs,

             a single statement is printed signalling a termination to the

             fitting :


DIVERGING SOLUTION



             At the end of the fitting process a prompt message occurs on the

             terminal screen below the final plot.


ANOTHER FIT? (Y/N) 

             A response of 'Y' returns to the beginning of the EXAFIT program.

             This is useful if more iterations are desired.  If a new setup

             file is not read in then the values of the parameters from the

             last iteration are stored in the cards.

             A response of 'N' ends the EXAFIT program.  



EF-17

PLOTTING:      The plotting in the EXAFIT program occurs after each completed
          
             iteration.  The input data file is displayed with a solid

             line and the model function curve is displayed with a dotted

             line.  Appropriate labels are displayed as well as the iteration

             number, standard deviation and best damping factor.  After each

             iteration a plot is constructed.   The terminal waits for a user

             response.  A response of Y<ret> initiates a hard copy of the plot

             on the graphics terminal, while any other response ignores the

             hard copy and begins the next iteration.  Most terminals have a

             buffer in which to store a number of consective responses allow-

             ing the user to run the fit iterations unattended.


EF-18

NOTES:         This section is for providing helpful hints and comments.

             REMEMBER TO RUN A CARD 1 SETUP BEFORE OTHER CARDS ARE SETUP.

             THE CASEMEMBER NAME IN CARD 5 MUST BE DEFAULTED WITH A (/).
             IF ONLY <ret> IS STRUCK THEN THE CASEMEMBER NAME IS NOT SPECIFIED
             AND A TABULAR AMPLITUDE IN CARD 7 IS ASSUMED.

             GENERALLY, THE CURRENT SETUP IS RETRIEVABLE AFTER AN ABNORMAL
             TERMINATION OF THE EXAFIT PROGRAM.  THE SETUP IS SAVED IN SETUP
             FILE 6 WHEN I/O ERRORS OCCUR DURING INPUT OF THE DATA FILES.

             AN ERROR OCCURS IF NOT ENOUGH ROOM IS LEFT ON THE DEFAULT DEVICE
             TO WRITE THE SETUP FILES.  THE ERROR IS AN I/O END OF FILE ERROR
             WHICH RESULTS IN THE LOSS OF THE SETUP FILE.  THE USER SHOULD BE
             EFFICIENT AND TIDY IN THE USE OF DISK SPACE WITH THIS PROGRAM.

             ALL INPUT FILES SPECIFIED IN THE SETUP CARDS MUST BE ON THE
             DISK AT THE TIME THE CARDS ARE SETUP.



EF-19

                    INDEX OF EXAFIT DOCUMENTATION

                                                                Pages

Introduction                     ..............................  1,2
Operation                        ..............................  2
Hardware                         ..............................  2
Setup                            ..............................  3
Execution                        ..............................  3,4
Cards                            ..............................  5-12
       Card 1 dialog             ..............................  5,6,7
       Card 2 dialog             ..............................  8
       Card 3 dialog             ..............................  8
       Card 4 dialog             ..............................  9
       Card 5 dialog             ..............................  10
       Card 6 dialog             ..............................  10
       Card 7 dialog             ..............................  11
       Card 8 dialog             ..............................  11
       Card 0 cards complete     ..............................  12
Output of setup cards to disk    ..............................  13
Setup map                        ..............................  14
Iterating                        ..............................  15,16
Plotting                         ..............................  17
Notes and comments               ..............................  18
Index                            ..............................  19



PH-1

******************************************************************************
************ DOCUMENTATION FOR EXAFS PHASE TABLE PROGRAM *********************
******************************************************************************
                       REVISED  11-Nov-82



INTRODUCTION: The PHASE TABLE PROGRAM will allow you to create,inspect, and

            alter entries in two types of EXAFS phase function tables which

            are used as input for phase fitting (PF) and phase removing (PH)

            options in the EXAPLT PROGRAM.


TABLES:       The three types of phase tables are (1) tabular phase tables

            (named TEOLEE.PHT after B.K. Teo and P.A. Lee who provided

            tabular phase functions from quantum mechanical calculations)

            with 17 points on the Teo and Lee grid, (2) TEOLEE.MST, the phase

	    table with 20 points for multiple scattering modeling, and (2) 

 	    parameterized phase tables (named PARAM.PHF) where

            phase functions are adequately described by the functional form

            Phi(k) = A0 + A1*k + A2*k**2 + A3/k**3 .  For the parameterized

            tables, the coefficients A0,A1,A2,A3 are stored and a parameter

            E0 which alters the k(wave vector) scale k'= sqrt(k**2-.262467E0).

            E0 is identified as the 'inner potential' in the EXAFS literature.


SIZE:         Presently the table TEOLEE.PHT, TEOLEE.MST provides for 300 sets

	    of tabular entries and the table PARAM.PHF provides for 100 sets

  	    of function entries.  Each tabular or functional set is accessed 

	    by name.  The identifying name is provided by you at the time of 

	    entry but can subsequently be changed along with the numerical 

	    values whenever desired.


PH-2

OPERATION:    The PHASE PROGRAM should be run from the default I/O device. All

	    three phase tables should also be maintained on the same default

            device and if created will automatically exist on the default de-

            device.  NOTE OF PRECAUTION:  BACKUP COPIES OF THE CURRENT PHASE

            TABLES SHOULD ALWAYS BE MAINTAINED ON ANOTHER DEVICE. The first 

	    question in the program allows you to select the single (17 points

	    grid) or the multiple scattering (20 points grid) tables. When the

            prompt symbol >> occurs on the screen or teletype the phase pro-

            gram is waiting for your instructions. A list of valid instuc-

            tions (two-letter keywords) is given below with a short descrip-

            tion for each option.  A more detailed description of each option

            is given further on. All the described commands for the table 

	    TEOLEE.PHT have the same effect on TEOLEE.MST, when multiple

	    scattering formalism is selected.


OPTIONS:      A list of two-letter responses to the phase program prompt >> :

                    EX --- Exit from the Phase Program

                    DT --- Directory of Tabular entries in TEOLEE.PHT 

                    DF --- Directory of Function entries in PARAM.PHF

                    NT --- New Tabular Phase Table is created

                    NF --- New Function Phase Table is created

                    CT --- Check and/or Change existing Tabular Entry

                    CF --- Check and/or Change existing Function Entry

                    ET --- New Tabular Entry to TEOLEE.PHT 

                    EF --- New Function Entry to PARAM.PHF

                    PT --- Printout Directory of Tabular Entries

                    PF --- Printout Directory of Function Entries


PH-3

DESCRIPTIONS: Detailed description of program operation by option:

            >>

            EX<ret>

                    The EX option closes all immediate options and exits

                  from the phase table program leaving the phase tables at 

                  their current status.

            >>

            DT<ret>

                    The DT option displays the directory of the tabular 

                  phase table TEOLEE.PHT by entry name.  The name conven-

                  tions for this table allow one or two letter symbols for

                  identification of each entry. Ideally the periodic element

                  symbol should be used to identify both the absorbing atom

                  and backscattering atom entries to the phase table. A third

                  numerical character is used to identify the final state

                  quantum number associated with the central atom element and 

                  is treated in the directory listing as part of the name

                  (either 0,1,or 2 is an appropriate entry for indentifying

                  the central atom final state). If a blank or carriage return

                  is typed in for the third character then the table entry

                  will always be assumed to be a backscattering element. An

                  error message is displayed if the tables are missing from

                  the default device.

                  ERROR - PHASE TABLE NOT FOUND ON DISK

                  An error message is displayed if any (xT) options are chosen

                  before the DT option.  You must get a directory before pro-

                  ceding on to other options.

                  ERROR - YOU HAD BETTER GET A PHASE TABLE DIRECTORY FIRST ! 


PH-4
            >>

            DF<ret>

                    The DF option displays the directory of the phase function

                  entries in PARAM.PHF by entry name. The naming convention

                  in this table allows the flexibility of up to 10 characters

                  typically expressed in a form such as   XXXX-XXXX .  An 

                  example would be    CU1-CU  for a copper absorber, copper

                  scatterer phase shift.  The 1, which denotes the final state

                  of the backscattered electrons, is optional to enter in this

                  table. An error message is displayed if the function table 

                  is not on the default device.

                  ERROR - PARAMETERIZED PHASE FUNCTION TABLE NOT ON DISK

            >>

            NT<ret>

                    The NT option creates a new tabular phase table on the

                  default device, providing for over 300 entry locations. If

                  the tabular phase table TEOLEE.PHT already exists on the 

                  default device then the NT option will not supercede the old

                  one unless the old one is renamed or removed from the de-

                  fault device.  An error message is displayed if this con-

                  dition occurs.

                  ERROR - THEORETICAL PHASE TABLE ALREADY ON DEFAULT DISK

            >>

            NF<ret>

                    The NF option is exactly indentical to the above NT

                  option for the parameterized function table PARAM.PHF.

                  The new function table provides for 100 entry locations.

                  The error messsage displayed when this option is executed

                  and the function table already resides on the default device

                  is:

                  ERROR - FUNCTION TABLE ALREADY ON DEFAULT DISK


PH-5
            >>

            ET<ret>

                    The ET option allows the creation of a new tabular phase

                  entry.  Here is a sample dialog:

                  SPECIFY 1 OR 2 LETTER ELEMENT SYMBOL:   CU<ret>

                  IF ABSORBER,TYPE FINAL STATE QUANTUM NO. L ,
                  
                  OTHERWISE <RETURN> :   1<ret>

                  (L=0,1,2 are acceptable options, or just return assumes 

                  a backscattering phase table entry.)

                  ENTER THEORETICAL PHASE VALUES AS PROMPTED

                  TABLE VALUE 1 :   4.2345<ret>

                  TABLE VALUE 2 :   5.3469<ret>

                  . . .

                  TABLE VALUE 17:   4.3513<ret>

                  >>

                  Be sure to check for proper entry by listing a directory DT.

            >>

            EF<ret>

                    The EF option allows creation of a new parameterized phase

                  entry.  Sample dialog:

                  SPECIFY FUNCTION TITLE     XXXX-XXXX  :  CU1-CU<ret>

                  TYPE  A0,A1,A2,A3,E0   SEPARATED BY COMMAS

                  2.929,-1.1586,.0245,-84.41,0.<ret>

                  >>

                  Be sure to check your entry with a DF directory listing.


PH-6
            >>

            CT<ret>

                    The CT option will check or change tabular phase entries.

                  Sample dialog:

                  SPECIFY ELEMENT SYMBOL FOR THE SCREEN CHECK :  CU<ret>

                  IF ABSORBER, TYPE FINAL STATE QUANTUM NO. L ,

                  OTHERWISE <RETURN> :  2<ret>

                  CU2    xx.xxxx xx.xxxx xx.xxxx xx.xxxx xx.xxxx xx.xxxx

                         xx.xxxx xx.xxxx xx.xxxx xx.xxxx xx.xxxx xx.xxxx

                         xx.xxxx xx.xxxx xx.xxxx xx.xxxx xx.xxxx

                  (If the entry name you specify is not found in the table

                  directory then an error message is displayed.

                  ERROR - CU2   NOT FOUND IN THE PHASE TABLES)

                  OK ?  N<ret>       (a response of yes assumes a satisfactory

                  screen check and >> is returned)

                  TYPE APPROPRIATE CHANGES AS PROMPTED

                  SPECIFY 1 OR 2 LETTER ELEMENT SYMBOL:  CU<ret>

                  IF ABSORBER, TYPE FINAL STATE QUANTUM NO. L ,

                  OTHERWISE <RETURN> :  1<ret>

                  DEFAULT IS COMMA OR SLASH, THEN <RETURN>

                  TABLE VALUE 1 :  /<ret>

                  . . .

                  TABLE VALUE 17:  4.1586<ret>

                  CU1    xx.xxxx xx.xxxx xx.xxxx xx.xxxx xx.xxxx xx.xxxx

                         xx.xxxx xx.xxxx xx.xxxx xx.xxxx xx.xxxx xx.xxxx

                         xx.xxxx xx.xxxx xx.xxxx xx.xxxx  4.1586

                  This example altered the quantum number from 2 to 1 and 

                  changed the 17th value of the entry

                  OK ?  Y<ret>

                  >>


PH-7
            >>

            CF<ret>

                    The CF option will check or change phase function entries.

                  Sample dialog:

                  SPECIFY NAME OF FUNCTION FOR SCREEN CHECK :   CU2-CU<ret>

                  CU2-CU  xxxx.xxxx,xxxx.xxxx,xxxx.xxxx,xxxx.xxxx,xxxx.xxxx

                  (if the entry is not found in the table then an error 

                  message is displayed

                  ERROR - CU2-CU      NOT FOUND IN FUNCTION TABLE

                  OK ?  N<ret>

                  TYPE NAME CHANGE , DEFAULT IS <RETURN> :  CU1-CU<ret>

                  ENTER PARAMETER CHANGES WITH PROPER SEPARATING COMMAS

                  DEFAULT IS NOTHING BETWEEN COMMAS

                  ,,,-85.51,

                  CU1-CU    xxxx.xxxx xxxx.xxxx xxxx.xxxx  -85.51   xxxx.xxxx

                  (this example changed the name and the fourth parameter 

                  value of this entry)

                  OK ?  Y<ret>

                  >>

            >>

            PT<ret>

                    The PT option repeats precisely the DT option but outputs

                  the directory to the printer.

            >>

            PF<ret>
 
                    The PF option repaets precisely the DF option but outputs

                  the directory to the printer.


PH-8

NOTES:        This section is for providing helpful hints and comments.


            AVOID USING THE SAME NAME FOR TWO ENTRIES. IF THIS HAPPENS, IT IS

            ADVISABLE TO RENAME ONE, OTHERWISE THE FIRST ENTRY WILL ALWAYS BE

            USED.


            ENTRIES CAN'T BE DELETED, BUT OUTDATED ENTRIES CAN BE RENAMED OR

            CHANGED IN THE (Cx) OPTIONS. A CONVENIENT WAY TO KEEP TRACK IS TO

            RENAME ALL OUTDATED ENTRIES {UNUSED} (THIS MEANS SIMPLY TYPING

            'UN'   FOR THE NAME OF A TABULAR ENTRY OR   '<UNUSED>' FOR THE

            NAME OF A FUNCTION ENTRY FOR FUNCTIONS) AND ZERO THE VALUES.  

            THESE UNUSED ENTRIES WILL BECOME AVAILABLE FOR LATER USE ON A

            FIRST-COME-FIRST-SERVE BY USING THE (Cx) OPTION AGAIN.


            USE OF THE PHASE TABLES FOR STORAGE OF TABULAR OR FUNCTION

            AMPLITUDES IS ALSO SUGGESTED.  PROCEED AS IF THESE ENTRIES ARE

            PHASE ENTRIES, BUT BE CAREFUL OF NAMING CONVENTIONS WHICH INTER-

            FERE WITH PHASE ENTRY NAMES.


            REMEMBER TO FREQUENTLY UPDATE THE BACKUP PHASE TABLES WHICH SHOULD

            BE MAINTAINED ON ANOTHER DEVICE.



PH-9

                             INDEX FOR PHASE DOCUMENTATION

                                                                   Pages

Introduction                     ..................................  1
Tables                           ..................................  1
Size                             ..................................  1
Operation                        ..................................  2
Options                          ..................................  2
Description of options

CF   Check/Change function entry ..................................  6  
CT   Check/Change tabular entry  ..................................  7
DF   Directory of function table ..................................  4
DT   Directory of tabular table  ..................................  3
EF   New function entry          ..................................  5
ET   New tabular entry           ..................................  5
EX   Exit                        ..................................  3
NF   Create new function table   ..................................  4
NT   Create new tabular table    ..................................  4
PF   Print function directory    ..................................  7
PT   Print tabular directory     ..................................  7

Notes and comments               ..................................  8
Index                            ..................................  9





CN-1
*************************************************************************
**********  DOCUMENTATION FOR THE CONHLD PROGRAM UTILITY  ***************
*************************************************************************
                       REVISED 9-FEB-83


INTRODUCTION:  The CONHLD program is a utility program for creating the

             CONST.HLD map file.  The program only needs to be executed

             once unless the CONST.HLD file is lost or destroyed.  The

             newly created file is empty and will build as needed in

             the EXAPLT program.  The CONST.HLD file holds or retains

             important constants, coefficients, range parameters, and 

             other relevent information which maps the analysis carried

             out in EXAPLT.  This information is stored by EXAPLT invisibly

             and can be displayed only by options in EXAPLT or by printing

             the header of special format files written in EXAPLT.



INSTRUCTIONS:  Store CONHLD utility and source on auxiliary device until

             needed.  To execute, simply type RUN Dev:CONHLD.  The result

             is the creation of an empty CONST.HLD file on the system 

             device.  The file CONST.HLD should be maintained on the system

             device for access by EXAPLT.  The CONST.HLD is a Random Access

             Unformatted Binary File, therefore do not try to read, list

             or print the contents of the file directly.  


MC-1
**************************************************************************
*************  DOCUMENTATION FOR THE MCMAST PROGRAM UTILITY  *************
**************************************************************************
                           REVISED 9-FEB-83


INTRODUCTION:  The MCMAST program is a utility program for creating the

             McMaster coefficient table MCMSTR.TBL.  The program only needs

             to be executed once unless the MCMSTR.TBL file is lost or

             destroyed.  The newly created file is empty and can be filled

             as needed in the EXAPLT program.  The MCMSTR.TBL file stores

             the x-ray cross section coefficients used in the background

             normalization in EXAPLT.  The coefficients can be entered

             and changed only through dialogue in the EXAPLT program.



INSTRUCTIONS:  Store MCMAST utility and source on auxiliary device until

             needed.  To execute, simply type RUN Dev:MCMAST.  The result

             is the creation of an empty MCMSTR.TBL table file on the system 

             device.  The file MCMSTR.TBL should be maintained on the system

             device for access by EXAPLT.  The MCMSTR.TBL is a Random Access

             Unformatted Binary File, therefore do not try to read, list

             or print the contents of the file directly.  


CU-1
*****************************************************************************
******* DOCUMENTATION FOR THE CURSRT GRAPHIC INPUT MODE TEST PROGRAM ********
*****************************************************************************
                        REVISED 9-FEB-83


INTRODUCTION:  CURSRT is a program to test the graphic crosshair input

             mode and graphic output in the PLOT10 Terminal Control System.

             The graphic hardware required is at least a Tek 4010-1 Storage

             Tube or comparable  emulation.



INSTRUCTIONS:  The CURSRT program should page (clear) the graphic screen,

             draw a centered square frame, and present the graphic curser

             (cross hairs).  The following list of options exercise the

             graphic input and output.  The cross hairs should be located

             at a desired point within the framed window before giving a

             keyboard response.  The beginning origin is the located at the

             lower left hand corner of the window.




OPTIONS:       The curser will await any keyboard response, but will only

             perform action on certain keystrokes: 


             P<ret>  (point)-Draws a point at the curser location and
                     relocates origin at new curser position.

             M<ret>  (move)-Moves origin to new curser position; nothing
                     drawn.

             D<ret>  (draw)-Draws a solid vector from origin to new curser
                     location and relocates origin at new position.

             -<ret>  (dash)-Draws a dashed vector from origin to new curser
                     location and relocates origin at new position.

             N<ret>  (new)-Clears graphic screen and draws new frame.


             S<ret>   (stop)-Exits to monitor.


             If this test is satisfactory, then the EXAFS programs using the

             the graphic input mode should execute properly.