DOCUMENTATION FOR PROGRAM CMPR

 Program CMPR is used to perform operations that compare
 diffractograms: operations such as plotting, addition/subtraction and
 simulation of patterns from JCPDS data.

===> COMMAND  ADD
  Used to add two files. The file numbers can be entered on
  the command line or can prompted. File numbers may be separated by
  either spaces or commas (or both).
     ADD 2 4    is equivalent to
     ADD 2,4
---  Qualifiers
/TITLE="file_title"
  This option is used to specify a title line for the the new file
/SCALE=scale_factor
  The intensities in second file will be multiplied by scale_factor.
  The scale_factor need not be an integer, but should be greater than
  zero.
/OFFSET=offset_val
  A fixed offset can be added (offset_val greater than zero) or
  subtracted (offset_val less than zero) to the resultant
  diffractogram after the two files are added. offset_val will
  be added to each point; offset_val may be a floating point number.

  If /MINIMUM is used with /OFFSET, the offset, offset_val,
  is added after subtracting the minimum intensity from all points,
  thus if the command SUB/MIN/OFF=100  is used, the lowest
  intensity point in the pattern will have an intensity of 100.
/MINIMUM
  Subtracts the intensity of the least intense point from all points
  in the diffractogram.
===> COMMAND  ATTRIBUTES
  This command is used to set the plot attributes which define how a
  diffractogram is plotted. The files to be affected may be included on
  the command line or may be input with a prompt. If more than one file
  is specified, the attributes for all specified files will be set to
  the same values.
---  Qualifiers
/COLOR=color
 Sets the color for the plot. The number of colors available is
 determined by the graphics device (see the PGPLOT documentation). Color 0
 corresponds to the background (producing an invisible plot).
 Numbers less than 0 or greater than 255 should not be used.
/WIDTH=width
 The line width to be used for plotting the diffractogram and/or the peak
 positions. A width of 1 is the usual default, but thicker lines may be
 specified by using larger numbers. Numbers less than 1 should not be used.
/LINE=line_type
 Determines the type of line used for plotting the diffractogram intensity
 versus angle data. line_type of 1 produces a single connecting line.
 /LINE=2 through /LINE=5 produce dashed, dot-dashed, dotted and
 dot-dot-dashed lines, respectively. /LINE=6 puts dots at each
 data point (this is not exactly the same as a dotted line.) A line type
 of 0 indicates that the diffractogram data is not to be plotted.
 Numbers less than 0 or greater than 6 should not be used.
/PEAK=peak_type
 Determines the type of line used for plotting the peak position data.
 Ignored for files that do not have peaks. A peak_type of 1 produces a
 single straight line for each peak.  Types of 2 through 5 produce
 dashed, dot-dashed, dotted and dot-dot-dashed lines, respectively.
 A peak type of 0 indicates that the peaks are not to be plotted.
 If 8 is added to the peak type, the intensity is considered arbitrary
 and will be plotted full scale.
 Numbers less than 0 or greater than 14 should not be used.
/OFFSET=off_value
Specifies an offset to be added to the data when the data is plotted.
The value is a floating point number which may be positive or negative.
/MAGNIFICATION=mag_value
Specifies a magnification factor for the data for plotting.
The value is a floating point number which may be greater than or less than
one.
/ALL
 Sets the specified attributes for all files.
---  Examples
  ATT 1 2 3
			Sets the attributes for files 1, 2 and 3. The
			values for the attributes will be requested
			using prompted input.
  ATT
 			As before except the file numbers will also be
			prompted for.
  ATTR/COLOR=2  4,3
			Resets the color for files 3 and 4 to color
			type #2 (actual color is device dependant,
			usually red).
  ATTR/ALL/C=1
			Resets the color for all files the default color.
===> COMMAND  COMBINE
  Used to combine two or more files into one file.  The file numbers can
  be entered on the command line or can be prompted.  File numbers may be
  separated by spaces or commas or both.

  Command format: COMBINE [file_list]
---  Parameter
file_list
 File numbers may be specified on the command line separated by
 commas or spaces.

 If no files are placed on the command line, a prompt will be
 generated for file numbers.
===> COMMAND  DCL
 Spawns a subprocess to execute DCL commands, type LOGOUT to
 return back to CMPR without affecting the current list of files.
 This command is useful for quick DCL "errands" such as answering
 a mail message without exiting the program.
===> COMMAND  DEFAULT
  This program can operate in two modes, AUTO mode and MANUAL mode. In
  AUTO mode, default values are used where possible to cut down on the
  amount of questions the need to answered. In MANUAL mode, if a
  parameter is not specified on the command line, a prompt will be
  generated for an option or value. The current mode is listed on the
  top of the screen.

  Command qualifiers always override default options. For example,
  in AUTO mode command WRITE/NBS produces a file in NBS format,
  while WRITE defaults to /BINARY. In MANUAL mode, the latter
  command would generate a prompt requesting a choice for file format.

  The mode can be toggled by entering the DEFAULT command without any
  qualifiers. Alternately, a qualifier may be used:
    DEF/MAN  	(sets the mode to MANUAL)
    DEFAULT/A	(sets the mode to AUTO)
    DEF      	(sets the mode to the opposite of the current mode)
---  Qualifiers
/AUTO
/NOMANUAL
		If either of these qualifiers are used, the mode is set
		to AUTO. Thus, default values will be used for options
		(where possible) to reduce the number of prompts.
		(/NOMANUAL is equivalent to /AUTO)
/MANUAL
/NOAUTO
		If either of these qualifiers are used, the mode is set
		to MANUAL. Thus, the program will prompt rather than
		using default option(s).
		(/MANUAL is equivalent to /NOAUTO)
===> COMMAND  DELETE
  Used to remove a "file" from the list of available files. This will not
  delete the file from disk storage (unless it was created in CMPR and
  never actually written on disk). Only one file can be removed at a
  time and file number 1 can only be removed with the the DELETE/ALL 
  command -- which removes all files (equivalent to starting a new CMPR
  run).

  usage:
          DELETE [file_number]    or
          DEL/ALL
---  Parameter
file_number
 The number of a single file to be removed may be specified on the
 command line. If the file number is not specified a prompt will be
 given requesting a file number. The file number must be in the range of
 2 to 10. No file number may be specified if /ALL is used.
---  Qualifier
/ALL
  Removes all files (equivalent to starting a new session). When
  running interactively, a prompt will be generated for new file names
  to read. No file numbers can be specified if /ALL is specified.
===> COMMAND  DGEN
  Computes the allowed d-spaces for a given unit cell optionally omitting 
  reflections extinct by translation symmetry. Must be run interactively.
---  Qualifier
/A=a_length
/B=b_length
/C=c_length
/ALPHA=bc_angle
/BETA=ac_angle
/GAMMA=ab_angle
Defines the unit cell lengths in Angstroms and the angles in degrees
for the d-space generation. 
If a_length is not specified, values for the cell Laue symmetry and
then all appropriate unit cell parameters will be requested.
If b_length and/or c_length are not specified, they default to 
a_length. Any angles that are not specified default to 90 degrees.
===> COMMAND  EXIT
 Type EXIT (which can be abbreviated to E) to exit; alternately
 press Control Z (^Z) to exit the program. After exiting, you will 
 be prompted to write any files that have been modified or created
 within the program.
===> COMMAND  FILE
 Allows a series of commands to be input to the program from an external
 file. The file should be prepared before starting the program, or using
 the DCL command to invoke an editor. 
---  Parameter
file_name
 A single file may be specified on the command line containing the name
 of the file with commands. If the file is not specified, a prompt will be
 given to request a file name. 

 If no file extension is supplied, the default extension is .CMD
===> COMMAND  HKLPLOT
  Used to label hkl values and show which peaks would be expected to 
become extinct for a give set of symmetry elements.

  A symmetry operation is supplied to the program and reflections
from the file are displayed in one of three colors (or line styles
if the graphics device is incapable of displaying color graphics). 
The basic color is used for peaks that would not be extinct, the second
color is used for peaks that would be extinct. A third color is used 
for peaks that would be overlapped.

  If raw data is in the diffractogram file, that data is also displayed.
If two file numbers are given, the data from the second file is displayed.

  If the interactive graphics device has a graphics cursor, the cursor can
be used to selectively label the indices of selected reflections.
---  Qualifier
/WIDTH=P_width
  The value of P_width dictates the width where it is expected to 
be impossible to discern two overlapped reflections. This should normally 
be in the range of one and a half to one quarter of the expected peak FWHM.
/XLOW=low_limit
/XHIGH=high_limit
  Defines the plot limits for the x-axis. If either is specified,
  the values for plotting limits will not be prompted. Values may be
  integers or floating point numbers, but must be included if the
  qualifier is specified. The units are degrees two-theta.
/DATASCALE=data_scale
/PEAKSCALE=peak_scale
  Defines the plot limits for the y-axis. A value of 1.0 means data/peaks
  are plotted so that the maximum value is full scale, 2.0 means a
  magnification factor of x2. 

  A value of 0.0 for peak_scale means that all peaks will be plotted
  to full scale.
===> COMMAND  LOGIC
 Use this command to invoke the LOGIC program to search the JCPDS database
 (without exiting CMPR.)  After exiting from LOGIC, CMPR will be resumed
 with all current files still loaded and all current parameters unchanged.
===> COMMAND  MANIP
 Use this command to invoke the MANIP program without exiting CMPR.
 When exiting from MANIP, the computer will return to CMPR with all
 CMPR files still loaded in memory. It is possible to pass a file
 from CMPR's list of current files to MANIP and/or pass one or more
 files from MANIP back to CMPR.
---  Parameter
file_number
 The number of a single file may be specified on the command line
 referencing the number of the file to be passed to MANIP. If the file
 number is not specified a prompt will be given requesting a file number.
 Files must be written on disk in order to be passed. If the file has
 been modified and does not exist in the current form on disk,
 confirmation will be requested before the file is written.
===> COMMAND  PLOT
Used to produce a plot on either a terminal or on a hard copy device.
Several options are available to determine the format of the plot. 

Note that the x-axes for all files to be plotted must all be of the
same type (have the same units) except that if /Q is specified. In
that case files in two-theta units may be mixed with files in Q units.

Command format: PLOT [/qualifiers] [file_list]
---  Parameter
file_list
 File numbers may be specified on the command line separated by
 commas or spaces:
        PLOT 1,2,3
        PLOT 1 2 3
        PLOT 1 2,3
 all of the above are equivalent and valid.

 If no files are placed on the command line, a prompt will be
 generated for file numbers.
---  Qualifiers
/XLOW=low_limit
/XHIGH=high_limit
  Defines the plot limits for the x-axis. If either is specified,
  the values for plotting limits will not be prompted. Values may be
  integers or floating point numbers, but must be included if the
  qualifier is specified. The units are degrees two-theta, unless the
  the /Q or /DSPACE option is used.
/Q
 Graph will be plotted in Q units (in reciprocal Angstrom) rather than
 the x-axis units (typically two-theta).
 This parameter is not prompted; plots will be produced in the file x-axis
 units, unless /Q, /DSPACE, or /WAVELENGTH is placed on the 
 command line.
/DSPACE
 Graph will be plotted in D-space units (in Angstrom) rather than
 the x-axis units (typically two-theta).
 This parameter is not prompted; plots will be produced in the file x-axis
 units, unless /Q, /DSPACE, or /WAVELENGTH is placed on the 
 command line.
/WAVELENGTH=wavel
  Graph will be plotted in two-theta units at wavelength wavelAngstrom.
 This parameter is not prompted; plots will be produced in the file x-axis
 units, unless /Q, /DSPACE, or /WAVELENGTH is placed on the 
 command line.
/XSTACK=x_spacing
/XSTACK
 Causes plots to be "stacked" -- drawn on a single set of axes.
 x_spacing is the horizontal distance in percent of the full scale
 between the zero values in successive plots. 
/YSTACK=y_spacing
/YSTACK
 Causes plots to be "stacked" -- drawn on a single set of axes.
 Y_spacing is the vertical distance in percent of full scale
 between the zero values in successive plots. 
/NOSTACK
 Causes each plot to be put in a separate box.
/RELATIVE
/FIRST
  There are two scaling options: They are only applicable if more
  than one file is to be plotted:

 /FIRST    
    The maximum intensity for the vertical axis is set from the first 
    file to be plotted.

 /RELATIVE    
    The vertical axis is set to the maximum point in each plot. 
    If the plot is "stacked" (see /XSTACK or /YSTACK) the full
    scale be increased, if needed to include all files.

  Only one of /YHIGH, /FIRST and /RELATIVE can be used.
/YLOW=low_limit
/YHIGH=high_limit
  Defines plot limits for the y-axis. low_limit and high_limit are
  the minimum and maximum number of counts that can fit on the plot
  axes. (These numbers need not be integers and are not prompted.)
  If /YLOW is not specified, low_limit will be 0.
  If /YHIGH is not specified, high_limit will depend on options
  for /XSTACK or /YSTACK. 

  Cannot be used with /FIRST or /RELATIVE.
/SIZE=(X_len,Y_len,X_mar,Y_mar)
/SIZE=(X_len,Y_len)
/SIZE
  Used to specify the size of the plot in inches. X_len and Y_len
  are the lengths of the x- and y-axes, respectively.
  Y_mar and X_mar are the margins below and to the left of the
  axes. (The default margins are 1 inch.) These numbers may be
  floating point numbers.

 The command can be used two ways, if /SIZE is used without any
 values, CMPR will prompt for values. If values are specified
 on the command line, both X_len and Y_len must be specified.
 X_mar and Y_mar are optional, but X_mar must be specified
 before Y_mar.

 It is the user's responsibility to insure that the requested size
 is compatible with the graphics device. 
/TITLE
/NOTITLE
  Plot(s) will be labeled with the TITLE for (each) file.
/FILE
/NOFILE
  Controls if file names will be shown for each plot in the upper
  right corner. 
/CLIP
  Segments of the plot that lie outside the plot axes may "squared off"
  (clipped) at the axis limit (/CLIP) or may be simply omitted (/NOCLIP).
/LINEAR
/LOG
/SQRT
  The intensity scale can plotted proportional to the number of
  counts (/LINEAR), logarithmic units (/LOG) or proportional to 
  the square-root of the number of counts (/SQRT). 
  Plots will be made in /LINEAR mode, unless /LOG or /SQRT is
  specified.
/GRID
  Grid hash marks will be drawn if /GRID is specified.
  Default is /NOGRID (Not prompted).
/HARD
 If /HARD is specified, graphics will be sent
 to the default hardcopy device, rather than displayed the terminal.
===> COMMAND  QUIT
 Type QUIT (which can be abbreviated to Q) to quit the program. Unlike
 the exit command, you will not be prompted to write any files that have 
 been modified or created within the program.
===> COMMAND  READ
  Used to read one or more new files into the list of available file
  names. (Assuming there is still space in the list for additional files.
  If not, first use the DELETE command to make room.)

  usage:
        READ [filename1] [,filename2] [,filename3],...


---  Parameter
file_name
file_name_1, file_name_2,... file_name_8
 Files may be specified on the command line. If no files are specified,
 a prompt will be given requesting a file name to read.

 file_name may be VMS filename or logical name or a JCPDS-ICDD entry 
 number. For interactive input, a question mark (?)may be used to see 
 help information and if a wildcard is used (* or %), a directory
 listing is shown.
 
 If file_name is a VMS filename it can be of form FILE.EXT or 
 DEV:[DIR]FILE.EXTENSION;2 -- subject to a limitation that the 
 file name must not exceed 80 characters.

 It is usually preferable to supply the file name without a file 
 extension, as the default extension will then depend on the file
 format. This improves the speed that the program has available 
 when searching for the file.
 The subroutines which read data and peak files, (subroutines 
 READDATA and READPEAK respectively), will attempt to determine 
 the format of the file from the file contents and the extension.

 More than one file name can be specified on the command line, but 
 names must be separated by commas. If more file names are specified
 than may be read, the extra names will be ignored.

 Filenames may not be specified if the /JCPDS qualifier is used.
---  Qualifier
/FORMAT=fileform
 This optional qualifier may be used to specify the file format that will
 be used for reading the file(s). If more than one file is given and 
 /FORMAT is used, all files must all be in the specified format.

 In most cases it is not necessary to specify the file format, as the 
 program will discern the file format from the file. However, in certain
 cases where problems are encountered, it may be necessary to use the 
 format option.

 File formats may not be specified if the /JCPDS qualifier is used.
/JCPDS=card_list
/JCPDS
 Use this qualifier to select entries using their ICDD-JCPDS entry number.
 The entry number is always a five or six digit number consisting
 of the "old" entry number plus 10,000 times the set number. For
 example, entry 413 in set 7 would be coded as:
---  Examples
 READ group.mother\FORMAT=DUPONT
 READ
 READ/JCPDS=(271402,400001)
 READ group.mom,[.test]exper.fil,somewhere:overthe.rainbow;1
===> COMMAND  SCALE
 Rescales the x and/or y values for a data file.
---  Parameter
file_number
 The number of a single file to be rescaled may be specified on the
 command line. If the file number is not specified a prompt will be
 given requesting a file number.
---  Qualifiers
/YMULT=Y_Factor
/YOFFSET=Y_Offset
  Rescales the y-values in the file from by first adding the offset
  (Y_Offset) and then by multiplying the y-values by the multiplier
  (Y_Factor).

  If not specified, Y_Offset defaults to 0.0 and Y_Factor defaults 
  to 1.0. If neither value is specified, a prompts will be generated 
  for values.
/XMULT=X_Factor
/XOFFSET=X_Offset
  Rescales the x-values in the file from by first adding the offset
  (X_Offset) and then by multiplying the x-values by the multiplier
  (X_Factor).

  If not specified, X_Offset defaults to 0.0 and X_Factor defaults 
  to 1.0. If neither value is specified, a prompts will be generated 
  for values.
===> COMMAND  SIMULATE
 This option is used to construct a simulated diffraction pattern from
 a set of peak positions and intensities. The peak positions may be
 generated by an external program, such as Lazy/Pulverix, read from the 
 JCPDS-ICDD data base, or obtained from an experimental source.

 The peak positions must be loaded into one or more files using the READ
 command. This command may then be used to construct a simulated pattern 
 by convoluting that data. More than one set of peaks may be combined to
 simulate a mixture, in which case weights for each file may be specified.

 If one or more files will be combined, or the file to be convoluted already
 has a corresponding diffraction pattern, a new file will be created. If
 only one file is used and no diffractogram is present for that file, 
 the diffractogram will be added to the same file as the peaks

 The command format is:
     SIM [file_1] [file_2]... [file_8] [/qualifiers]
---  Parameter
file_list
 File numbers may be specified on the command line separated by
 commas or spaces.

 If no files are placed on the command line, a prompt will be
 generated for file numbers.
---  Qualifiers
/RANGE=(x_min,x_max)
/RANGE
  Specifies the two-theta range of the simulated pattern. If only x_min
  is specified, x_max defaults to the largest x value in file #1.
  If both numbers are omitted, both default to the same as file #1. The
  numbers may be specified as floating point.
/WEIGHT=(Wt_2,Wt_1,...Wt_n)
 Specifies the weights for the n files to be convoluted. The default value
 is 100.
/STEP=step_size
/STEP
  Specifies the two-theta step size for the simulated pattern in units of
  degrees. If the value is omitted, the default is the same as the
  step size in file number #1. step_size should always be less than
  1.0 but greater than 0.
/CAUCHY=(p_wid,p_ang)
/CAUCHY
/GAUSSIAN=(p_wid,p_ang)
/GAUSSIAN
 Selects the peak profile as either Lorentzian (Cauchy) or Gaussian
 (not both). If both p_wid and p_ang and are specified, peaks at
 angle p_ang will have a WIDTH of p_wid degrees. If both numbers
 are not specified, the NBS width table will be used. Either number
 may be floating point.
/OFFSET=offset_val
  A fixed integer offset of offset_val counts can be added to the
  simulated pattern. Cannot be used with /AMORPHOUS.
/AMORPHOUS=(a_wid,a_ang,a_int)
   Specifies that a broad peak simulating amorphous scattering
   be added to the simulated pattern. A peak will be placed at
   angle a_ang, with width a_wid and intensity a_int. The default
   values for a_ang, and a_wid are 25 and 30 degrees two-theta
   respectively, for a_int it is 2 percent of full scale. Any of these
   numbers may be floating point values.

  Cannot be used with /OFFSET.
/WAVELENGTH=wave_length
  A single wavelength may be specified, where wave_length is the
  x-ray or neutron wavelength in Angstrom. If wave_length is used,
  /TARGET and /WTYPE should not. (The target_type will be assumed
  to be SY for synchrotron radiation).
/TARGET=target_type
/TARGET
 Specifies an x-ray target for conventional x-ray sources.
 The choices for targets are:
 Cu, Mo, Ni, Co, Fe, Cr, Ag, NU, or SY.
 Specifying /TARGET without a target_type is equivalent to
 /TARGET=CU. (Capitalization of the target type is ignored.)
 If NU or SY (for neutron or synchrotron radiation) is used,
 the program prompts for a wavelength. This option cannot be used if
 a wave_length value is specified using /WAVELENGTH.
/WTYPE=wave_type
   wave_type may be either 1, 2, 3 or 4 which determines
   the exact value used for the wavelength specified with /TARGET.
   The choices are:
  	1 to use K alpha 1 radiation
  	2 to use K alpha 2 radiation
  	3 to use the intensity weighted average of K alpha 1 and K alpha 2\
	  radiation.
  	4 to use both K alpha 1 and K alpha 2 radiation.
   Specifying /WTYPE without a value is equivalent to /WTYPE=4.
   This qualifier is ignored if the radiation source has a single
   wavelength, (e.g. /TARGET=NU or /TARGET=SY) and cannot be used
   if /WAVELENGTH is specified.
/NOISE=sig_level
/NOISE
  Used to add random noise to the simulated diffractogram.
  Noise will be added at a level of sig_level standard deviations.
  sig_level may be floating point and defaults to 2.0
/MAXIMUM=max_count
/MAXIMUM
  This qualifier is used to set the maximum intensity in the pattern
  after scaling to max_count. The value for max_count must be an
  integer, if not specified it defaults to 5000 counts.
---  Examples
 SIMUL
 SIM 7,413
 SIM 7,413,50 7,414,50/CAUCHY/TARGET=MO
===> COMMAND  SUBTRACT
  Used to subtract two files. The file numbers can be entered on
  the command line or can prompted. File numbers may be separated by
  either spaces or commas (or both).
     SUB 2 4    is equivalent to
     SUB 2,4
  (file #4 will be subtracted from file #2)
---  Qualifiers
/TITLE="file_title"
  This option is used to specify a title line for the the new file
/SCALE=scale_factor
  The intensities in second file will be multiplied by scale_factor.
  The scale_factor need not be an integer, but should be greater than
  zero.
/OFFSET=offset_val
  A fixed offset can be added (offset_val greater than zero) or
  subtracted (offset_val less than zero) to the resultant
  diffractogram after the two files are subtracted. offset_val will
  be added to each point; offset_val may be a floating point number.

  If /MINIMUM is used with /OFFSET, the offset, offset_val,
  is added after subtracting the minimum intensity from all points,
  thus if the command SUB/MIN/OFF=100  is used, the lowest
  intensity point in the pattern will have an intensity of 100.
/MINIMUM
  Subtracts the intensity of the least intense point from all points
  in the diffractogram.
/IGNORE
/CLIP
  Action to be taken if negative intensities are present. If /CLIP
  is used, negative intensities are set to zero, if /IGNORE is used,
  they are left unchanged. These options cannot be used if /MINIMUM
  is used (which will prevent negative intensities by shifting the
  pattern up). If /OFFSET and /CLIP are both used, offset_val
  will be added after negative points are clipped to zero.
===> COMMAND  TITLE
 Used to change the title of a file. The format of this command is:
      TITLE [file_number] title
 The title can be specified on the command line only if preceeded by a
 file number, but neither must be specified. At this time, any lower case
 letters used in the title will be converted to uppercase.
---  Examples
TITLE 1 This is the new title for file number 1
			Note that the title will be converted to all
			capital letters.
TITLE 1
			using this version, the title will be prompted.
TITLE
			Prompts will be generated for the file number
			and the title.
===> COMMAND  WAVELENGTH
 Used to enter a default wavelength for the READ and SIMULATE command.  
---  Parameter
wave_length
  A single wavelength value may be specified directly, where wave_length 
  is the x-ray or neutron wavelength in Angstrom. (The target_type will be 
  assumed to be SY for synchrotron radiation).

  If 0.0 is used for the wave_length, the program will enter d-space 
  mode (same as specifying WAVELENGTH/NOTARGET).

  If wave_length is used, /TARGET and /WTYPE should not. 
---  Qualifiers
/TARGET=target_type
/TARGET
/NOTARGET
 Specifies an x-ray target for conventional x-ray sources. 
 The choices for targets are:
 Cu, Mo, Ni, Co, Fe, Cr, Ag, NU, or SY. 
 Specifying /TARGET without a target_type is equivalent to 
 /TARGET=CU. (Capitalization of the target type is ignored.)
 If NU or SY (for neutron or synchrotron radiation) is used, 
 the program prompts for a wavelength. 

 For input/output using d-spacings specify /NOTARGET

 The /TARGET option cannot be specified with a wave_length value.
/WTYPE=wave_type
   wave_type may be either 1, 2 or 3 which determines 
   the exact value used for the wavelength specified with /TARGET.
   The choices are:
  	1 to use K alpha 1 radiation 
  	2 to use K alpha 2 radiation 
  	3 to use the intensity weighted average of K alpha 1 and K alpha 2 
	  radiation.
   Specifying /WTYPE without a value for wave_type is equivalent 
   to specifying /WTYPE=1.
   This qualifier is ignored if the radiation source has a single 
   wavelength, (e.g. /TARGET=NU or /TARGET=SY) or a 
   wave_length value is specified.
---  Examples
WAVELENGTH/TARGET=CU/WTYPE=3
	The wavelength will be set to the average of Cu K alpha 1 and 
	K alpha 2.
WAVELENGTH/TARGET
	The wavelength will be set to Cu K alpha 1 
WAVE/NOTAR
	Peaks positions, etc. will be displayed as d-spaces.
WAVE 0.0
	Peaks positions, etc. will be displayed as d-spaces.
WAVE 2.5401
	The wavelength will be set to 2.5401Angstrom.
WAVE
	The user will be prompted to choose a wavelength or two use
	d-spacings. 
WAVELENGTH/TARGET=NU/WTYPE=3
	The user will be prompted to enter a wavelength; the /WTYPE=3
	qualifier will be ignored.
===> COMMAND  WRITE
  Write one of the "files" in memory (from the table of available
  files) onto disk.
---  Parameter
file_number
 The number of a single file may be specified on the command line
 referencing the number of the file to be written. If the file number
 is not specified a prompt will be given requesting a file number.
---  Qualifiers
/FILENAME=file_name
 The name to be used for the file. This overrides the name already
 associated with the file and will replace that name. If /FILENAME is
 not specified and CMPR is run interactively, a prompt will be
 generated for the name of the file.
/BINARY
/NBS
/PROFPV
/GSAS
/JONES
/PEAKS
 Determines the format of the file to be written. If CMPR is run
 in MANUAL mode (see command DEFAULT) and none of these options is
 specified, a prompt will be generated. (In AUTO mode the default is
 /BINARY)
      /BINARY writes a file in du Pont format
      /PEAKS  Writes an ASCII file with just the peak information.
---  Examples
 WRITE 1
			This command causes file #1 to be written. The
			file name and format will be prompted for (in
			MANUAL mode).
 write 7/BIN/FILE=tmp:copy.bin
			This command causes file #7 to be written
			as TMP:COPY.BIN in binary format.
 WR/NB
			This command causes file #1 to be written in
			"NBS" format. The file number will be prompted
			for and in MANUAL mode, so will the file name.