DOCUMENTATION FOR PROGRAM LOGIC

 Program LOGIC is used to search the ICDD-JCPDS database for materials with
 selected characteristics. 
 The ICDD-JCPDS database contains approximately 60,000 sets of summarized 
 diffraction patterns. The database is copyright by the International
 Centre for Diffraction Data and may be used only by license.
 This program maintains a working subset of the full database, referred 
 to as the "current table" where the contents of the table may be 
 increased or decreased according to logical criteria  set by the user.

 There are five basic categories of instructions that may be given to
 LOGIC. 
 Commands READ and WRITE are used to read in or write out a stored table;
 commands TABLES, BROWSE, and INDEX are used to examine the entries
   in the current table;
 commands ADD, MATCH and CULL modify the current list by applying logical
   criteria;
 command WAVELENGTH controls whether the program will use d-spaces or 
   two-theta angles for input and output; and command DELETED controls
   usage of "deleted" patterns.
 commands DCL, FILE, HELP and EXIT are used for program control.


The following element symbols are defined within program LOGIC:
   
	H, He, Li, Be, B, C, N, O, F, Ne, Na, Mg, Al, Si, P, S, Cl, 
	Ar, K, Ca, Sc, Ti, V, Cr, Mn, Fe, Co, Ni, Cu, Zn, Ga, Ge, 
	As, Se, Br, Kr,	Rb, Sr, Y, Zr, Nb, Mo, Tc, Ru, Rh, Pd, Ag, 
	Cd, In,	Sn, Sb, Te, I, Xe, Cs, Ba, La, Ce, Pr, Nd, Pm, Sm,
	Eu, Gd, Tb, Dy, Ho, Er, Tm, Yb, Lu, Hf, Ta, W, Re, Os, Ir, 
	Pt, Au, Hg, Tl, Pb, Bi, Po, At, Rn, Fr, Ra, Ac, Th, Pa, U, 
	Np, Pu, Am, Cm, Bk, Cf, Es, Fm, Md, No, Lr


   LN    Lanthanides (La - Lu)
   AD    Actinides (Ac - Lr)
   1a    period 1 (H,Li,Na,K,Rb,Cs,Fr)
   2a    period 2 (Be,Mg,Ca,Sr,Ba,Ra)
   3a    period 3 (B,Al,Ga,In,Tl)
   4a    period 4 (C,Si,Ge,Sn,Pb)
   5a    period 5 (N,P,As,Sb,Bi)
   6a    period 6 (O,S,Se,Te,Po)
   7a    period 7 (H,F,Cl,Br,I,At)
   8a    period 8 (He,Ne,Ar,Kr,Xe,Rn)
   1b    transition metals period 9 (Cu,Ag,Au)
   2b    transition metals period 10 (Zn,Cd,Hg)
   3b    transition metals period 1 (Sc,Y,La,Ac)
   4b    transition metals period 2 (Ti,Zr,Hf)
   5b    transition metals period 3 (V,Nb,Ta)
   6b    transition metals period 4 (Cr,Mo,W)
   7b    transition metals period 5 (Mn,Tc,Re)
   8b    transition metals period 6-8 (Fe,Co,Ni,Ru,Rh,Pd,Os,Ir,Pt)

===> COMMAND  ADD
 Command ADD increases the number of entries in the current table using 
 a logical .OR. operation to add all entries which match a specified
 logical criterion. Command OR is completely equivalent to command ADD.

 There are four possible logical criteria that may be established: 
    /ELEMENTS A list of entries is specified by a partial or
		complete elemental composition
    /CARD     A list of entries is specified by ICDD-JCPDS number
    /PEAKS    A list of entries is specified by positions of the major
		peaks in the pattern.
    /COUNT    A list of entries is specified by the number of different 
		elements in the chemical formula.

 Qualifiers may be specified in only certain combinations. Square brackets 
 ([ ]) indicate parameters that are allowed but are not required.
 For example, if /ELEMENTS/OPTIONAL is used, /EXACT is assumed,
 and need not be specified explicitly.
 Angle brackets (< >) indicate that only one of the enclosed 
 parameters parameters may be chosen. For example, for /PEAKS/OR 
 either /DSPACE or /WAVELENGTH may be used, but not both.
 Curly brackets ({ }) indicate that more than one of the the enclosed 
 parameters parameters may be chosen, but at least one must be chosen.
 For example, either /OPTIONAL or /I_SPAN or both may be specified
 with /ELEMENTS but one of the two must be specified, unless /OR or
 /AND or /EXACT is used.

    ADD {/ELEMENTS= /E_SPAN=} /OR
    ADD {/ELEMENTS= /E_SPAN=} /AND
    ADD {/ELEMENTS= /E_SPAN=} /EXACT
    ADD {/ELEMENTS= /E_SPAN=} {/OPTIONAL= /O_SPAN=} [/EXACT]
    
    ADD/CARDS
    
    ADD/COUNT=
    
    ADD/PEAKS=/OR/FAST  [/ERROR=] [/LEVEL=] </DSPACE /WAVELENGTH=]>
    ADD/PEAKS=/AND/FAST [/ERROR=] [/LEVEL=] </DSPACE /WAVELENGTH=]>
    ADD/PEAKS=/OR/EXACT/ERROR=  [/LEVEL=] </DSPACE /WAVELENGTH]>
    ADD/PEAKS=/AND/EXACT/ERROR= [/LEVEL=] </DSPACE /WAVELENGTH]>
    

 The /ELEMENTS (or /E_SPAN), /CARD or /PEAKS qualifier 
 should be specified before other all other qualifiers. 
---  Qualifiers
/ELEMENTS=required_list
/ELEMENTS
/E_SPAN=req_range(s)
 Use this options to specify a list of elements which must be present for
 the logical criterion to be matched. The list of elements may be used 
 in one of four different ways:
    /OR       
		An entry with a composition containing any one of the 
		specified elements is a match.
    /AND      
		An entry with a composition containing all of the 
		specified elements is a match.
    /EXACT    
		An entry with a composition containing all of the 
		specified elements and no others is a match.
    /OPTIONAL (and/or /O_SPAN) 
		An entry with a composition containing all of the 
		specified elements and any or none of the optional 
		elements, but no others no others is a match.

 Use /E_SPAN to specify a range of elements which must be present for
 the logical criterion to be matched. This option is equivalent to 
 specifying the elements individually in the required_list using 
 /ELEMENTS.

 Examples of the use of these qualifiers are:
    /ELEMENTS=SI
    /elem=(si,o,H)
    /E_SPAN=(H,BE)
    /E_SPAN=(Be,H) (same as previous)
    /ELEMENTS=(H,HE,LI,BE) (same as previous)
    /E_SPAN=(H,BE,C,F) (specifies two ranges: from H to Be and 
		from C to F.

 Note that capitalization is ignored and the elements must be surrounded
 by parentheses and separated by commas, if more than one element is
 specified. For the /E_SPAN qualifier, element ranges may be 
 specified in either ascending or descending order. 
 To specify more than one range, specify more than one pair of endpoints.
 If no elements are specified with /ELEMENTS, and /E_SPAN is not 
 used, the program will prompt for elements.

 The following qualifiers may not be used with /ELEMENTS or /E_SPAN: 
	/CARDS, /PEAKS, /FAST, /ERROR, or /LEVEL.
 The /ELEMENTS or /E_SPAN qualifier should be specified before 
 other all other qualifiers. 
/COUNT=elm_count
/COUNT=(c_min,c_max)
/COUNT
 Use this qualifier to select entries using the number of unique elements 
 in the chemical formula. The qualifier may be used three ways, if a 
 single value is specified, for example /COUNT=2, then entries are 
 selected with that single number of elements. If two values are used, 
 for example /COUNT=(2,4) the two numbers represent a range of values,
 in this case 2, 3 or 4 elements are allowed. If no value is specified,
 the computer will prompt for one or more values.

 Note that Cr2O3 . xH2O will be counted as having 3 elements in the
 formula.

 No other qualifiers are allowed with /COUNT. 
/CARDS=card_list
/CARDS
 Use this qualifier to select entries using their ICDD-JCPDS entry number.
 The entry number is always a five or six digit number consisting
 of the "old" entry number plus 10,000 times the set number. For
 example, entry 413 in set 7 would be coded as:
    /CARD=70413 or
   	/CARD=070413
 To specify more than one entry, separate the list with commas and
 enclose the list in parentheses:
   	/CARD=(070413,10001)

No other qualifiers are allowed with use of the /CARDS qualifier.
/PEAKS=peak_list
/PEAKS
 Use this option to select entries based on the location of the
 intense peaks in the pattern. The peak positions must be input
 as either two-theta angles or as d-spaces depending on the 
 current wavelength setting (see command WAVELENGTH). The 
 wavelength setting may be overridden using the /WAVELENGTH
 or the /DSPACE qualifiers.

 All entries with intense peaks (the intensity threshold is set by
 the /LEVEL option) within some region around input peak
 position will be selected. The actual window depends on the
 value(s) used on the /ERROR option.  If more than one peak 
 is input, the peaks should be separated by  commas and enclosed 
 in parentheses.  The list of peaks may be used in one of two 
 different ways:
    /OR  An entry with a composition containing any one of the 
		specified peaks is a match.
    /AND An entry with a composition containing all of the 
		specified peaks is a match.
 If no peaks are input, the program will prompt for a list of peaks.

 The following qualifiers may not be used with /PEAKS: 
	/CARDS, /ELEMENTS, /E_SPAN, /COUNT,
	/OPTIONAL, or /O_SPAN.
 Specify /PEAKS as the first qualifier on the line.
/ERROR=error_list
 The error_list specifies an allowed range for each peak.
 The range is used in one of two ways, depending on mode used by
 the program. If the mode is /EXACT, the error range is used
 exactly as specified. For example, If 
	/PEAK=15.5/ERROR=0.1/EXACT
 is used, peaks at locations between 15.4 and 15.6 will be 
 selected. The other mode, /FAST, may be considerably more rapid
 than /EXACT. In /FAST mode, the range specified with /ERROR 
 is expanded to match spacing of records in the peak index files.
 For example, if the peak index records cover the ranges, 15.15-15.3, 
 15.3-15.45, 15.45-15.6, etc., then if 
	/PEAK=15.5/ERROR=0.1/FAST
 is used, then the error range will be expanded to select peaks 
 between 15.3 and 15.6.
 
 An error value may be specified for each peak, but if the number 
 of values in the error_list is less than the number of peaks in 
 the peak_list, the last error value will be used for all 
 remaining peaks. If the /ERROR parameter is not used, the 
 program will prompt for a single error value for all peaks.
 The error value should be specified in the same units (d-space 
 or two-theta) as the peak positions.

 The /PEAKS qualifier must precede this qualifier.
 The following qualifiers may not be used with /ERROR:
	/CARDS, /ELEMENTS, /E_SPAN, /COUNT,
	/OPTIONAL, or /O_SPAN.
/DSPACE
 Using this qualifier overrides the current wavelength setting and forces
 peaks to be input as d-spaces. This qualifier cannot be used with 
 /WAVELENGTH and will be ignored if used with a qualifier other than 
 /PEAKS.
/WAVELENGTH=wave_length
 Using this qualifier overrides the current wavelength setting and forces
 peaks to be input as two-theta angles at wave_lengthAngstrom. This qualifier 
 cannot be used with /DSPACE and will be ignored if used with a qualifier 
 other than /PEAKS.
/LEVEL=peak_level
 Specifies a relative intensity threshold for peak positions specified 
 with the /PEAKS qualifier. The threshold value is used slightly 
 differently in /FAST mode versus /EXACT mode. In /EXACT mode,
 the value specifies the exact intensity threshold (in percent relative 
 intensity). For example if /PEAKS=20.5/ERR=0.1/LEVEL=75/DSPACE/EXACT 
 is specified, entries with peaks having d-spaces from 20.4 to 20.6 Angstrom 
 with relative intensities of 75% or greater will be located.
 In /FAST mode, the threshold value specifies a peak index to 
 be searched. If there is no peak index at this value, a peak index
 with a lower threshold is used (at 10 % increments). Thus in the 
 example /PEAKS=20.5/ERR=0.1/LEVEL=75/DSPACE/FAST, the error range is 
 opened (see /ERROR) and the intensity threshold is also possibly 
 lowered, so that potentially more entries will be selected than in 
 /EXACT mode. It is also possible to specify /LEVEL=3s in /FAST mode.
 This specifies an index of the three strongest peaks in each entry.

 The /PEAKS qualifier must precede this qualifier.
 The following qualifiers may not be used with /LEVEL:
	/CARDS, /ELEMENTS, /E_SPAN, /COUNT 
	/OPTIONAL, or /O_SPAN.
/EXACT
 Use /EXACT with /ELEMENTS to specify that only entries
 containing all of the specified elements and no others
 match as the specified logical criterion. It is possible to widen 
 this criterion so that certain elements are allowed, but not required, 
 using the /OPTIONAL and/or /O_SPAN qualifiers. 

 Use /EXACT with /PEAKS to specify that the error range specified
 for peak positions should not be extended, but instead be used as given.
 (See the description given for /ERROR.)

 The following qualifiers may not be used with /EXACT and /ELEMENTS: 
	/CARDS, /PEAKS, /OR, /AND, /ERROR, /FAST,
	/COUNT or /LEVEL.

 The following qualifiers may not be used with /EXACT and /PEAKS: 
	/CARDS, /ELEMENTS, /E_SPAN, /FAST, /COUNT 
	/OPTIONAL, or /O_SPAN.
/FAST
 Use /FAST with /PEAKS to specify that the error range specified
 for peak positions may be extended for most efficient searching.
 (See the description given for /ERROR.)

 The following qualifiers may not be used with /FAST: 
	/CARDS, /ELEMENTS, /E_SPAN, /OPTIONAL, /EXACT,
	/COUNT or /O_SPAN.
/OR
 Use /OR with either /PEAKS or /ELEMENTS to specify that any entry
 containing the specified element or peak is a match for the specified 
 logical criterion.
 The following qualifiers may not be used with /OR: 
	/CARDS, /AND, /COUNT, /OPTIONAL, or /O_SPAN.
 Also, if /ELEMENTS and /OR are used, /EXACT cannot be used.
/AND
 Use /AND with either /PEAKS or /ELEMENTS to specify that only entries
 containing all of the specified elements or peaks match for the specified 
 logical criterion.
 The following qualifiers may not be used with /AND: 
	/CARDS, /OR, /COUNT, /OPTIONAL, or /O_SPAN.
 Also, if /ELEMENTS and /AND are used, /EXACT cannot be used.
/OPTIONAL=optional_list
/O_SPAN=opt_range(s)
 Use /OPTIONAL or /O_SPAN with /ELEMENTS to specify that only 
 entries containing all of the required elements specified in the 
 required_list (see /ELEMENTS and /E_SPAN) and optionally those 
 in the optional_list, but no others, as the specified logical 
 criterion. /O_SPAN is equivalent to /OPTIONAL except that ranges
 of elements may be specified.

 Examples of the use of this qualifier are:
    /OPTIONAL=SI
    /ig=(si,o,H)
    /O_SPAN=(H,BE) 
    /O_SPAN=(BE,H) (equivalent to previous)
    /OPTIONAL=(H,HE,LI,BE) (equivalent to previous)
    /O_SPAN=(H,BE,C,F) specifies two ranges: from H to Be and 
		from C to F.
 Note that capitalization is ignored and the elements must be surrounded
 by parentheses and separated by commas, if more than one element is
 specified. 
 Ranges may be specified in either ascending or descending order.
 To specify more than one range, specify more than one pair of endpoints.

 The following qualifiers may not be used with /OPTIONAL or /O_SPAN: 
	/CARDS, /PEAKS, /FAST, /OR, /AND, 
	/ERROR, /COUNT, or /LEVEL.
 Qualifier /EXACT is assumed to be present if /OPTIONAL or /O_SPAN
 is used and thus is optional. /O_SPAN may be used with /OPTIONAL.
===> COMMAND  BROWSE
 Use this function to examine tables of angles or d-spaces for all entries 
 in the "current list" from a terminal. Entries are displayed one at a 
 time; it is possible to page backwards or forwards in the list and to
 print selected entries. If the full ICDD-JCPDS (PDF-2) database is on-line,
 the entire ICDD-JCPDS entry may be displayed or printed.

 After entering the BROWSE command, a prompt line is displayed, which 
 shows the total number of entries in the current list and the relative 
 position of the current entry within the list. Also displayed is a 
 list of available commands.  The following commands are defined:
  	 +n_p moves forward in the list by n_p entries; 
  	 -n_p moves backward by n_p entries;
  	 >n_p displays the n_p-th entry in the list;
  	 [crd displays ICDD-JCPDS entry crd, or the closest entry in the 
		list by number;
  	      (blank line) displays the next entry;
  	 P    prints the chemical information and D/I data (PDF-1 data) 
		for the current entry and advances to the next entry;
  	 C    culls (removes) the current entry from the current table 
		and advances to the next entry;
  	 D    displays all the information for the current entry 
		in the full ICDD-JCPDS (PDF-2) database;
  	 A    prints All the information for the current entry 
		and advances to the next entry;
  	 G    graphically displays one or more entries, starting from
		the current entry;
  	 ^Z   or advancing past the last entry terminates BROWSE mode.
 
 The command letter or symbol, (+, > or P, for example) must be 
 the first letter on the line. Commands which are not valid are not
 given in the list of options. 
 Commands D and A both require the PDF-2 database either on disk or on 
 CD-ROM. If the PDF-2 database is unavailable, these options will not be 
 listed.
 The graph command, G, is only available on graphics-compatible terminals. 
 This command can be used to display experimental data as well as ICDD-JCPDS
 entries. Each time the command is called, one can input a data or peak file
 to the program and this data will be displayed as well as the selected 
 entries. A wide variety of peak and data files may be read 
 Of particular use will be SEARCH temporary files, which may 
 be read directly at this point by LOGIC and may then then be plotted.
===> COMMAND  COMMENT
 The program records a summary of the logical steps (commands that 
 modify the contents of the current table). Use this command to 
 place a comment line into the list of logical steps. The comment
 may be placed on the same line as the COMMENT command, or will be
 prompted.
---  Parameter
comment_line
 A single line of comments may be placed after the COMMENT command.
 Lowercase letters will be translated to uppercase if the 
 comment_line is placed on the same line, rather than entered at 
 the prompt.

===> COMMAND  CULL
 Command CULL decreases the number of entries in the current table using 
 a logical .AND. .NOT. operation to remove all entries which match a 
 specified logical criterion. Command NAND is completely equivalent to 
 command CULL.

 There are five possible logical criteria that may be established: 
    /ELEMENTS A list of entries is specified by a partial or
		complete elemental composition
    /CARD     A list of entries is specified by number
    /PEAKS    A list of entries is specified by positions of the 
		major peaks in the pattern.
    /NAME     A list of entries is specified by chemical/mineral name
    /COUNT    A list of entries is specified by the number of different 
		elements in the chemical formula.

 Qualifiers may be specified in only certain combinations. Square brackets 
 ([ ]) indicate parameters that are allowed but are not required.
 For example, if /ELEMENTS/OPTIONAL is used, /EXACT is assumed,
 and need not be specified explicitly.
 Angle brackets (< >) indicate that only one of the enclosed 
 parameters parameters may be chosen. For example, for /PEAKS/OR 
 either /DSPACE or /WAVELENGTH may be used, but not both.
 Curly brackets ({ }) indicate that more than one of the the enclosed 
 parameters parameters may be chosen, but at least one must be chosen.
 For example, either /OPTIONAL or /I_SPAN or both may be specified
 with /NOELEMENTS but one of the two should be specified.

    CULL {/ELEMENTS= /E_SPAN=} /OR
    CULL {/ELEMENTS= /E_SPAN=} /AND
    CULL {/ELEMENTS= /E_SPAN=} /EXACT
    CULL {/ELEMENTS= /E_SPAN=} {/OPTIONAL= /O_SPAN=} [/EXACT]
    CULL/NOELEMENTS {/OPTIONAL= /O_SPAN=} [/EXACT]
    
    CULL/CARDS=
    
    CULL/NAME=
    
    CULL/COUNT=
    
    CULL/PEAKS=/OR/FAST  [/ERROR=] [/LEVEL=] </DSPACE /WAVELENGTH=]>
    CULL/PEAKS=/AND/FAST [/ERROR=] [/LEVEL=] </DSPACE /WAVELENGTH=]>
    CULL/PEAKS=/OR/EXACT/ERROR=  [/LEVEL=] </DSPACE /WAVELENGTH=]>
    CULL/PEAKS=/AND/EXACT/ERROR= [/LEVEL=] </DSPACE /WAVELENGTH=]>
    

 The /ELEMENTS (or /E_SPAN), /CARD, /NAME or /PEAKS qualifier 
 should be specified before other all other qualifiers. 
---  Qualifiers
/ELEMENTS=required_list
/ELEMENTS
/NOELEMENTS
/E_SPAN=req_range(s)
 Use this options to specify a list of elements which must be present for
 the logical criterion to be matched. The list of elements may be used 
 in one of four different ways:
    /OR       
		An entry with a composition containing any one of the 
		specified elements is a match.
    /AND      
		An entry with a composition containing all of the 
		specified elements is a match.
    /EXACT    
		An entry with a composition containing all of the 
		specified elements and no others is a match.
    /OPTIONAL (and/or /O_SPAN) 
		An entry with a composition containing all of the 
		specified elements and any or none of the optional 
		elements, but no others no others is a match.

 Use /E_SPAN to specify a range of elements which must be present for
 the logical criterion to be matched. This option is equivalent to 
 specifying the elements individually in the required_list using 
 /ELEMENTS.

 The /NOELEMENTS option is used if there are no required elements,
 but optional elements will be specified using the /OPTIONAL or
 /O_SPAN options. Thus, entries will be removed that have any 
 combination of the optional elements and no others. Use of this
 option will remove all entries with unassigned chemical formulas, 
 as would be performed by a CULL/COUNT=0 command.

 Examples of the use of these qualifiers are:
    /ELEMENTS=SI
    /elem=(si,o,H)
    /E_SPAN=(H,BE)
    /E_SPAN=(Be,H) (same as previous)
    /ELEMENTS=(H,HE,LI,BE) (same as previous)
    /E_SPAN=(H,BE,C,F) (specifies two ranges: from H to Be and 
		from C to F.

 Note that capitalization is ignored and the elements must be surrounded
 by parentheses and separated by commas, if more than one element is
 specified. For the /E_SPAN qualifier, element ranges may be 
 specified in either ascending or descending order. 
 To specify more than one range, specify more than one pair of endpoints.
 If no elements are specified with /ELEMENTS, and /E_SPAN is not 
 used, the program will prompt for elements.

 The following qualifiers may not be used with /ELEMENTS or /E_SPAN: 
	/CARDS, /NAME, /PEAKS, /FAST, /ERROR, or /LEVEL.
 The /ELEMENTS or /E_SPAN qualifier should be specified before 
 other all other qualifiers. 
/COUNT=elm_count
/COUNT=(c_min,c_max)
/COUNT
 Use this qualifier to select entries using the number of unique elements 
 in the chemical formula. The qualifier may be used three ways, if a 
 single value is specified, for example /COUNT=2, then entries are 
 selected with that single number of elements. If two values are used, 
 for example /COUNT=(2,4) the two numbers represent a range of values,
 in this case 2, 3 or 4 elements are allowed. If no value is specified,
 the computer will prompt for one or more values.

 Note that Cr2O3 . xH2O will be counted as having 3 elements in the
 formula.

 No other qualifiers are allowed with /COUNT. 
/CARDS=card_list
/CARDS
 Use this qualifier to select entries using their ICDD-JCPDS entry number.
 The entry number is always a five or six digit number consisting
 of the "old" entry number plus 10,000 times the set number. For
 example, entry 413 in set 7 would be coded as:
    /CARD=70413 or
   	/CARD=070413
 To specify more than one entry, separate the list with commas and
 enclose the list in parentheses:
   	/CARD=(070413,10001)

No other qualifiers are allowed with use of the /CARDS qualifier.
/NAME=compound_name
/NAME=mineral_name
  A fragment of a chemical or mineral name to be matched. The name 
  listed on an entry must match the compound_name fragment letter 
  for letter (lowercase letters will be converted to uppercase). If
  spaces are to be included in the fragment, the fragment should be 
  enclosed in quotation marks ("). For example, 
    /NAME=silicon
    /NAME="silicon oxide"

  No other qualifiers may be used with /NAME.
/PEAKS=peak_list
/PEAKS
 Use this option to select entries based on the location of the
 intense peaks in the pattern. The peak positions must be input
 as either two-theta angles or as d-spaces depending on the 
 current wavelength setting (see command WAVELENGTH). The 
 wavelength setting may be overridden using the /WAVELENGTH
 or the /DSPACE qualifiers.

 All entries with intense peaks (the intensity threshold is set by
 the /LEVEL option) within some region around input peak
 position will be selected. The actual window depends on the
 value(s) used on the /ERROR option.  If more than one peak 
 is input, the peaks should be separated by  commas and enclosed 
 in parentheses.  The list of peaks may be used in one of two 
 different ways:
    /OR  An entry with a composition containing any one of the 
		specified peaks is a match.
    /AND An entry with a composition containing all of the 
		specified peaks is a match.
 If no peaks are input, the program will prompt for a list of peaks.

 The following qualifiers may not be used with /PEAKS: 
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /COUNT,
	/OPTIONAL, or /O_SPAN.
 Specify /PEAKS as the first qualifier on the line.
/ERROR=error_list
 The error_list specifies an allowed range for each peak.
 The range is used in one of two ways, depending on mode used by
 the program. If the mode is /EXACT, the error range is used
 exactly as specified. For example, If 
	/PEAK=15.5/ERROR=0.1/EXACT
 is used, peaks at locations between 15.4 and 15.6 will be 
 selected. The other mode, /FAST, may be considerably more rapid
 than /EXACT. In /FAST mode, the range specified with /ERROR 
 is expanded to match spacing of records in the peak index files.
 For example, if the peak index records cover the ranges, 15.15-15.3, 
 15.3-15.45, 15.45-15.6, etc., then if 
	/PEAK=15.5/ERROR=0.1/FAST
 is used, then the error range will be expanded to select peaks 
 between 15.3 and 15.6.
 
 An error value may be specified for each peak, but if the number 
 of values in the error_list is less than the number of peaks in 
 the peak_list, the last error value will be used for all 
 remaining peaks. If the /ERROR parameter is not used, the 
 program will prompt for a single error value for all peaks.
 The error value should be specified in the same units (d-space 
 or two-theta) as the peak positions.

 The /PEAKS qualifier must precede this qualifier.
 The following qualifiers may not be used with /ERROR:
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /COUNT,
	/OPTIONAL, or /O_SPAN.
/DSPACE
 Using this qualifier overrides the current wavelength setting and forces
 peaks to be input as d-spaces. This qualifier cannot be used with 
 /WAVELENGTH and will be ignored if used with a qualifier other than 
 /PEAKS.
/WAVELENGTH=wave_length
 Using this qualifier overrides the current wavelength setting and forces
 peaks to be input as two-theta angles at wave_lengthAngstrom. This qualifier 
 cannot be used with /DSPACE and will be ignored if used with a qualifier 
 other than /PEAKS.
/LEVEL=peak_level
 Specifies a relative intensity threshold for peak positions specified 
 with the /PEAKS qualifier. The threshold value is used slightly 
 differently in /FAST mode versus /EXACT mode. In /EXACT mode,
 the value specifies the exact intensity threshold (in percent relative 
 intensity). For example if /PEAKS=20.5/ERR=0.1/LEVEL=75/DSPACE/EXACT 
 is specified, entries with peaks having d-spaces from 20.4 to 20.6 Angstrom 
 with relative intensities of 75% or greater will be located.
 In /FAST mode, the threshold value specifies a peak index to 
 be searched. If there is no peak index at this value, a peak index
 with a lower threshold is used (at 10 % increments). Thus in the 
 example /PEAKS=20.5/ERR=0.1/LEVEL=75/DSPACE/FAST, the error range is 
 opened (see /ERROR) and the intensity threshold is also possibly 
 lowered, so that potentially more entries will be selected than in 
 /EXACT mode. It is also possible to specify /LEVEL=3s in /FAST mode.
 This specifies an index of the three strongest peaks in each entry.

 The /PEAKS qualifier must precede this qualifier.
 The following qualifiers may not be used with /LEVEL:
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /COUNT 
	/OPTIONAL, or /O_SPAN.
/EXACT
 Use /EXACT with /ELEMENTS to specify that only entries
 containing all of the specified elements and no others
 match as the specified logical criterion. It is possible to widen 
 this criterion so that certain elements are allowed, but not required, 
 using the /OPTIONAL and/or /O_SPAN qualifiers. 

 Use /EXACT with /PEAKS to specify that the error range specified
 for peak positions should not be extended, but instead be used as given.
 (See the description given for /ERROR.)

 The following qualifiers may not be used with /EXACT and /ELEMENTS: 
	/CARDS, /NAME, /PEAKS, /OR, /AND, /ERROR, /FAST,
	/COUNT or /LEVEL.

 The following qualifiers may not be used with /EXACT and /PEAKS: 
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /FAST, /COUNT 
	/OPTIONAL, or /O_SPAN.
/FAST
 Use /FAST with /PEAKS to specify that the error range specified
 for peak positions may be extended for most efficient searching.
 (See the description given for /ERROR.)

 The following qualifiers may not be used with /FAST: 
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /OPTIONAL, /EXACT,
	/COUNT or /O_SPAN.
/OR
 Use /OR with either /PEAKS or /ELEMENTS to specify that any entry
 containing the specified element or peak is a match for the specified 
 logical criterion.
 The following qualifiers may not be used with /OR: 
	/CARDS, /NAME, /AND, /COUNT, /OPTIONAL, or /O_SPAN.
 Also, if /ELEMENTS and /OR are used, /EXACT cannot be used.
/AND
 Use /AND with either /PEAKS or /ELEMENTS to specify that only entries
 containing all of the specified elements or peaks match for the specified 
 logical criterion.
 The following qualifiers may not be used with /AND: 
	/CARDS, /NAME, /OR, /COUNT, /OPTIONAL, or /O_SPAN.
 Also, if /ELEMENTS and /AND are used, /EXACT cannot be used.
/OPTIONAL=optional_list
/O_SPAN=opt_range(s)
 Use /OPTIONAL or /O_SPAN with /ELEMENTS to specify that only 
 entries containing all of the required elements specified in the 
 required_list (see /ELEMENTS and /E_SPAN) and optionally those 
 in the optional_list, but no others, as the specified logical 
 criterion. /O_SPAN is equivalent to /OPTIONAL except that ranges
 of elements may be specified.

 Examples of the use of this qualifier are:
    /OPTIONAL=SI
    /ig=(si,o,H)
    /O_SPAN=(H,BE) 
    /O_SPAN=(BE,H) (equivalent to previous)
    /OPTIONAL=(H,HE,LI,BE) (equivalent to previous)
    /O_SPAN=(H,BE,C,F) specifies two ranges: from H to Be and 
		from C to F.
 Note that capitalization is ignored and the elements must be surrounded
 by parentheses and separated by commas, if more than one element is
 specified. 
 Ranges may be specified in either ascending or descending order.
 To specify more than one range, specify more than one pair of endpoints.

 The following qualifiers may not be used with /OPTIONAL or /O_SPAN: 
	/CARDS, /NAME, /PEAKS, /FAST, /OR, /AND, 
	/ERROR, /COUNT, or /LEVEL.
 Qualifier /EXACT is assumed to be present if /OPTIONAL or /O_SPAN
 is used and thus is optional. /O_SPAN may be used with /OPTIONAL.
===> COMMAND  DCL
 Spawns a subprocess to execute DCL commands, type LOGOUT to 
 return back to LOGIC without affecting the "current list". 
 This command is useful for quick DCL "errands" such as answering a 
 mail message without exiting the program.

===> COMMAND  DELETED
 Some of the entries in the database are marked as "deleted" by the
 editors of the database. If these entries are included in the database
 (using the ENCODE program, PDF1) it is possible to select that these
 entries will be included or excluded from the operations of this
 program. 

 This command causes logical name PS_DELETED to be set so that 
 subsequent operations with the program and with other programs in the
 Powder Suite package will use the same option. The default mode for
 the program is DELETED/EXCLUDE. However, if desired the PS_DELETED
 logical name may be predefined (see customization instructions) to change
 the default.
---  Qualifiers
/INCLUDE
 Specifies that deleted entries will be included in the logical operations.
/EXCLUDE
 Specifies that deleted entries will be not be included in the logical operations.
===> COMMAND  EXIT
 Type EXIT (which can be abbreviated to EX) to exit from the program.
 Alternately, press Control Z (^Z) to exit. 

===> COMMAND  FILE
 Allows a series of commands to be input to the program from an external
 file. The file should be prepared before starting the program, or using
 the DCL command to invoke an editor. 
---  Parameter
file_name
 A single file may be specified on the command line containing the name
 of the file with commands. If the file is not specified, a prompt will be
 given to request a file name. 

 If no file extension is supplied, the default extension is .CMD

===> COMMAND  INDEX
 Displays an index of the entries in the current list, with the information
 for each entry summarized to a single line.
 There are three possible formats: 
 In "names" format, the chemical composition, chemical and mineral name 
 for each entry in the current list are given. In "Hanawalt" format, the
 most intense lines are listed with intensity and d-spacing or angle.
 This list may optionally be sorted in order of increasing d-space or 
 angle and the most intense lines may be permuted. In "maxD" format, 
 the lines are listed in order of decreasing d-space (or increasing 
 angle). This list may be sorted and permuted, as before. 

 If /PRINT is not specified, the list is displayed on the terminal in 
 sections. After each section, a "Continue?" prompt appears. If the
 response is "N", "P" or ^Z, no more sections will be displayed. 
 If "P" is specified, the complete list will be printed. Enter "Y" 
 or a blank line for the next section.
---  Qualifiers
/HANAWALT=sort_lines
/HANAWALT
 The list is displayed in Hanawalt format -- an entry number followed by 
 the d-spaces or angles ordered by intensity. 
 
 Entries are listed by PDF file in sequential order, unless the sort_lines
 option is specified, in which case the records are sorted by 
 increasing d-spacing or angle. 

 sort_lines specifies the number of peaks to be used for sorting:
  	 /HANAWALT=0 -- the list is sorted by set and entry number.
  	 /HANAWALT=1 -- the list is sorted based on the 
	most intense line.
  	 /HANAWALT=sort_lines -- (sort_lines=2,3,4 or 5), 
	the sort_lines most intense lines are permuted and then sorted, 
	thus the length of the list increases by a factor of sort_lines.
/MAXD=sort_lines
/MAXD
 The list is displayed in maxD format -- an entry number followed by 
 the d-spaces or angles ordered by decreasing d-space (increasing angle). 
 
 Entries are listed by PDF file in sequential order, unless the sort_lines
 option is specified, in which case the records are sorted by 
 increasing d-spacing or angle. 

 sort_lines specifies the number of peaks to be used for sorting:
  	 /MAXD=0 -- the list is sorted by set and entry number.
  	 /MAXD=1 -- the list is sorted based on the 
	highest d-space line.
  	 /MAXD=sort_lines -- (sort_lines=2,3,4 or 5), 
	the sort_lines highest d-space lines are permuted and then sorted, 
	thus the length of the list increases by a factor of sort_lines.
/NAMES
 The "current list" is displayed with chemical formula, compound name and
 mineral name. Entries are listed in sequential order by set and entry number.
/PRINT
 Prints the index rather than displaying it on the terminal.

===> COMMAND  MATCH
 Command MATCH decreases the number of entries in the current table using 
 a logical .AND. operation to remove all entries which do not match a 
 specified logical criterion. Command AND is completely equivalent to 
 command MATCH.

 There are five possible logical criteria that may be established: 
    /ELEMENTS A list of entries is specified by a partial or
		complete elemental composition
    /CARD     A list of entries is specified by number
    /PEAKS    A list of entries is specified by positions of the 
		major peaks in the pattern.
    /NAME     A list of entries is specified by chemical/mineral name
    /COUNT    A list of entries is specified by the number of different 
		elements in the chemical formula.

 Qualifiers may be specified in only certain combinations. Square brackets 
 ([ ]) indicate parameters that are allowed but are not required.
 For example, if /ELEMENTS/OPTIONAL is used, /EXACT is assumed,
 and need not be specified explicitly.
 Angle brackets (< >) indicate that only one of the enclosed 
 parameters parameters may be chosen. For example, for /PEAKS/OR 
 either /DSPACE or /WAVELENGTH may be used, but not both.
 Curly brackets ({ }) indicate that more than one of the the enclosed 
 parameters parameters may be chosen, but at least one must be chosen.
 For example, either /ELEMENTS or /E_SPAN or both may be specified, 
 but one of the two should be specified.

    MATCH {/ELEMENTS= /E_SPAN=} /OR
    MATCH {/ELEMENTS= /E_SPAN=} /AND
    MATCH {/ELEMENTS= /E_SPAN=} /EXACT
    MATCH {/ELEMENTS= /E_SPAN=} {/OPTIONAL= /O_SPAN=} [/EXACT]
    MATCH/NOELEMENTS {/OPTIONAL= /O_SPAN=} [/EXACT]
    
    MATCH/CARDS=
    
    MATCH/NAME=
    
    MATCH/COUNT=
    
    MATCH/PEAKS=/OR/FAST  [/ERROR=] [/LEVEL=] </DSPACE /WAVELENGTH=]>
    MATCH/PEAKS=/AND/FAST [/ERROR=] [/LEVEL=] </DSPACE /WAVELENGTH=]>
    MATCH/PEAKS=/OR/EXACT/ERROR=  [/LEVEL=] </DSPACE /WAVELENGTH=]>
    MATCH/PEAKS=/AND/EXACT/ERROR= [/LEVEL=] </DSPACE /WAVELENGTH=]>
    

 The /ELEMENTS (or /E_SPAN), /CARD, /NAME or /PEAKS qualifier 
 should be specified before other all other qualifiers. 
---  Qualifiers
/ELEMENTS=required_list
/ELEMENTS
/NOELEMENTS
/E_SPAN=req_range(s)
 Use this options to specify a list of elements which must be present for
 the logical criterion to be matched. The list of elements may be used 
 in one of four different ways:
    /OR       
		An entry with a composition containing any one of the 
		specified elements is a match.
    /AND      
		An entry with a composition containing all of the 
		specified elements is a match.
    /EXACT    
		An entry with a composition containing all of the 
		specified elements and no others is a match.
    /OPTIONAL (and/or /O_SPAN) 
		An entry with a composition containing all of the 
		specified elements and any or none of the optional 
		elements, but no others no others is a match.

 Use /E_SPAN to specify a range of elements which must be present for
 the logical criterion to be matched. This option is equivalent to 
 specifying the elements individually in the required_list using 
 /ELEMENTS.

 The /NOELEMENTS option is used if there are no required elements,
 but optional elements will be specified using the /OPTIONAL or
 /O_SPAN options. Thus, entries will be selected that have any 
 combination of the optional elements and no others. Use of this
 option will allow some unexpected entries, entries with unassigned
 chemical formulas. These entries may be removed using a 
 CULL/COUNT=0 command.

 Examples of the use of these qualifiers are:
    /ELEMENTS=SI
    /elem=(si,o,H)
    /E_SPAN=(H,BE)
    /E_SPAN=(Be,H) (same as previous)
    /ELEMENTS=(H,HE,LI,BE) (same as previous)
    /E_SPAN=(H,BE,C,F) (specifies two ranges: from H to Be and 
		from C to F.

 Note that capitalization is ignored and the elements must be surrounded
 by parentheses and separated by commas, if more than one element is
 specified. For the /E_SPAN qualifier, element ranges may be 
 specified in either ascending or descending order. 
 To specify more than one range, specify more than one pair of endpoints.
 If no elements are specified with /ELEMENTS, and /E_SPAN is not 
 used, the program will prompt for elements.

 The following qualifiers may not be used with /ELEMENTS or /E_SPAN: 
	/CARDS, /PEAKS, /ERROR, or /LEVEL.
 The /ELEMENTS or /E_SPAN qualifier should be specified before 
 other all other qualifiers. 
/COUNT=elm_count
/COUNT=(c_min,c_max)
/COUNT
 Use this qualifier to select entries using the number of unique elements 
 in the chemical formula. The qualifier may be used three ways, if a 
 single value is specified, for example /COUNT=2, then entries are 
 selected with that single number of elements. If two values are used, 
 for example /COUNT=(2,4) the two numbers represent a range of values,
 in this case 2, 3 or 4 elements are allowed. If no value is specified,
 the computer will prompt for one or more values.

 Note that Cr2O3 . xH2O will be counted as having 3 elements in the
 formula.

 No other qualifiers are allowed with /COUNT. 
/CARDS=card_list
/CARDS
 Use this qualifier to select entries using their ICDD-JCPDS entry number.
 The entry number is always a five or six digit number consisting
 of the "old" entry number plus 10,000 times the set number. For
 example, entry 413 in set 7 would be coded as:
    /CARD=70413 or
   	/CARD=070413
 To specify more than one entry, separate the list with commas and
 enclose the list in parentheses:
   	/CARD=(070413,10001)

No other qualifiers are allowed with use of the /CARDS qualifier.
/NAME=compound_name
/NAME=mineral_name
  A fragment of a chemical or mineral name to be matched. The name 
  listed on an entry must match the compound_name fragment letter 
  for letter (lowercase letters will be converted to uppercase). If
  spaces are to be included in the fragment, the fragment should be 
  enclosed in quotation marks ("). For example, 
    /NAME=silicon
    /NAME="silicon oxide"

  No other qualifiers may be used with /NAME.
/PEAKS=peak_list
/PEAKS
 Use this option to select entries based on the location of the
 intense peaks in the pattern. The peak positions must be input
 as either two-theta angles or as d-spaces depending on the 
 current wavelength setting (see command WAVELENGTH). The 
 wavelength setting may be overridden using the /WAVELENGTH
 or the /DSPACE qualifiers.

 All entries with intense peaks (the intensity threshold is set by
 the /LEVEL option) within some region around input peak
 position will be selected. The actual window depends on the
 value(s) used on the /ERROR option.  If more than one peak 
 is input, the peaks should be separated by  commas and enclosed 
 in parentheses.  The list of peaks may be used in one of two 
 different ways:
    /OR  An entry with a composition containing any one of the 
		specified peaks is a match.
    /AND An entry with a composition containing all of the 
		specified peaks is a match.
 If no peaks are input, the program will prompt for a list of peaks.

 The following qualifiers may not be used with /PEAKS: 
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /COUNT,
	/OPTIONAL, or /O_SPAN.
 Specify /PEAKS as the first qualifier on the line.
/ERROR=error_list
 The error_list specifies an allowed range for each peak.
 The range is used in one of two ways, depending on mode used by
 the program. If the mode is /EXACT, the error range is used
 exactly as specified. For example, If 
	/PEAK=15.5/ERROR=0.1/EXACT
 is used, peaks at locations between 15.4 and 15.6 will be 
 selected. The other mode, /FAST, may be considerably more rapid
 than /EXACT. In /FAST mode, the range specified with /ERROR 
 is expanded to match spacing of records in the peak index files.
 For example, if the peak index records cover the ranges, 15.15-15.3, 
 15.3-15.45, 15.45-15.6, etc., then if 
	/PEAK=15.5/ERROR=0.1/FAST
 is used, then the error range will be expanded to select peaks 
 between 15.3 and 15.6.
 
 An error value may be specified for each peak, but if the number 
 of values in the error_list is less than the number of peaks in 
 the peak_list, the last error value will be used for all 
 remaining peaks. If the /ERROR parameter is not used, the 
 program will prompt for a single error value for all peaks.
 The error value should be specified in the same units (d-space 
 or two-theta) as the peak positions.

 The /PEAKS qualifier must precede this qualifier.
 The following qualifiers may not be used with /ERROR:
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /COUNT,
	/OPTIONAL, or /O_SPAN.
/DSPACE
 Using this qualifier overrides the current wavelength setting and forces
 peaks to be input as d-spaces. This qualifier cannot be used with 
 /WAVELENGTH and will be ignored if used with a qualifier other than 
 /PEAKS.
/WAVELENGTH=wave_length
 Using this qualifier overrides the current wavelength setting and forces
 peaks to be input as two-theta angles at wave_lengthAngstrom. This qualifier 
 cannot be used with /DSPACE and will be ignored if used with a qualifier 
 other than /PEAKS.
/LEVEL=peak_level
 Specifies a relative intensity threshold for peak positions specified 
 with the /PEAKS qualifier. The threshold value is used slightly 
 differently in /FAST mode versus /EXACT mode. In /EXACT mode,
 the value specifies the exact intensity threshold (in percent relative 
 intensity). For example if /PEAKS=20.5/ERR=0.1/LEVEL=75/DSPACE/EXACT 
 is specified, entries with peaks having d-spaces from 20.4 to 20.6 Angstrom 
 with relative intensities of 75% or greater will be located.
 In /FAST mode, the threshold value specifies a peak index to 
 be searched. If there is no peak index at this value, a peak index
 with a lower threshold is used (at 10 % increments). Thus in the 
 example /PEAKS=20.5/ERR=0.1/LEVEL=75/DSPACE/FAST, the error range is 
 opened (see /ERROR) and the intensity threshold is also possibly 
 lowered, so that potentially more entries will be selected than in 
 /EXACT mode. It is also possible to specify /LEVEL=3s in /FAST mode.
 This specifies an index of the three strongest peaks in each entry.

 The /PEAKS qualifier must precede this qualifier.
 The following qualifiers may not be used with /LEVEL:
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /COUNT 
	/OPTIONAL, or /O_SPAN.
/EXACT
 Use /EXACT with /ELEMENTS to specify that only entries
 containing all of the specified elements and no others
 match as the specified logical criterion. It is possible to widen 
 this criterion so that certain elements are allowed, but not required, 
 using the /OPTIONAL and/or /O_SPAN qualifiers. 

 Use /EXACT with /PEAKS to specify that the error range specified
 for peak positions should not be extended, but instead be used as given.
 (See the description given for /ERROR.)

 The following qualifiers may not be used with /EXACT and /ELEMENTS: 
	/CARDS, /NAME, /PEAKS, /OR, /AND, /ERROR, /FAST 
	/LEVEL or /COUNT.

 The following qualifiers may not be used with /EXACT and /PEAKS: 
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /FAST, /COUNT 
	/OPTIONAL, or /O_SPAN.
/FAST
 Use /FAST with /PEAKS to specify that the error range specified
 for peak positions may be extended for most efficient searching.
 (See the description given for /ERROR.)

 The following qualifiers may not be used with /FAST: 
	/CARDS, /NAME, /ELEMENTS, /E_SPAN, /OPTIONAL, /EXACT,
	/COUNT or /O_SPAN.
/OR
 Use /OR with either /PEAKS or /ELEMENTS to specify that any entry
 containing the specified element or peak is a match for the specified 
 logical criterion.
 The following qualifiers may not be used with /OR: 
	/CARDS, /NAME, /AND, /COUNT, /OPTIONAL, or /O_SPAN.
 Also, if /ELEMENTS and /OR are used, /EXACT cannot be used.
/AND
 Use /AND with either /PEAKS or /ELEMENTS to specify that only entries
 containing all of the specified elements or peaks match for the specified 
 logical criterion.
 The following qualifiers may not be used with /AND: 
	/CARDS, /NAME, /OR, /COUNT, /OPTIONAL, or /O_SPAN.
 Also, if /ELEMENTS and /AND are used, /EXACT cannot be used.
/OPTIONAL=optional_list
/O_SPAN=opt_range(s)
 Use /OPTIONAL or /O_SPAN with /ELEMENTS to specify that only 
 entries containing all of the required elements specified in the 
 required_list (see /ELEMENTS and /E_SPAN) and optionally those 
 in the optional_list, but no others, as the specified logical 
 criterion. /O_SPAN is equivalent to /OPTIONAL except that ranges
 of elements may be specified.

 Examples of the use of this qualifier are:
    /OPTIONAL=SI
    /ig=(si,o,H)
    /O_SPAN=(H,BE) 
    /O_SPAN=(BE,H) (equivalent to previous)
    /OPTIONAL=(H,HE,LI,BE) (equivalent to previous)
    /O_SPAN=(H,BE,C,F) specifies two ranges: from H to Be and 
		from C to F.
 Note that capitalization is ignored and the elements must be surrounded
 by parentheses and separated by commas, if more than one element is
 specified. 
 Ranges may be specified in either ascending or descending order.
 To specify more than one range, specify more than one pair of endpoints.

 The following qualifiers may not be used with /OPTIONAL or /O_SPAN: 
	/CARDS, /NAME, /PEAKS, /FAST, /OR, /AND, 
	/ERROR, /COUNT, or /LEVEL.
 Qualifier /EXACT is assumed to be present if /OPTIONAL or /O_SPAN
 is used and thus is optional. /O_SPAN may be used with /OPTIONAL.
===> COMMAND  READ
 Reads a table (subfile) written by the WRITE command, prepared 
 using some other program, such as MATCH, or one of the standard 
 ICDD-JCPDS subfiles. The READ command can also be used to read a list of
 entries from a free-format ASCII text file or to select a list of
 entries in a range by number.

---  Parameter
file_name
 A single file may be specified on the command line containing the name
 of the file to be read. If the file is not specified, a prompt will be
 given to request a file name to be read. 

 If no file extension is supplied, the default extension is .USRPDF

 To read one of the standard subfiles, omit the file_name parameter 
 and specify the /SUBPDF qualifier. 
---  Qualifiers
/SUBPDF=sub_file
 Use this option to read in one of the standard subfiles, such as the
 the inorganic subfile.

 The available subfiles are: 
     FULL         all entries in the database
     NULL         null table (a table without any entries)
     INORGANICS   Inorganic materials
     ORGANICS     Materials with a C-H bond
     COMMON       commonly found materials or phases
     MINERALS     Minerals, natural and synthetic
     METALS       metals, alloys and related materials
     NIST         patterns recorded by NIST (NBS)
     FORENSIC     materials of forensic interest
     ZEOLITES     zeolites and molecular sieves
     DELETED      superceeded but not removed patterns (if any)
     LOCAL        locally defined patterns (if any)
     SUPERCON     superconductors and related materials
     EXPLOSIVES   explosives and related materials
     EDUCATION    educationally relevant materials
     CEMENT       materials related to cement production
     CORROSION    corrosion products and related materials

  Note that the sub_file name may be abbreviated by only including
  the initial letters as long as the name is uniquely specified.
  Also, note that by default, "DELETED" patterns are not included, 
  unless the DELETE/INCLUDE command is used to force inclusion 
  of deleted patterns.

  Do not include a file_name parameter if /SUBPDF is used.
/LIST=list_file
  Use this option to read a list of entries from a text file, named
  list_file (with default extension .CARDS). This file will usually
  be prepared prior to starting LOGIC through use of a text editor or
  with a non-Powder Suite program. 
  The list_file contains a list of ICDD-JCPDS entries with one entry 
  entry per line in the file. If an invalid number is used, a warning
  is reported.
  The entry number may entered either with or without a comma separating 
  the set number from the entry number (38,1 and 380001 are equivalent). 
  Comments may be included on each line provided that two commas or 
  are placed before the comment or the comment starts after column 20
  (see below). Blank lines in the file are ignored. A negative set number
  terminates reading the file, but use of a -1 is not required.

  Sample list_file:
              380001,,         this is the 1st entry in the list
   
              390001,,         this is the last entry
              -1

 The /LIST option may not be used with /SUBPDF or /RANGE.
 Omit the file_name parameter if /LIST is used.
/RANGE=(entry1,entry2)
  Create a list with entries starting with entry1 and ending with
  entry2. The number must contain both the set and entry numbers.
  For example READ/RANGE=(360000-369999) will select all entries 
  in set 36.
  The /RANGE option may not be used with /SUBPDF, /LIST.
  Omit the file_name parameter if /RANGE is used.
/OR
 Specify this option to merge the requested subfile with the current 
 table. Thus, the new current table will contain the entries in either 
 the subfile OR the current table. (NEW_TABLE = OLD_TABLE .or. SUB_FILE)

 /OR may not be used with /AND, /NOT  or /REPLACE
/AND
 Specify this option to match the requested subfile against the current 
 table. The new current table will contain the entries in both the subfile 
 AND the current table. (NEW_TABLE = OLD_TABLE .and. SUB_FILE)

 /AND may not be used with /OR, /NOT or /REPLACE
/NOT
 Specify this option to cull entries from the requested subfile from 
 the current table. All entries present in the both subfile and the current 
 table will be removed from in the new current table. 
 (NEW_TABLE = OLD_TABLE .and. .not. SUB_FILE)

 /NOT may not be used with /OR, /AND or /REPLACE
/REPLACE
 Specify this option to set the new current table to be the same as the 
 requested subfile. (NEW_TABLE = SUB_FILE)

 /REPLACE may not be used with /OR, /AND or /NOT

===> COMMAND  TABLES
 Prints a table of the d-spaces and chemical name for all entries in 
 the current list on the PS hardcopy listing device. 
 If the wavelength has been set (see command WAVELENGTH), both d-spaces 
 and two-theta angles are printed.
---  Qualifiers
/FULL
 If this qualifier is used, the full ICDD-JCPDS (PDF-2) entry is displayed.
===> COMMAND  WAVELENGTH
 Peaks positions may be input or output as d-spacings (in Angstrom) or 
 as two-theta (Bragg) angles corresponding to a given x-ray or neutron 
 wavelength. This command is used to select between d-spacings 
 and angles and to select a wavelength for the latter option.

 The current mode of the program is displayed in the header line at the
 top of the computer screen; the default when the program is started 
 is d-space mode.
---  Parameter
wave_length
  A single wavelength value may be specified directly, where wave_length 
  is the x-ray or neutron wavelength in Angstrom. (The target_type will be 
  assumed to be SY for synchrotron radiation).

  If 0.0 is used for the wave_length, the program will enter d-space 
  mode (same as specifying WAVELENGTH/NOTARGET).

  If wave_length is used, /TARGET and /WTYPE should not. 
---  Qualifiers
/TARGET=target_type
/TARGET
/NOTARGET
 Specifies an x-ray target for conventional x-ray sources. 
 The choices for targets are:
 Cu, Mo, Ni, Co, Fe, Cr, Ag, NU, or SY. 
 Specifying /TARGET without a target_type is equivalent to 
 /TARGET=CU. (Capitalization of the target type is ignored.)
 If NU or SY (for neutron or synchrotron radiation) is used, 
 the program prompts for a wavelength. 

 For input/output using d-spacings specify /NOTARGET

 The /TARGET option cannot be specified with a wave_length value.
/WTYPE=wave_type
   wave_type may be either 1, 2 or 3 which determines 
   the exact value used for the wavelength specified with /TARGET.
   The choices are:
  	1 to use K alpha 1 radiation 
  	2 to use K alpha 2 radiation 
  	3 to use the intensity weighted average of K alpha 1 and K alpha 2 
	  radiation.
   Specifying /WTYPE without a value for wave_type is equivalent 
   to specifying /WTYPE=1.
   This qualifier is ignored if the radiation source has a single 
   wavelength, (e.g. /TARGET=NU or /TARGET=SY) or a 
   wave_length value is specified.
---  Examples
WAVELENGTH/TARGET=CU/WTYPE=3
	The wavelength will be set to the average of Cu K alpha 1 and 
	K alpha 2.
WAVELENGTH/TARGET
	The wavelength will be set to Cu K alpha 1 
WAVE/NOTAR
	Peaks positions, etc. will be displayed as d-spaces.
WAVE 0.0
	Peaks positions, etc. will be displayed as d-spaces.
WAVE 2.5401
	The wavelength will be set to 2.5401Angstrom.
WAVE
	The user will be prompted to choose a wavelength or two use
	d-spacings. 
WAVELENGTH/TARGET=NU/WTYPE=3
	The user will be prompted to enter a wavelength; the /WTYPE=3
	qualifier will be ignored.
===> COMMAND  WRITE
 This command writes the current list in a format suitable for use as a 
 "user supplied" PDF subfile for program MATCH.
---  Parameter
file_name
A single file may be specified on the command line containing the 
name of the file to be written. If the file is not specified, a prompt will
be given requesting a file name to be written.

If no file extension is supplied, the default extension is .USRPDF
---  Examples
 WRITE MYINDEX.FILE
       This writes file MYINDEX.FILE on the current default device and 
       directory.
 WRITE XRAY:[mother.group]myindex
       This writes file [MOTHER.GROUP]MYINDEX.USRPDF on device XRAY.
 WRITE
       The program will prompt for the name of a file to write.

***
Logic Examples
%------------%

A few examples are presented to show how LOGIC may be used. Note that 
there may be several ways to achieve the same results [as is shown in
in Example 1(a) and (b).] Also note that the READ and 
WAVELENGTH commands may not be needed, as the subfile may be
selected when the program starts and the wavelegth may have already
been set appropriately.
 
Example 1(a):
  Find all entries in the full database that contain both Si and O and may
  also contain Al and/or H (or neither) The resulting entries are then 
  examined using the BROWSE command.

	READ/REPLACE/SUBPDF=FULL\_JCPDS
	MATCH/ELEMENT=(SI,O)/OPTIONAL=(AL,H)
	BROWSE

Example 1(b):
  Find all entries in the full database that contain both Si and O and may
  also contain Al and/or H (or neither). This yields the same results as 
  Example 1(a).
 
	READ/REPLACE/SUBPDF=NULL
	MATCH/ELEMENT=(SI,O)/OPTIONAL=(AL,H)
	BROWSE

Example 2:
  Find all entries in the metals section of database that contains Fe
  or Mn and two or three other elements. The entries must have a 30% or 
  greater intensity peak within approximately 0.25 degrees of 12, 14 
  or 16 degrees and may not have any strong peaks (greater than 70%) 
  between approximately 5 and 10 degrees. (Angles are two-theta values 
  for Cu K alpha 1 radiation).
  Two lisings of these entries are made, one with the entry numbers and 
  the other with the most intense three lines permuted and sorted. The 
  first list will be printed and the second list will be displayed on 
  the screen and then optionally printed.
 
	READ/REPLACE/SUBPDF=METAL
	MATCH/ELEMENT=(FE,MN)/OR
	WAVELENGTH/TARGET=CU/WTYPE=1
	MATCH/PEAK=(12,14,16)/OR/ERROR=0.25/LEVEL=70/FAST
	CULL/PEAK=7.5/ERROR=2.5/LEVEL=30/FAST
	INDEX/NAME/PRINT
	INDEX/HANAWALT=3


Example 3:
  For some complex searches, it may be necessary to perform a search in
  sections and save intermediate results on files and finally combine 
  these files. To find all the entries in the ZEOLITE database that 
  contain C plus all the entries in the ORGANIC database that contain
  both Al and Si, it is necessary to perform each search separately.
 
	READ/REPLACE/SUBPDF=ZEOLITE
	MATCH/ELEMENT=(C)/OR
	COMMENT Carbon containing Zeolites
	WRITE c-zeol
	READ/REPLACE/SUBPDF=ORGANIC
	MATCH/ELEMENT=(AL,SI)/AND
	COMMENT Alumino-silicate organics
	READ/OR c-zeol
	COMMENT C-containing Zeolites and Al-Si organics